Energy Education and Research Collaboration

Second Quarter Report

April 16, 2007 – June 30, 2007

###### Prepared by

Prof. Nariman Farvardin, Senior Vice President for Academic Affairs and Provost

Principal Investigator and EERC Project Director

Prof. Avram Bar-Cohen, Chair

EERC Project Deputy Director

A.J. Clark School of Engineering

University of Maryland, College Park, MD 20742-3035

Prepared for

The Petroleum Institute

Abu Dhabi, United Arab Emirates

June 30, 2007

EERC Key Contributors

##### University of Maryland – College Park, MD, USA

Sami Ainane

Shapour Azarm

Balakumar Balachandran

Avram Bar-Cohen

John Cable

Serguei Dessiatoun

Nariman Farvardin

Ashwani K. Gupta

Ali Haghani

Yunho Hwang

Greg Jackson

Mohammad Modarres

Linda Schmidt

Reinhard Radermacher

##### Petroleum Institute – Abu Dhabi, UAE

Ahmed Abdala

Tareq Al Ameri

Saleh Al Hashimi

Valerie Eveloy

Afshin Goharzadeh

Mansour Karkoub

Rocky Kubo

Michael Ohadi

Peter Rodgers

Mohamed Sassi

Abdennour Seibi

Table of Contents

List of EERC Key Contributors	ii

Table of Contents	iii

Executive Summary	1

Introduction	5

Individual Project Reports	7

Development and Delivery of Course Material for Engineering Project Management 	8

Courses

A. Haghani (UMD), J. Cable (UMD)

Development of a Probabilistic Model for Degradation Effects of Corrosion-Fatigue-	9

Cracking

in Oil and Gas Pipelines

M. Modarres (UMD), A. Seibi (PI)

Dynamics and Control of Drill Strings on Fixed and Floating Platforms	12

B. Balachandran (UMD), M. Karkoub (PI)

An EHD-Enhanced Gas/Liquid Separator	21

S. Dessiatoun (UMD), M. Ohadi (PI)

Force-Fed Cooling of Photovoltaic Arrays for High Efficiency 	26

Solar Energy Conversion Systems

S. Dessaitoun (UMD), R. Kubo (PI), M. Ohadi (UMD)

Fundamentals of Engineering Education	29

S. Ainane (UMD), P. Rodgers (PI)

Robust Optimization of Petrochemical Systems	31

S. Azarm (UMD), S. Al Hashimi (PI), T. Al Ameri (PI)

Solid Oxide Fuel Cells for CO2 Capture and Enhanced Oil Recovery	41

G. Jackson (UMD), V. Eveloy (PI), A. Goharzadeh (PI)

Study of Condensing Flows in a Micro-scale Channel with a Micro-element Array 	46

and Visual Techniques

S. Dessiatoun (UMD), A. Goharzadeh (PI)

Sulfur Recovery from Gas Stream using Flameless and Flame Combustion Reactor	52

Prof. A.K. Gupta (UMD), M. Sassi (PI)

Thermally Enhanced Polymer Heat Exchanger for Seawater Applications	59

A. Bar-Cohen, P. Rodgers, A. Abdala (PI)

Undergraduate Design and Best Educational Practices	65

L. Schmidt (UMD), R. Kubo (PI)

Waste Heat Utilization in the Petroleum Industry	67

R. Radermacher (UMD), Yunho Hwang (UMD), S. Al Hashimi (PI), P. Rodgers (PI)

Executive Summary

Progress on the thirteen collaborative research projects is ongoing. The activity during this second quarter has focused on the following:

- Literature reviews and databases

- Conference and print journal papers

- Modeling and simulations

- Design and construction of experimental facilities

- Testing and experimentation

Progress on the individual projects is summarized below.

Development and Delivery of Course Material for Engineering Project Management Courses

A. Haghani (UMD), J. Cable (UMD)

Objective: To develop and deliver course material for an Engineering Project Management program at PI, develop and deliver a short course for GASCO, and perform a feasibility study of establishing a graduate program in Engineering Project Management at PI.

Progress:

- There were no tasks to be completed for this quarter on this project.

Development of a Probabilistic Model for Degradation Effects of Corrosion-Fatigue-Cracking in Oil and Gas Pipelines

M. Modarres (UMD), A. Seibi (PI)

Objective: To propose and validate a probabilistic model for health management of oil pipelines in process plants.

Progress:

- Specific, degradation-based models for fatigue-corrosion life assessment have been proposed.

- Dr. Abdennour Seibi visited UMD on May 14-18. During the visit the development of a PI accelerated testing lab was discussed and planned, and a student was selected to work on Phase II of the project.

- A meeting was arranged for Dr. Seibi with Professor David Wei of Lehigh University. Professor Wei is a leading researcher in corrosion-fatigue, and Dr. Seibi visited his lab to discuss the needs of the planned PI accelerated laboratory.

Dynamics and Control of Drill Strings on Fixed and Floating Platforms

B. Balachandran (UMD), M. Karkoub (PI)

Objective: To develop and analytically and numerically study control-oriented models for drill strings; to investigate control of an under-actuated nonlinear system (drill string) with complex interactions with the environment; and to build a drill-string testbed at the PI/UMD to test the theoretical findings.

Progress:

- Different drill string models were investigated, and an experimental arrangement complementing one at PI was designed for studying drill-string dynamics.

- Professor Balachandran visited PI in February 2007 and met with Professors Karkoub and Abdelmagid of PI. All three of them visited the National Drilling Company of Abu Dhabi, UAE.

An EHD-Enhanced Gas/Liquid Separator

S. Dessiatoun (UMD), M. Ohadi (PI)

Objective: To study hybrid inertia-EHD gas-liquid separation phenomena for electrically conductive and nonconductive liquid particles suspended in a moving gaseous medium.

Progress:

- A conference paper is being prepared that highlights major literature findings and latest results.

- A visualization test setup was constructed to observe the effect of electrostatic forces on air-water separation.

- The experimental air-water test setup was constructed to study the effect of various parameters on the separation process.

Force-Fed Cooling of Photovoltaic Arrays for High-Efficiency Solar Energy Conversion Systems

S. Dessaitoun (UMD), I. Kubo (PI), M. Ohadi (UMD)

Objective: To create a database on the available cooling techniques for high heat flux solar concentrator arrays necessary for efficient conversion of solar energy to electric power, and to design and fabricate an experimental prototype and associated setup to verify the feasibility of this concept and the capacity for force-fed cooling.

Progress:

- A literature survey is being conducted on flat-plate solar cells, solar cells under concentration, and cooling of PV cells.

- Micro-fabrication technology is being studied, and training courses are being started.

Fundamentals of Engineering Education

S. Ainane (UMD), P. Rodgers (UMD)

Objective: To design a review course to prepare PI students for Fundamentals of Engineering examination; to prepare and grade “practice” Fundamentals of Engineering examination for PI students; and to use the practice exam results to identify the program strengths/weaknesses.

Progress:

- FE review material was developed and sent to the PI.

- Dr. Ainane flew to the UAE and conducted a sixteen-hour review for the test.

- Seventy-three graduating seniors from the PI took an eight-hour FE exam; the exams were graded by Dr. Ainane; and the results were communicated to the PI.

Robust Optimization of Petrochemical Systems

S. Azarm (UMD), S. Al Hashimi (PI), T. Al Ameri (PI)

Objective: The objective of this study is to develop a framework for robust optimization the design of a distillation column, while considering the net profit effect at the plant level.

Progress:

- A preliminary literature review for distillation tower optimization was completed.

- The PI-UMD team met on a regular basis via MSN.

- A preliminary optimization model for distillation tower design was developed/implemented. Further extensions of this model are underway.

- A new optimization method was completed and applied to a distillation tower, and other numerical test problems were completed.

- A report of the progress was given during the PI-UMD video-conference meeting on May 23, 2007.

- A joint journal paper is under preparation.

Solid Oxide Fuel Cells for CO2 Capture and Enhanced Oil Recovery

G. Jackson (UMD), V. Eveloy (PI), A. Goharzadeh (PI)

Objective: This multi-faceted project will investigate the feasibility of implementing advanced solid oxide fuel cell (SOFC) technology for producing power from oil well off-gases while providing a source of concentrated CO2 for sequestration and enhanced oil recovery.

Progress:

- UMD has explored fabrication methods for developing optimal micro-architectures for metal-doped ceria anodes.

- Along with the fabrication study for thin electrolytes with porous anode supports, work has continued with thick, electrolyte-supported cells with both Ni and CeO2 anode catalysts.

- Preliminary work has been done on sputter-deposited CeO2 anodes with porous gold overlayers for current collection with thick electrolytes.

- The modeling of 1-D SOFC architectures for design optimization has continued on this program.  The models have been further developed in this quarter to include distributed electrochemical reaction regions, improved kinetic models with operation on CH4 as well as syngas (H2/CO) on Ni/YSZ anodes.

Study of Condensing Flows in a Micro-scale Channel with a Micro-element Array and Visual Techniques

S. Dessiatoun (UMD), A. Goharzadeh (PI)

Objective: To investigate the fundamentals of the two-phase condensing flow phenomenon in a sub-millimeter microchannels.

Progress:

- Leaks have been located and fixed.

- Tests for the refrigerant R24fa have been completed.

Sulfur Recovery from Gas Stream using Flameless and Flame Combustion Reactor

Prof. A.K. Gupta (UMD), M. Sassi (PI)

Objective: To obtain fundamental information on the thermal process for sulfur recovery from sour gas by conventional flame combustion and flameless combustion using numerical and experimental studies. The ultimate goal is to determine optimal operating conditions for sulfur conversion.

Progress:

- Sample simulation results have been obtained for low to high concentrations of H2S in the gas under both non-reactive and reactive conditions.

- A journal paper based on the literature review has been written for a special issue of the American Journal of Environmental Sciences.

Thermally Enhanced Polymer Heat Exchanger for Seawater Applications

A. Bar-Cohen (UMD), Dr. Peter Rodgers (PI), Dr. Ahmed Abdala (PI)

Objective: To address the fundamental thermal performance issues associated with the use of thermal high-conductivity polymer materials in heat exchangers.

Progress:

- Current uses and applications have been identified for low-k polymer heat exchangers in the cooling processes of highly corrosive or chemically aggressive fluids where the chemical inertness of the polymers is beneficial.

- The few companies that produce thermally-conductive polymers and their pertinent material properties have been identified.

- The thermo-fluid performance of a parallel heat exchanger module has been modeled.

- The performances of double-finned polymer heat exchanger modules, from un-enhanced through thermally enhanced polymers, have been evaluated.  These performances have been compared to the performance of an aluminum module over a range of liquid velocities.

Undergraduate Design and Best Educational Practices

L. Schmidt (UMD), R. Kubo (PI)

Objective: To partner with PI design faculty to (1) assess existing PI curriculum to profile the design content and (2) compare the design content level to that of a top-ranked, ABET-accredited, US institution; and, (3) prepare design modules and recommend their selected placement within existing PI courses.

Progress:

  - Dr. Kubo allocated a half-day of his April 27th visit to meeting with Dr. Schmidt to review UM Capstone Design Course materials; to attend a course lecture and a lab section; and to tour DesignME lab facilities.

Waste Heat Utilization in the Petroleum Industry

R. Radermacher (UMD), Yunho Hwang (UMD), S. Al Hashimi (PI), P. Rodgers (PI)

Objective: To utilize waste heat in petroleum processing plants to minimize overall energy consumption.

Progress:

- Preliminary waste heat analysis has been completed for the ADNOC plants at ASAB and ADGAS.

Introduction

In line with its mission to provide world-class education to the citizens of the United Arab Emirates in engineering and the applied sciences, the Petroleum Institute (PI) of Abu Dhabi, UAE, has entered into a long-term collaborative effort with the University of Maryland (UMD) to enhance its own undergraduate, graduate studies/research, and continuing education practices. The PI was founded by Emiri decree in 2001 under the direction of H.H. Sheikh Khalifa bin Zayed Al-Nahyanand.  It is sponsored by a consortium of Abu Dhabi National Oil Company (ADNOC) and its international partners (Shell, BP, Total, and Japan Oil Development Company.

The PI and UMD recognize the many potential benefits for both institutions that could result specifically from collaborative educational and research activities in the field of Energy Sciences and Engineering.  The Energy Education and Research Collaboration (EERC) has been created within the A.J. Clark School of Engineering at the University of Maryland to provide the administrative structure and academic oversight for these collaborative efforts.

During this second quarter of the EERC’s funded effort, partnerships between UMD and PI faculty have been further solidified, and significant progress has been made on the collaborative research projects.

Updated Quarterly Schedule

Because the first quarterly period expanded to fill nearly five months, an adjusted quarterly schedule is now in place.  UMD will provide quarterly reports to the PI on the following dates:

| Quarter 2 | June 30, 2007 |
| --- | --- |
| Quarter 3 | September 30, 2007 |
| Quarter 4 | December 15, 2007 |
| Quarter 5 | February 29, 2008 |
| Quarter 6 | May 15, 2008 |
| Quarter 7 | July 31, 2008 |
| Quarter 8 | October 31, 2008 |

Collaborative Activities

Progress made on the EERC research projects during the second quarter of activity is summarized below.

I.  	Collaborative research projects

Progress on the thirteen collaborative research projects is ongoing. The activity during this second quarter has focused on the following:

- Literature reviews and databases

- Conference and print journal papers

- Modeling and simulations

- Design and construction of experimental facilities

- Testing and experimentation

Progress on the specific projects is described in greater detail in the next section of this report.

II.  	EERC faculty visits

Face-to-face meetings have continued to prove useful to the various projects.  UMD faculty members have visited PI, and vice versa, to collaborate on experimental facilities and to meet with representatives from industry and other universities who have an interest in EERC research.

Faculty and student visits include:

- Dr. Bala Balachandran to PI, Feb 2007

- Dr. Greg Jackson to PI, March 2007

- Dr. Rocky Kubo to UMD, April 2007

- Dr. Abdennour Seibi to UMD, May 14-18

- Juan Cevallos, UMD graduate student, to PI June 19-July 20

III.	Joint monthly meetings via video-conference

Joint monthly meetings have continued as an effective means for faculty members to present their research to the entire group.  In contrast to the first video-conference meeting, at which all the projects were presented, fewer faculty members now present at each meeting, which allows them to discuss their findings in greater detail.

IV.	PI Distance Learning Students

Three PI students successfully completed the UMD graduate Mechanical Engineering course ENME 635, “Energy Systems Analysis.”  The students participated in the course as distance learners, and they received UMD graduate credit for their participation.

Progress Report Contents

The remainder of this report contains descriptions and progress updates of the current collaborative research projects.  The format of the individual reports has been modified from the first quarterly report to better accommodate the information presented.

For each project the following information is included as applicable:

- Objective/Abstract

- Milestones/Deliverables Scheduled for Completed Quarter

- Summary of Project Activities for the Completed Quarter

- Difficulties Encountered/Overcome

- Planned Project Activities for the Next Quarter

- Appendix

  - Justification and Background

  - Approach

  - Two-Year Schedule

  - Key References

Conclusion

During this second quarter, now that initial start-up delays have been resolved, the EERC has made significant progress on its joint research projects.  UMD looks forward to our continued collaborative efforts.

Individual Project Reports

Development and Delivery of Course Material for Engineering Project Management Courses UMD Investigators: Ali Haghani & John Cable GRA’s: None PI Investigator(s): None Start Date: October 2006 Report Date: 1 December 2006

1.	Objective/Abstract

Develop and deliver course material for an Engineering Project Management program at PI, develop and deliver a short course for GASCO, and perform a feasibility study of establishing a graduate program in Engineering Project Management at PI.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

None.

3.	Summary of Project Activities for the Completed Quarter

UMD/PM does not have any tasks due this quarter. We are waiting to hear from PI regarding the next courses they want.

4.	Difficulties Encountered/Overcome

5.	Planned Project Activities for the Next Quarter

We plan to deliver a questionnaire for use in the market analysis to PI for beta testing by the end of August.

6.	Appendix

6.1	Justification and Background

PI’s need to develop a graduate program in Engineering Project Management.

6.2	Approach

The material for all of these courses will be derived from the course material for the engineering project management courses at the University of Maryland, supplemented by additional material developed by the CEE faculty as needed.  After delivery of the material, the feasibility study will entail visiting PI, interviewing the PI faculty who are interested in the program, and assessing the facilities and human resources needs.

6.3	Two-Year Schedule

- Develop and deliver a one-week short course in project management for GASCO: January 2007 – delivered in Abu Dhabi in January.

- Develop and deliver materials for a semester-ling course in project management: September 2007 – hand delivered in Abu Dhabi in January 2007 (7 months early)

- Develop and deliver materials for two additional semester-long courses in project management at PI: December 2007 – delivered slides only for ENCE 421 in January with the rest due in September 2007. The third course has not been requested by PI at this time.

6.4	Key References

N/A

Development of a Probabilistic Model for Degradation Effects of Corrosion-Fatigue-Cracking in Oil and Gas Pipelines UMD Investigator: Prof. Mohammad Modarres GRA-1: Mohamed Chooka GRA-2: To be assigned PI Investigator(s): Prof. Abdennour Seibi Start Date: October 2006 Report Date: 30 June 2007

1.	Objective/Abstract

This study involves developing and applying an engineering-based probabilistic model for health management of oil pipelines in process plants. The study involved two interrelated projects. The first project, which is the topic for the PhD student, focuses on model development and demonstration. The second project involves developing a degradation acceleration lab at PI and performing experiments to further validate the proposed models of the first project. Building the experimental set-up depends on the availability of funding from the Petroleum Institute.  GRA-1 is working on the first project and GRA-2 will work on the second project.

The objective of this study is to propose and validate a probabilistic model based on the underlying degradation phenomena whose parameters are estimated from the observed field data and experimental investigations. Uncertainties about the structure of the model itself and parameters of the model should also be characterized.  The proposed model should be able to capture wider ranges of pipelines rather than only the network ones.  Thus, the proposed model will better represent the reality of the pipeline’s health and can account for material and size variability.  The existing probabilistic models sufficiently address the corrosion and fatigue mechanisms individually, but are inadequate to capture mechanisms that synergistically interact.  Admitting the fact that capturing all degradation mechanisms will be a challenging task, the new model will address two of the most important mechanisms: corrosion/crack growth and corrosion/fatigue/crack growth.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

3.	Summary of Project Activities for the Completed Quarter

(As related to stated deliverables in #2.  Include findings, accomplishments, figures, and/or schedule changes in this section.)

1. Specific models for fatigue-corrosion degradation-based life assessment have been proposed.

2. Mohamed Chookah, the PI-funded graduate student, presented and passed his PhD proposal on May 14.

3. Dr. Abdennour Seibi visited UMD on May 14-18. During the visit the development of a PI accelerated testing lab was discussed and planned, and a student was selected to work on Phase II of the project. This student has agreed to spend 6-9 months at PI while the lab is being developed and will begin his stay in September 2007. Also, we arranged a meeting for Dr. Seibi to visit Professor David Wei of Lehigh University. He is a leading researcher in corrosion-fatigue, and Dr. Seibi visited his lab to discuss the needs of the upcoming PI accelerated laboratory.

4. We have invited Prof. David Wei to serve on Mohamed Chookah's PhD committee.

4.	Difficulties Encountered/Overcome

None.

5.	Planned Project Activities for the Next Quarter

6.	Appendix

6.1	Justification and Background

Oil pipelines are susceptible to degradation over the span of their service life. Corrosion is one of the most common degradation mechanisms, but other critical mechanisms such as fatigue and creep cannot be overlooked.  The rate of degradation is influenced by factors such as pipeline materials, process conditions, geometry, and location.  Based on these factors, a best estimate of the pipeline’s service life (reliability) is calculated.  This estimate serves as a target that guides maintenance and replacement practices. After a long period of service, however, this estimate requires reevaluation due to new evidence observed from monitoring the conditions of the pipeline.

A number of deterministic models have been proposed to estimate reliability of pipelines.  Among these models is the ASME B31G code [1], which is the most widely accepted method for the assessment of corroded pipelines [2].  However, these models are highly conservative and lack the ability to estimate the true life and health of the pipeline. It is necessary, therefore, to develop a best-estimate assessment of the life of these pipelines and integrate the uncertainties surrounding this estimate.  In addition to the limitations embedded in these deterministic models are the problems with inspection techniques and tools that may be inadequate and susceptible to errors and imprecision.  The proposed probabilistic models would be capable of addressing the limitations of these models (by accounting for model uncertainties), inspection data (characterizing limited and uncertain evidences) and subjective proactive maintenance (involving decision making process under uncertainty).

6.2	Approach

The researchers will attempt to identify a focal point in one of ADNOC’s operating companies, such as TAKREER, which will champion this project and provide data pertinent to the core activities of this research study.  The study consists of two interrelated projects that will run over a period of two years and a half.  The first phase of Project 1 will focus on the development of a PhD thesis proposal, which encompasses the latest technological development and ongoing research activities and outlines the subject of the research project.  The second phase will concentrate on the development of a probabilistic model for piping in process plants followed by model validation through collected experimental and field data.  The second project, which will run a year later, will focus on the design, construction and commissioning of the corrosion-fatigue test cell.  The test rig will be designed and built by the research team at the University of Maryland (UMD) with the assistance of Dr. Abdennour Seibi from the Petroleum Institute (PI).  The third phase of this study will deal with model application to ADNOC process facilities in order to predict their remaining service life.

The test rig, which will be built at PI, will be used by GRA-2 to conduct an experimental study reflecting field conditions for model validation developed in project 1.  The equipment needed would include corrosion test cells, autoclaves, multiphase flow loops, and testing machines for slow strain rate and crack growth testing. This activity also requires a complete line of monitoring equipment for evaluation of corrosion, scaling, and chemical treatment for field and laboratory.  This test rig, once built, will be a useful tool for teaching, research, and possibly training field engineers from operating companies.  See “Two-Year Schedule” for a summary of the major tasks and the corresponding timeline.

6.3	Two-Year Schedule

Project 1:

- PhD thesis proposal, which will include a literature search (9/1/2006 - 6/30/2007)

- Data collection from ADNOC process plants (1/1/2007 - 8/30/2007)

- Prof. Modarres visit to PI to review progress and plan for accelerated lab development (3/2007).

- Dr. Seibi visit to UMD to advise PhD student in his thesis work and assist in designing the accelerated Testing Facility (11 – 21 May).

- Empirical/Engineering-Based Model Development (9/1/2006 – 6/30/2007)

  - Streamlining of the model to pipeline/pressure vessel application.

  - Collection of appropriate data (data availability is at the discretion of ADNOC operating companies).

  - Actual model development.

- Probabilistic estimation of model parameters (4/1/2007 – 8/31/2007)

- Application example (9/1/2007 – 12/31/2007)

- Dr. Seibi visit to UMD for thesis proposal defense and thesis defense (dates to be announced).

Project 2:

- Design, construction, and commissioning of Accelerated Degradation Lab at PI.  UMD research team will design the test facility with the assistance of Dr. A. Seibi from PI (6/1/2007 - 12/31/2007).

- Test planning (1/1/2008 – 1/31/2008).  Dr. Seibi will visit UMD for two weeks during this period to jointly develop the test plan with UMD researchers.

- Experimental test for model testing/validation (1/1/2008 - 8/31/2008)

- Examples of model applications (9/1/2008 – 12/31/2008)

Conference and archival paper development (Dates of delivery depend on availability of results).

6.4	Key References

[1] ASME-B31G (1991).  Manual for Determining the Remaining Strength of Corroded Pipelines: A Supplement to ASME B31G Code For Pressure Piping.  New York: American Society of Mechanical Engineers.

[2] Lee, O. S., Kim, D. H. and Choi, S. S. (2006).  Reliability of Buried Pipeline Using A Theory Of Probability Of Failure. Solid State Phenomena, 110, 221-230.

Dynamics and Control of Drill Strings on Fixed and Floating Platforms UMD Investigators: Bala Balachandran UMD GRA: Chien-Min Liao (started in SPRING 2007) PI Investigators: Mansour Karkoub and Youssef Abdelmagid PI RA: Thomas Polzer Start Date: 12/01/2006 Report Date: 30 June 2007

1.	Objective/Abstract

Research objectives are the following: i) develop, and analytically and numerically study control-oriented models for drill strings, ii) investigate control of an under-actuated nonlinear system (drill string) with complex interactions with the environment, and iii) build drill-string arrangement at  PI & UMD to validate the analytical findings and suggest possible strategies to mitigate drill-string failures.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

In this quarter, different drill string models were investigated and an experimental arrangement complementing one at PI has been designed for studying drill-string dynamics.   Professor Balachandran visited PI in February 2007 and met with Professors Karkoub and Abdelmagid of PI.  All three of them visited the National Drilling Company of Abu Dhabi, UAE.  All of the models and the experimental arrangements discussed here have been constructed in close collaboration with Professors Karkoub and Abdelmagid.

3.	Summary of Project Activities for the Completed Quarter

(As related to stated deliverables in #2.  Include findings, accomplishments, figures, and/or schedule changes in this section.)

Figure 1. Sketch of drill-string system

and different models studied.

As illustrated in Figure 1, a drill-string system, conveying the rotary downward motion to the drill-bit, is primarily composed of a drill pipe, the drill collars, and the drill bit.  During a drilling operation, there is drilling mud or fluid between the drill pipe and collars. Different models have been studied for examining the drill-string dynamics. These models include the four model types, namely, Models I, II, III, and IV, discussed here.   In Model I, the lateral dynamics of the drill string are of interest, while in Model II, the torsional motions of the drill string are of interest. The effect of drilling mud is taken into account in Model II.  Both Models I and II have been reported in the literature as mentioned in the previous report.   The features of Models I and II are taken into account in constructing Model III, where the axial or longitudinal forces are also included.  This model can be used for studying torsional and bending motions of a drill string.  The features of Models I and II are not further discussed here, as they have been discussed in previous reports and presentations.   In Model IV, the drill string is treated like a rotating shaft and bending of the drill string due to an unbalanced mass is treated.   The development of Model IV is discussed in Section 3.1, and the experimental arrangement being conceived at the University of Maryland is briefly described in Section 3.2.    Preliminary results obtained through simulations are also included in Section 3.1.

3.1 Model IV: 4DOF model

In this section, the model development undertaken to construct a four degree-of-freedom model is discussed.    To aid the development of this model, illustrative sketches are included in Figures 2 and 3, where two sections of a drill string are shown.  The four degrees of freedom are the following: i)  the radial displacement of the center of Section II, ii)  the rotation of Section I, iii)   the bending angle along the tangential direction, and iv)  the rotation of Section II.   The unbalanced mass is   , and the eccentricity of this mass with respect to the rotation axis is given by the parameter e.  The four degree-of-freedom model can be extended to a five degree-of-freedom model by including an additional tilt angle of Section II.

Figure 2. Two sections of a drill string undergoing torsional motions.  In addition, the drill string undergoes bending motions much like a rotating shaft with a mass unbalance.

Figure 3. System with unbalanced mass mb.

3.1.1 Derivation of Equations of motion of the system

The system equations are derived from Lagrange’s equations.  To that end, the system kinetic energy, system potential energy, and the virtual work are determined as

(1)

(2)

(3)

where the definition of different quantities closely follow that provided in Melakhessou, Berlioz, and Ferraris (2003) (also see Section 6.4).  However, it should be mentioned that there are differences between the model constructed here and the model reported in the work of Melakhessou et al.  Starting from Eqs. (1)-(3), the equations of motion are obtained as

(4)-(7)

where .

3.1.2 Simulation results

Simulation results are presented for two different initial values of the radial displacement.  These simulations are based on a MATLAB program written on the basis of Eqs. (4) and (7).  Numerical values used for the different parameters are given in Section 6.4.  The choice of these parameter values will be refined in future simulations to correspond to an actual drill string.

Case I (Initial displacement close to the outer wall and no external force):   In this particular case, the initial displacement  has been picked to have a value of 2.0, which means that the initial position is close to the outer wall.   Free oscillations of the system are considered, and results obtained through numerical integration are shown in Figures 4 and 5.  The results indicate bounded, aperiodic behavior as expected.

| (a) | (b) |
| --- | --- |
| (c) | (d) |

Figure 4. Representative free-oscillation results obtained through numerical integration of Eqs. (4) through 7.  The four phase portraits correspond to the following: a) radial displacement of Section II, b) rotation angle of Section I, c) bending angle of Section II, and d) rotation angle of Section II.

| (a) | (b) |
| --- | --- |

Figure 5. Trajectory of the center of Section II in the X-Y plane:  a) without bending angle, (only) and b) with bending angle, ().

Case II (Initial displacement close to the origin and no external force):  In this particular case, the initial displacement  had been picked as 0.01, which is close to the origin.  Again, the results shown in Figures 6 and 7 indicate aperiodic motions: in particular, quasi-periodic motions.

| (a) | (b) |
| --- | --- |
| (c) | (d) |

Figure 6. Representative free-oscillation results obtained through numerical integration of Eqs. (4) through 7.  The four phase portraits correspond to the following: a) radial displacement of Section II, b) rotation angle of Section I, c) bending angle of Section II, and d) rotation angle of Section II.

| (a) | (b) |
| --- | --- |

Figure 7. Trajectory of the center of Section II in the X-Y plane:  a) without bending angle, ( only) and b) with bending angle, ().

3.2 Experimental Arrangement:

As shown in Figure 8, the setup consists of two rotational disks (to be made from brass), a power amplifier, a DC motor, and a brake that can be applied to the lower disk.  In addition, the lower disk is to be attached to a spring-actuator base to model the soil behavior. The drill string is enclosed by an outer shell, which in the real scenario would be full of mud. A possible dimension for the drill string (to be made from low-stiffness steel spring) is a length of about 1 m to 1.5 m and a diameter of 2 mm.  The drill-string and the lower brass disk represent the drill-

Figure 8. Experimental arrangement to study bending and torsional motions of a drill string; this arrangement is complimentary to that being developed at PI.

string with the bottom-hole-assembly in a real drill-string system, and the brake is to be used to simulate the friction force between the drill bit and borehole. The contact material of the brake is to be rubber. The brake can also be used for simulating the resistance of soil. Lateral forces are also to be applied by using a shaker as shown in the figure.  This shaker can be helpful for studying bending failures of the drill string.

- Difficulties Encountered/Overcome

Simulations with an external torque have not yielded results that can be explained thus far.  It is planned to include dissipation in the system and also to examine the contact dynamics between the string and the shell. It is also anticipated that it will take time to realize the appropriate interface and simulation conditions with the experimental arrangement.

5.	Planned Project Activities for the Next Quarter

Apart from the issues mentioned in Section 4, a model to simulate the bending motions of the drill string system under lateral and axial applied forces will be examined, and the role of drilling mud will also be studied.  On the experimental front, the following issues will be addressed:  i) applied static/dynamic longitudinal force to let the string bend while rotating, ii) relative displacement between two sections due to an applied lateral force, and iii)  application of  a dynamic lateral force.

Figure 9.  Different scenarios to be studied in the experiment.

6.	Appendix

6.1	Justification and Background

Drill-string dynamics needs to be better understood to control drill strings and steer them to their appropriate location in oil wells, in particular, for applications such as geosteered drilling.   Although a considerable amount of work has been carried out on oil-well rotary drilling (for example, Spanos et al. 2003), the nonlinear dynamics of this system is not well understood given that a drill string can undergo axial, torsional, and lateral vibrations, and  operational difficulties include sticking, buckling, and fatiguing of strings.

6.2	Approach

A combined analytical, numerical, and experimental approach will be pursued at the University of Maryland (UMD) in coordination with the Petroleum Institute (PI). Specifically, the drill string is to be modeled as a nonlinear dynamical system consisting of interconnected structural components (e.g., tubes) with joints. Appropriate attention will also be paid to the soil conditions. Finite element methods are to be used for developing computational models. The experiments at UMD & PI will be tailored to address specific aspects of the drill-string dynamics.  Actuator and sensor choices will also be explored to determine how best to control the system dynamics. The studies will be initiated with drill strings located on fixed platforms and later will be extended to systems located on floating platforms.

6.3	Two-Year Schedule

January 1, 2007 to July 31, 2007:  Modeling of drill-string dynamics, computational models; analytical and numerical studies; identification of appropriate oil-well model

August 1, 2007 to October 31, 2007:  Analytical and experimental studies and initiation of experimental studies

November 1, 2007 to January 31, 2008:  Completion of preliminary control design studies

February 1, 2008 to July 31, 2008: Studies on “optimal” actuator and sensor configurations for control of drill-string dynamics, and investigations into the need for vibration isolation schemes

August 1, 2008 to October 31, 2008: Studies on drill-string systems located on floating platforms

6.4 Nomenclature and values used for simulations

| Symbol | Analytical model definition | Variable/Simulation value |
| --- | --- | --- |
|  | Radial displacement | Variable |
|  | Rotational angle of Section I | Variable |
|  | Bending angle along the tangential direction | Variable |
|  | Rotational angle of Section II | Variable |
|  | Mass moment of inertia of Section I | 100 units |
|  | Mass moment of inertia of Section II | 100 units |
|  | Radial distance of the unbalance mass | 0.5 units |
|  | Initial displacement of Section II | 2.0 / 0.01 units |
|  | Mass of Section II | 2.05 units |
|  | Unbalanced mass | 2.0 units |
|  | Bending stiffness in radial direction | 0.5 units |
|  | Bending stiffness in tangential direction | 0.2 units |
|  | Torsional stiffness of Section II | 0.3 units |
|  | Contact stiffness of Section II | 0.8 units |
|  | Contact determination term; equals to 1 while contacting and 0 otherwise | 0 or 1 |
|  |  | -- |
|  | Separation from Section II to the outer wall at initial position | -- |

6.5	Key References

Leine, R. I., van Campen, D. H., and Keultjes, W. J. G. (2002). “Stick-Slip Whirl Interaction in Drill String Dynamics,” ASME Journal of Vibration and Acoustics, Vol. 124 (2), pp. 209-220.

Melakhessou, H., Berlioz, A., and Ferraris, G. (2003). “A Nonlinear Well-Drillstring Interaction Model,” ASME Journal of Vibration and Acoustics, Vol. 125 pp. 46-52.

Mihajlović, N., van de Wouw, N., Rosielle, P.C.J.N., and Nijmeijer, H. (2007) “Interaction between torsional and lateral vibrations in flexible rotor systems with discontinuous friction,” Nonlinear Dynamics, published online.

Mihajlović, N., van Veggel, A. A., van de Wouw, N., and Nijmeijer, H. (2004)  “Analysis of Friction-Induced Limit Cycling in an Experimental Drill-String System,”  ASME Journal of Dynamic Systems, Measurement, and Control, Vol. 126(4), pp. 709-720.

Nayfeh, A. H. and Balachandran, B. (1995). Applied Nonlinear Dynamics: Analytical, Computational, and Experimental Methods, Wiley, New York.

Spanos, P. D., Chevallier, A. M., Politis, N. P., and Payne, M. L. (2003). “Oil and Gas Well Drilling: A Vibrations Perspective,” Shock and Vibration Digest, Vol. 35(2), pp. 85-103.

An EHD-Enhanced Gas-Liquid Separator UMD Investigators: Dr. Serguei Dessiatoun GRA’s: Mohamed Alshehhi PI Investigator(s): Dr. Michael Ohadi Start Date: October 2006 Report Date: 30 June 2007

1.	Objective/Abstract

To study hybrid inertia-EHD gas-liquid separation phenomena for electrically conductive and nonconductive liquid particles suspended in a moving gaseous medium. This is useful in a variety of applications including air-conditioning, refrigeration and process industries.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

- Literature review

- Construction of visualization test setups to study the effect of electrostatic forces on air-water separation and the effects of various parameters on the separation process.

3.	Summary of Project Activities for the Completed Quarter

(As related to stated deliverables in #2.  Include findings, accomplishments, figures, and/or schedule changes in this section.)

- Literature Review:

  - A conference paper is being prepared that highlights major literature findings and latest results.

- Experimental Work:

  - A visualization test setup was constructed to observe the effect of electrostatic forces on air-water separation.

  - An experimental air-water test setup was constructed (Fig. 1) to study the effect on the separation process of some parameters, such as:

    - Current Voltage Characteristics (Fig. 2)

    - Electrode voltage (Fig. 3)

    - Separator length (Fig. 4)

    - Flow rate (Fig. 5)

(A TSI Aerodynamic Particle Sizer® Spectrometer was used to analyze the data).

Figure 1. Air-Water Separation Test Setup

Figure 2. Current-Voltage Characteristics

Figure 3. Voltage Effect

Figure 4. Separator Length Effect

Figure 5. Air Flow Rate Effect

4.	Difficulties Encountered/Overcome

- Some challenges in the design of a gas-and-conductive liquid separator are listed below:

  - Efficient charging procedure for all particles in the separator volume

  - Prevention of charge leakages and/or shortages due to the conductive nature of the fluid

  - Power supply design and control mechanisms

5.	Planned Project Activities for the Next Quarter

- Use numerical work (Fem Lab) to simulate the charging process through the separator.

- Design a water mist separation test loop with instrumentation for control and/or measurement of:

  - Temperature

  - Humidity

  - Flow rate

6.	Appendix

6.1	Justification and Background

Separation comprises a significant part of the oil and natural gas production process.  In many stages of this process, electrostatic separation significantly increases the efficiency and often decreases the cost of production. Most of the oil producers, including ADNOC, operate where the climate is hot and therefore use refrigeration and air-conditioning equipment.  The efficiency and reliability of this equipment appreciably suffers due to mal-distribution of lubricant oil in the system. Electrostatic separation can correct this mal-distribution and improve the efficiency of this refrigeration and air-conditioning equipment.   Similarly, vapor compression equipment with lubricant circulation is also used in oil refinery processes. This circulation can be significantly improved using EHD separators to increase heat-pumping efficiency. UMD has already developed a working prototype for gas-and-non-conductive droplet separation. However, the fundamentals of this separation mechanism must be better understood to enable optimization of the working design. There is also a need to explore the feasibility of separation of gas-and-conductive liquid mixtures, which poses additional challenges.

Conventional gas/liquid separators are based on inertial and gravitational forces. They have poor efficiency when separating micron-size particles in the flow due to low gravitational and inertial forces acting on small particles. In contrast, electro-hydrodynamic (EHD) forces strongly affect particles of such size. The combination of a conventional separator with EHD allows us to create the most effective and lowest pressure-drop particle separator, with potential applications to separation of electrically conductive and non-conductive liquid particles. The separation of electrically conductive particles like water-air mixtures (fog) imposes significant design constraints on separator electrode design and high-voltage power supply selection.

6.2	Approach

Detailed analysis and identification of the phenomena and the design challenges involved in effective implementation of the mechanism. Parametric study of existing and improved separators. Design iterations, including numerical flow and field simulations, fabrication, and testing. Creation of database and engineering design correlations.

6.3	Two-Year Schedule

Year 1:

- Conduct literature review to study current technologies for separation of solid or liquid particles from gas flows by electrostatic and electro-hydrodynamic (EHD) forces.

- Evaluate existing technologies and assess their applicability to flow separation of gas-and-liquid-droplet mixtures.

- Evaluate and optimize current designs of UMD EHD separators for non-conductive liquid particles in gas flow.

- Design and fabricate a two-phase gas-liquid droplet separator capable of operating with conductive fluids. Conduct a parametric study of separators for different conductive fluids, concentrations, and gas flow rates.

Year 2:

- Continue optimization and numerical study of hybrid gas-and-non-conductive liquid droplet separator. Continue parametric experimental study of gas-and conductive separator.

- Design iterations and implementation.

- Experiment on different designs.

- Develop design correlation.

- Prepare report.

6.4	Key References

1. Mo, B., M.M. Ohadi, and S.V. Dessiatoun, "Liquid vapor separation and thermal management in an EHD-enhanced capillary pumped loop", Heat Transfer 1998, Proceeding of 11th International Heat Transfer Conference, Vol. 2, Taylor & Francis Inc., Levittown, PA, pp.63-68.

2. Electrohydrodynamic Liquid-Vapor Separator USA Pat.# 6,582,500

3. Schrage, D.S., J.M. Shoemaker, and J. McQuillen, 1998, “Passive two-phase fluid separation,” AIAA 36th Aerospace Sciences Meeting & Exhibit, Reno, NV, Jan. 1998, AIAA-98-0731

4. Balachandran, W., Machowski, W., Ahmad, C.N. “Electrostatic atomization of conducting liquids using AC superimposed on DC fields” Industry Applications, IEEE Transactions on Volume 30, Issue 4, July-Aug. 1994 Page(s):850 - 855 Digital Object Identifier 10.1109/28.297899

Force-Fed Cooling of Photovoltaic Arrays for High-Efficiency Solar Energy Conversion Systems UMD Investigators: Dr. S. Dessaitoun GRA’s: E. Kermani, S. Chowdhury PI Investigator(s): Dr. I. Kubo, Dr. M. Ohadi Start Date: March 2007 Report Date: 30 June 2007

1.	Objective/Abstract

The proposed project will create, based on a survey of available literature, a database on the available cooling techniques for high heat flux solar concentrator arrays necessary for efficient conversion of solar energy to electric power. The typical cooling load necessary for optimum radiation concentration and optimum photovoltaic conversion efficiency will be identified, and a novel force-fed cooling technique that has been developed at UMD will be applied to contain this cooling load. An experimental prototype and associated setup will be designed and fabricated to verify the feasibility of this concept and the capacity for cooling by this technique. Based on these experimental results, the radiation concentration levels acceptable to this cooling capacity will be redefined. The type of fluid and its flow rate, the temperature of the surface where solar radiation is incident, and the uniformity of temperature on this active area are the main issues that will be addressed in this proposed project. The scalability of this technique for uniform cooling of industry-scale extended area panels will be a guiding parameter for the design and development of the heat exchanger prototype proposed here.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

- A literature survey is being conducted on flat plate solar cells, solar cells under concentration, and cooling of PV cells

- Micro-fabrication technology is being studied, and training courses are being started

3.	Summary of Project Activities for the Completed Quarter

(As related to stated deliverables in #2.  Include findings, accomplishments, figures, and/or schedule changes in this section.)

- Literature review

  - Photovoltaic effect

  - Types of photovoltaic cells

  - Energy conversion efficiency

  - Flat plate solar cells

  - Concentrating photovoltaic

  - Temperature rise in solar cells

- Micro fabrication technology

  - Deep reactive etching

  - Photolithography

  - Training course

4.	Difficulties Encountered/Overcome

- Lack of literature about the simultaneous effect of concentration on cell efficiency and temperature rise.

- Lack of literature about optimum concentration.

5.	Planned Project Activities for the Next Quarter

- Design a force-fed silicon-based heat sink for the concentrated solar cell

- Evaluate the possibility of fabrication of a silicon-based heat sink for the concentrated solar cell

- Explore the possibilities of fabrication of the heat sink using UMD microfabrication facilities

6.	Appendix

6.1	Justification and Background

The abundance of solar energy in Middle Eastern countries provides significant opportunity for development of eco-friendly power generation technologies essential in the modern world. Several decades of research have produced significant knowledge and innovations in design of economically viable, silicon-based photovoltaic (PV) panels and mirrors for concentration of solar radiation and its conversion to electric power. One of the outstanding challenges in this field is the active and uniform cooling of these large-area, high heat flux solar concentrator arrays, because the conversion efficiency is heavily dependent on device temperatures and drops significantly with an increase in temperature. If an appropriate cooling technique is possible, these solar panels will become more effective and commercially viable, which could pave the way for a rapid transition of the current power generation industry towards eco-friendly alternatives for local use, increasing currently available export resources and also creating a base for future energy export technologies.

Among several techniques enabling the use of solar energy, solar photovoltaics exhibit significant potential for economic and eco-friendly process for power generation industry. After five decades of research and development, photovoltaic energy production is growing exponentially across global markets. Northern Europe and Japan currently lead in the research and commercialization of PV technology. Solar panels on the facades and roofs of commercial and residential buildings are common pictures in these countries, where solar energy is used in every aspect of utilities, including heating, cooling and lighting needs. Most of those countries have climates with high cloudiness and low intensity direct sunlight, limiting the energy conversion effect. The static PV arrays that work well with dispersed sun light have already been developed. These cells are used in the static arrays and are simple silicon-based cells with poor conversion efficiency.

Progress has been made on decreasing the cost and consumption of solar array material by using thin film PV cells. Daytime tracking of the sun by sensor-enabled drives offers significant benefit in increasing solar array effectiveness. Also, in the recent decade, works have been published on the concentration of solar radiation by parabolic mirrors and lens structures onto smaller sized solar panels, which greatly reduce the cost and increase conversion efficiency by increasing specific power. The US Department of Energy has recently reported exceeding 40% efficiency level with concentrated arrays compared to 8.5% for static arrays. The efficiency of the array increases with the level of concentration if array temperature is kept at a low constant value. The same low array cost compared to the total system cost will allow updating to current technology. The radiation concentration up to 80,000 times is theoretically possible but currently just 400 to 500 times is feasible due to high heat dissipation requirement on the PV concentrator arrays.

6.2	Approach

UMD-side participation

- Conduct extensive literature survey on PV radiation concentrators. Summarize available cooling technologies for these arrays with notes on their cost, size and other scalability issues.

- Evaluate cooling loads, taking into account recent advances in radiation concentration technologies and conversion efficiencies.

- Develop a force-fed heat exchanger prototype capable of rejection of this expected heat flux. Explore the possibility of MEMS fabrication techniques for creating micro-grooves integrated with solar panels. Also identify possible fluid choices and pumps to meet the demand.

- Conduct experimental study on force-fed-based single- and two-phase processes to determine cooling capacity.

- Based on outcome of experiments, design, fabricate, and test a complete PV converter and cooler package in the field.

- Make recommendations for a radiation concentration that is commensurate with this thermal management technique.

PI-side participation

- Provide information and symbiotic assistance to the UMD team regarding current concentrator designs, available cooling techniques and expected heat loads.

- Prepare a solar concentrator to be packaged with UMD-made heat exchanger for final testing.

- Corroborate UMD testing of the concentrator and cooling element in UAE desert conditions

- Provide contributions to the preparation of final project report and recommendations.

6.3	Two-Year Schedule

UMD-side participation

Year 1

- Literature review and summary

- Design of force-fed cooler for PV array

- Fabrication of experimental prototype and experimental loop

Year 2

- Finalized experimental setup

- Experimental results

- Recommendations for optimized PV converters with respect to developed cooling capacity

- Final report

PI-side participation

Year 1

- Input on literature review and summary

- Discussion and assistance in design of test prototype

- Concentrator design

Year 2

- Discussion and assistance in experimentation

- Concentrator fabrication or participation in fabrication

- Testing of concentrator and cooling system in UAE conditions

- Input on final report and recommendation

6.4	Key References

- Muresan, C., Menezo, C., Bennacer, R., Vaillon, R., ’ Numerical Simulation of a Vertical Solar Collector Integrated in a Building Frame : Radiation and Turbulent Natural Convection Coupling’, Heat Transfer Engineering, vol. 27(2), pp. 29-42, 2006.

- Konnttinen, P., Lund, P.D., ‘Thermal Stability and Moisture Resistance of C/Al2O3/Al solar absorber surfaces,’ Solar Energy Materials and Solar Cells, vol. 82, pp. 361-383, 2004.

- Ramanathan, K., Keane, J., Koufi, R.,’Properties of High-Efficiency CIGS Thin-Film Solar Cells,’ Proceedings of 31st IEEE Photovoltaics Specialists Conference and Exhibition, Lake Buena Vista, FL, January, 2005.

- Han, D., ‘Microscopic Mechanism of Staebler-Wronski Effect in a-Si Films and High Efficiency Solar Cells,’ Final Subcontract Report prepared under subcontract no. ADJ-1-30630-09, National Renewable Energy Laboratory, 2004.

- Bakirov, M., ‘ Photoelectric and Radiation Characteristics of Silicon Solar Cells at High Illumination Levels and Elevated Temperatures,’ Semiconductors, vol. 31(5), pp. 439-440, 1997.

Fundamentals of Engineering (FE) Examination UMD Investigators: Dr. Sami Ainane PI Investigator: Dr. Peter Rodgers Start Date: June 2006 Report Date: 30 June 2007

1.	Objective/Abstract

- Design a review course to prepare PI students for the Fundamentals of Engineering Examination (FE Exam).

- Prepare and grade “practice” FE Exam for PI students.

- Use the practice FE Exam results to identify strengths/weaknesses of engineering programs.

- Determine whether an official NCEES FE Exam can be undertaken at the PI.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

- FE Exam review tutorial material was developed by UMD and sent to the PI.

- Dr. Ainane conducted a sixteen-hour tutorial review for the practice FE Exam test at the PI.  An additional thirty-two hours of tutorials were taught by PI faculty.

- Seventy-one 2007 graduating seniors from the PI undertook an eight-hour FE Exam (morning and afternoon exams, each of four hours duration).  The exams were graded by Dr. Ainane and the results communicated to the PI.

3.	Summary of Project Activities for the Completed Quarter

(As related to stated deliverables in #2. Include findings, accomplishments, figures, and/or schedule changes in this section.)

- All graduating 2007 PI senior students (71 in total) undertook the practice FE Exam on April 28, 2007.  The results were communicated to PI, which has performed detailed analyses of the results.

- Although the FE Exam undertaken by PI students was non-accredited, PI is seeking accreditation status from 2008 onwards.  In this regard, PI has solicited AMIDEAST (America-Mideast Educational and Training Services, Inc.) to consider proctoring an official NCEES FE Exam at PI.  AMIDEAST has agreed in principle to this request and has approached the Maryland State Board for Professional Engineers to inquire about the possibility of them administrating an official FE Exam in UAE, with AMIDEAST serving as proctor.  This proposal will be considered at the next scheduled meeting of the Maryland State Board, and their decision will be communicated directly to AMIDEAST.

4.	Difficulties Encountered/Overcome

- Even though a monetary award was offered to PI students who passed the FE exam [Grade A ($2,725), Passing grade ($1,362)], the majority of the students did not appear willing to put in the effort to pass the practice FE Exam.

5.	Planned Project Activities for the Next Quarter

- The FE Exam tutorial review notes will be updated, and a new exam, with discipline-specific afternoon tests in mechanical, electrical, and chemical engineering, will be developed.

- PI will continue discussions with AMIDEAST to determine whether an official NCEES FE Exam can be undertaken at the institute.

6.	Appendix

6.1	Justification and Background

- The National Council of Examiners for Engineering and Surveying (NCEES), who are the official body that administer the FE exam, have detailed statistics on the results for examinees who undertake the FE exam and have attended EAC/ABET-accredited college/university engineering programs.

- By undertaking a trial FE exam, PI will be able to benchmark student performance with corresponding US engineering programs as a metric for ABET accreditation.

- Although the trial FE exam undertaken by PI students on April 28, 2007 is non-accredited, UMD-PI team is seeking accreditation status from 2008 onwards.

6.2	Approach

Tutorial sessions are developed to prepare PI students for undertaking the trial FE exam, which covers the following topics:

- Mathematics, probability and statistics

- Statics, dynamics and materials science

- Thermodynamics and fluid mechanics

- Electrical circuits and computers

- Engineering economics

- Chemistry

- Ethics and business practices

A specially prepared tutorial revision package was supplied by the University of Maryland, supplemented with teaching materials developed by PI faculty.

These material was reviewed in 46 hours of tutorials, given over a nine week period.  PI faculty taught 32 hours, with an additional 16 hours of revision tutorials given by Dr. Ainane, during an on-site visit to PI in March 2007.

6.3	Two-Year Schedule

Year 1:

- Design review course to prepare PI students for Fundamentals of Engineering examination.

- Prepare and grade “practice” Fundamentals of Engineering examination for PI students.

- Establish if an official NCEES FE Exam can be undertaken at PI in 2008.

Year 2:

- Modify and revise review course to prepare PI students for Fundamentals of Engineering examination based on Year I experience.

- Prepare and grade “practice” Fundamentals of Engineering examination for PI students.

6.4	Key References

An overview of the FE exam process can be obtained at http://www.ncees.org, which is the official website for The National Council of Examiners for Engineering and Surveying (NCEES), which administers the FE exam.

Robust Optimization of Petrochemical Systems UMD Investigator: Dr. Shapour Azarm PI Investigators: Dr. Saleh Al Hashimi and Dr. Tareq Al Ameri GRAs: UMD’s GRAs (started in January 2007): Mr. Genzi Li and Mr. Ramzi Al Saari (ADNOC Fellow); PI’s GRA: Ms. Naveen Al Qasas Start Date: October 2006 Report Date: 30 June 2007

1.	Objective/Abstract

The objective of this study is to develop a framework for robust optimal design of distillation columns, while considering net profit effects at the plant level. The investigation will mainly focus on engineering decisions but will also consider the effects of these decisions on business objectives while maintaining the required product specifications. The investigation will also explore tradeoffs between engineering objectives versus expected profit and other business goals when there is uncertainty.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

- A preliminary literature review for distillation tower optimization has been completed. A copy of this report was sent to PI for their perspective and additions.

- The PI-UMD team met on a regular basis via MSN. The last meeting was on May 17, 2007.

- A preliminary optimization model for distillation tower design has been developed/implemented. Further extensions of this model are underway.

- The development of a new optimization method has been completed. This new method was applied to a distillation tower, and other numerical test problems were completed (see Section 3 for details). A report of the progress was given during the PI-UMD video-conference meeting on May 23, 2007.

- A joint journal paper is under preparation.

3.	Summary of Project Activities for the Completed Quarter

(As related to stated deliverables in #2.  Include findings, accomplishments, figures, and/or schedule changes in this section.)

The next few slides provide a summary of project activities for the completed quarter.

4.	Difficulties Encountered/Overcome

N/A

5.	Planned Project Activities for the Next Quarter

- Perform robust optimization with interval uncertainty.

- Update distillation tower model, i.e., cost model, and subsequently the optimization.

- Complete the joint journal paper on the new MOGA with distillation column design optimization

6.	Appendix

6.1	Justification and Background

Optimization-based design of distillation towers needs to be better understood, particularly when significant variability exists during the operation of these systems in a refinery plant.

A preliminary review of the literature has revealed that previous methods in design and/or operation of petrochemical systems have been mainly based on either engineering decisions or business decisions.  The literature is sparse for the cases when these two types of decisions are integrated sequentially. However, given that operating decisions are based on engineering and business considerations simultaneously, these methods should be further developed and tuned to actual conditions of real plants to increase profitability.

6.2	Approach

There are two main tasks in the proposed approach. Both tasks will begin after a literature review in the respective domain is performed.

Task 1 (PI):

Develop and implement engineering analysis models for a petrochemical system:

- Task 1.1: Develop a MATLAB-based multi-input, multi-output analysis model for a distillation column.

- Task 1.2: Extend the above analysis model for the distillation column to include: (i) additional complexity, (ii) subsystem details; or, expand the model to include other subsystems in a plant. The ultimate goal is to develop an integrated multi-subsystem petrochemical analysis model for a plant or a group of units in the plant.

Task 2 (UMD):

Develop and implement a robust optimization approach:

- Task 2.1: Develop and implement a MATLAB-based multi-objective and reliability-based robust optimization approach for the above analysis models.

Task 2.2: Extend the robust optimization approach to consider the case when: (i) the upper and lower bounds for the known range of inputs include quantifiable variability, (ii) for a subset of uncertain inputs, their probability distribution is available, while for the remaining inputs the range is given.

6.3	Two-Year Schedule

Tasks 1 and 2 will begin in the first year. Tasks 1.1 and 2.1 are expected to be completed by the end of the first year. Tasks 1.2 and 2.2 will begin toward the end of the first year and are expected to be completed by the end of the second year.

6.4	Key References

- Forbes, R.J., Short History of the Art of Distillation, E.J. Brill, Leiden, 1948.

- Grossmann, I. E., Sargent, R. W. H., “Optimum Design of Chemical Plants with Uncertain Parameters,” AIChE Journal, 24(6): 1021-1028, 1978.

- Halemane K. P., Grossmann I. E., “Optimal Process Design under Uncertainty,” AIChE Journal, 29 (3): 425-433, 1983.

- Inamdar, S. V.; Gupta, Santosh K.; Saraf, D. N, “Multi-Objective Optimization of an Industrial Crude Distillation Unit Using the Elitist Non-Dominated Sorting Genetic Algorithm,” Chemical Engineering Research and Design, 82(5): 611-623, 2004.

- Janak, S. L., Lin, X., Floudas, C. A., “A New Robust Optimization Approach for Scheduling Under Uncertainty: II. Uncertainty with Known Probability Distribution,” Computers and Chemical Engineering, 31, 171-195, 2007.

- Li, M., S. Azarm, and A. Boyars, “A New Deterministic Approach using Sensitivity Region Measures for Multi-Objective and Feasibility Robust Design Optimization,” Trans. ASME, Journal of Mechanical Design, 128 (4), 874-883, 2006.

Lin, X., Janak, S. L., Floudas, C. A., “A New Robust Optimization Approach for Scheduling Under Uncertainty: I. Bounded Uncertainty,” Computers and Chemical Engineering, 24, 1069-1085, 2004.

Solid Oxide Fuel Cells for CO2 Capture and Enhanced Oil Recovery UMD Investigators: Prof. Greg Jackson Senior Research Associates: Dr. Serguei Dessaitoun, Dr. Mary Sukeshini GRA’s: Paul Jawlik and Young Kyong Jo PI Investigator(s): Prof. Valerie Eveloy, Prof. Afshin Goharzadeh Start Date: October 2006 Report Date: 30 June 2007

1.	Objective/Abstract

This multi-faceted project will investigate the feasibility of implementing advanced solid oxide fuel cell (SOFC) technology for producing power from oil well off-gases while providing a source of concentrated CO2 for sequestration and enhanced oil recovery.  This project will explore fundamental issues in identifying preferred material combinations for durable SOFC anode operation with typical oil well off-gas composition. Along with these fundamental issues, multi-scale modeling will include detailed models for assessing SOFC membrane electrode assembly architectures for optimal operation with hydrocarbons, and higher-level system models for evaluating integrated systems with all accessory equipment within the context of oil well operation.  System models will assess the economic viability of such a system and thereby determine technology performance requirements for successful implementation of SOFC-based systems for enhanced oil recovery with CO2 injection.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

The following milestones are listed for the project, and although none were scheduled for completion until Fall 2007, several accomplishments were made toward meeting the first two milestones for the upcoming Fall.

- Operational experimental rig at the PI by Fall 2007 – PI faculty, with significant UMD guidance (including a visit by Dr. Jackson in late March), have been acquiring necessary flow and process equipment along with analytical equipment (such as electrochemical workbench) for establishing an SOFC test facility there this fall.

- SOFC design modeling tool with results showing preferred architectures by Fall 2007 – The UMD team has continued to enhance the SOFC modeling tool to look at fuels other than H2.  This tool is being validated against a wide array of data both from UMD experiments as well as from the literature.

- System-level modeling tool for exploring integration feasibility with oil production facilities by Fall 2007 – PI/UMD have discussed and prepared to implement models into HiSys/Aspen, which is currently used at the PI facility.

- Summary of experimental findings, kinetic models, and electrochemical performance for light hydrocarbons on preferred SOFC membrane electrode assemblies by Fall 2008.

3.	Summary of Project Activities for the Completed Quarter

Over the past quarter, UMD and PI have focused efforts on Tasks 1 and 2 as described in Appendix 1.    Accomplishments on these first two tasks along with preliminary work on Task 3 are discussed here.

Task 1:  Experimental study of SOFC MEA’s for hydrocarbons

UMD has spent significant effort exploring fabrication methods for developing optimal micro-architectures for metal-doped ceria anodes.   Figure 1 shows the experimental configuration for single-cell SOFC’s in which these anode architectures are being explored.   The anodes (both the functional and support regions) are an integrated mixture of catalyst (Ni or CeO2) with a porous YSZ electrolyte matrix (in direct contact with the dense YSZ electrolyte membrane, as indicated in Figure 1).  Various processes have been tested for fabricating the optimal YSZ porous anode matrix as well as subsequent CeO2 (or Ni) impregnation.  Methods to date have included the use of YSZ powders (Tosoh, Inc.) with carbon-based pore formers that are burned out during processing to form the porous YSZ matrix as well as the use of prefabricated porous tapes (from Electro-Science, Inc.).  Along with this effort, the UMD team has been focusing on ways to integrate these anodes with very thin but dense electrolyte membranes (< 20 μm) with the focus on using electrolyte tapes from Electro-Science, Inc.   These efforts have revealed the importance of the process heating and cooling cycle in maintaining solid thin-film electrolytes integrated with the anodes.  Completion of the fabrication processing studies will be this month, with transitioning to testing of high-power density cells.

Figure 1. Schematic (taken from Kee, Zhu, Sukeshini, and Jackson 2007) which shows architecture of single-cell SOFC’s with the anode layer including the functional layer near the dense YSZ electrolyte and the support layer providing structural integrity and gas diffusion for the anode.

Along with the fabrication study for thin electrolytes with porous anode supports, work has continued with thick electrolyte-supported cells with both Ni and CeO2 anode catalysts.  The thick electrolytes do not permit high power density due to the significant bulk resistance losses in the thick electrolyte.  Nonetheless, results have been obtained with hydrocarbon/H2 mixtures on both porous Ni/YSZ anodes as well as on CeO2 anodes (discussed further in Task 2).  Some results for Ni/YSZ anodes running on H2/n-C4H10 mixtures are shown in Figure 2.  With Ni anodes, performance was found to degrade for C4H10 after 150 s of exposure.  The low-current densities are indicative of the electrolyte-supported cells, and these results, along with past in-house and literature studies, are motivating the development of composite metal/CeO2 anodes.

Figure 2. Single-cell SOFC performance at 720 °C after exposure to a) H2/CH4 mixture and b) H2/C4H10 mixture.  SOFC’s were made with porous Ni/YSZ porous anodes (20 μm thick), dense YSZ electrolytes (800 μm thick), and LSM/YSZ composite cathodes.  Red curves are after 10 s of exposure, and blue curves are after 150 s of exposure.

Preliminary work has also been done on sputter-deposited CeO2 anodes with porous gold overlayers for current collection with thick electrolytes.  These tests have been performed to provide idealized geometries for developing electrochemical kinetic models for H2, CO, and hydrocarbon oxidation on CeO2. These models are to be used in Task 2.  This work will transition to porous Cu/CeO2 and/or Au/CeO2 anodes with thin electrolytes for high power densities in the upcoming quarter.

Interactions with the PI faculty and UMD faculty and students have been extensive over the past quarter in the attempts to design and assemble a fully functioning single-cell SOFC test rig at the PI.  UMD and PI faculty designed and specified a test facility for the PI, and PI faculty through conversations with suppliers and further discussions with UMD have revised some of the rig specifications to meet safety concerns as well as to address issues related to cost.  PI has purchased some equipment, such as an electrochemical workbench, furnaces, and other supplies, with the expectation that the rig will be functioning in Fall 2007.  UMD will assist the PI in setting up this facility.

Task 2: Numerical modeling for design of SOFC architectures

The modeling of 1-D SOFC architectures for design optimization has continued on this program.  The models have been further developed in this quarter to include distributed electrochemical reaction regions, improved kinetic models with operation on CH4 as well as syngas (H2/CO) on Ni/YSZ anodes.  Efforts to extract fundamental kinetic rates on CeO2 catalysts continue through analysis of sputter-deposited thin-film anodes as mentioned in Task 1.  Progress on fitting these results to proposed oxidation and mixed ionic-electronic conductivity models for CeO2 is ongoing and should be complete by the end of next quarter.

Finally, these 1-D through the membrane-electrode assembly (MEA) models are being integrated into a down-the-channel model from which results should be presented in the next quarterly report.

Task 3: System-level analysis of integrated SOFC plants

The only accomplishment on this task during the past quarter was the establishment of a plan to implement Aspen/Hisys models housed in the Chemical Engineering Department at PI for this part of the project.  This effort has not yet begun, but it is planned for the upcoming quarter.

4.	Difficulties Encountered/Overcome

The principal challenges for this program have been in the fabrication of anode-supported cells (Task 1), the acquisition of equipment for the PI rig (Task 1) and in the development of the CeO2 electrochemical kinetic models for the modeling design effort (Task 2).  These challenges are the focus of progress to be made in the upcoming quarter.

5.	Planned Project Activities for the Next Quarter

In the upcoming quarter, the following activities are expected for Tasks 1-3.

Task 1:  Experimental study of SOFC MEA’s for hydrocarbons

- Finalize fabrication protocol for high-power density cells with thin electrolytes and metal-doped CeO2 anodes.

- Complete preliminary UMD studies comparing operation of SOFC’s with syngas and with humidified and dry hydrocarbons (no larger than n-C4H10).

- Complete purchase and acquisition of supplies and equipment for PI SOFC test facility and begin assembly of test rig.

Task 2: Numerical modeling for design of SOFC architectures

- Complete development of hydrocarbon electrochemical models (CeO2 and Ni) and study optimal anode architectures for hydrocarbons  with 1-D through-the-MEA models.

- Develop a down-the-channel model at UMD and begin study of SOFC operation with high fuel utilization and various inlet fuel compositions.

Task 3: System level analysis of integrated SOFC plants

- Begin development of SOFC and balance of plant models in Aspen or Hisys at PI.

Task 4: Identification of multi-university research team for SOFC’s in the petroleum industry.

- No activities are planned for this task until after some of the above accomplishments are achieved in Fall 2007.

6.	Appendix

6.1	Justification and Background

This work, combined with the development of detailed microstructure models and higher-level system models, will provide the basis for pursuing a combined experimental and multi-scale modeling effort that will explore the possibility of implementing new high-temperature solid oxide fuel cells in petroleum extraction. These models will aid in both high-efficiency power production and production of concentrated CO2 streams for enhancing oil recovery while sequestering CO2 emissions.  This collaborative work will allow the Petroleum Institute and UMD to become leaders in promoting SOFC technology to improve the operation of and reduce the environmental impact of oil recovery.

SOFC power plants provide a unique opportunity to provide ultra-high efficiencies (> 64% electrical) while simultaneously separating CO2 emissions from N2 dilution for efficient CO2 sequestration1. While SOFC architectures/membrane electrode assemblies (MEA’s) have been developed for operating with small-molecule fuels (H2, CO, and CH4)2, challenges remain in the development of SOFC assemblies for higher hydrocarbon fuels, although recent progress in SOFC design and materials has indicated the feasibility of such systems3,4 . The UMD team has been evaluating SOFC anodes5 for small hydrocarbon fuels, and recent unpublished work on alternative ceria-based anodes shows promise for stable operation with hydrocarbons.

6.2	Approach

Four tasks identified for this project are presented here.

Task 1:  Experimental study of SOFC MEA’s for hydrocarbons

UMD has high-temperature single-cell rigs with electrochemical characterization tools, electronic flow controls, and data acquisition for studying SOFC MEA’s.  This project will expand these capabilities to study porous MEA architectures of ceria-based anodes for stable operation on C3-C5 gases.  Experiments will explore the role of metal doping of the ceria for improved electronic conductivity and activity for fuel breakdown to avoid carbon build-up. The experiments will include V-I measurements as well as impedance spectroscopy to validate models developed in Task 2, as well as post-testing microscopy and surface characterization to evaluate the durability of the SOFC anodes for the different fuels. After being established at UMD, these capabilities will be duplicated at the Petroleum Institute (PI) with the aid of UMD researchers such that faculty at the PI will also participate in this effort while providing PI students a chance to explore SOFC technology.

Task 2: Numerical modeling for design of SOFC architectures

Modeling of membrane electrode assemblies will explore optimal design of SOFC’s for hydrocarbon operation and high fuel conversion efficiency to provide optimal CO2 capturing by eliminating downstream combustion of unburned fuel.  This work will build on 1-D and 2-D detailed Matlab/Cantera-based models developed at UMD for SOFC MEA analysis.  New efforts will involve the development and validation of hydrocarbon kinetic models on preferred anode materials identified in Task 1.  The Petroleum Institute will seek to implement some of the multi-physics modeling capabilities/predictions of the UMD codes into commercial codes that provide for simulation of complex geometries.

Task 3: System level analysis of integrated SOFC plants

The economic and engineering viability of an integrated SOFC plant for CO2 sequestration and efficient power production1 will be put within the context of petroleum production with system level modeling tools developed at UMD (in Matlab) and at PI (in selected commercial software).  These tools will be used to explore overall balance of the plant, adequacy of fuel supplies, and power requirements for CO2 capture.

Task 4: Identification of multi-university research team for SOFC’s in the petroleum industry.

The UMD/PI team will spend a portion of his time developing a broader-base team for pushing this project further toward implementation. Potential partners may include the Colorado School of Mines and the Norwegian University of Science and Technology, with whom UMD has established collaborations.

6.3	Two-Year Schedule

Year 1:

- Begin experiments for identifying preferred material systems using ceria-based anodes for hydrocarbon SOFC operation.

- Perform post-testing material characterization for evaluation.

- Acquire equipment for assembly rig at the PI.

- Adopt Matlab SOFC models at UMD for hydrocarbon studies.

- Input Matlab models into Fluent simulations at PI.

- Establish system level models at both institutions.

Year 2:

- Perform experiments with preferred material systems for typical off-gas compositions (with varying team loadings).

- Validate models and perform SOFC design for both MEA microstructure and overall all fuel cell size.

- Identify preferred system configurations for overall balance of plant.

6.4	Key References

1.	Moller, B. F.; Arriagada, J.; Assadi, M.; Potts, I. Journal of Power Sources 2004, 131, 320-326.

2.	Brandon, N. P.; Skinner, S.; Steele, B. C. H. Annual Review of Materials Research 2003, 33, 183-213.

3.	Gorte, R. J.; Vohs, J. M.; McIntosh, S. Solid State Ionics 2004, 175, 1-6.

4.	Murray, E. P.; Harris, S. J.; Liu, J.; Barnett, S. A. Electrochemical and Solid State Letters 2006, 9, A292A294.

5.	Sukeshini, A. M.; Habibzadeh, B.; Becker, B. P.; Pomfret, M. B.; Demircan, O.; Walker, R. A.; Eichhorn, B. W.; Jackson, G. S. SOFC-IX Symposium, Quebec City, Canada, 2005; p 1294-1303.

Study of Condensing Flows in a Micro-scale Channel with a Micro-element Array and Visual Techniques UMD Investigators: Dr. S. Dessiatoun GRA’s: Ebrahim Al-Hajri, Sourav Chowdhury PI Investigator(s): Dr. A. Goharzadeh Start Date: December 2006 Report Date: 30 June 2007

1.	Objective/Abstract

The proposed two-year study will investigate, by different experimental techniques, the fundamentals of the two-phase condensing flow phenomenon in a sub-millimeter microchannel. In order to understand the mechanism of the flow, local measurements of heat flux, temperature and flow velocities are necessary. The present project intends to use a micro-heat sensor array along the microchannels and the optimum flow-visualization technique to measure heat flux distribution and local fluid- and vapor-phase velocities, respectively.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

- Leaks were located and fixed.

- Finished the tests for R24fa; however, there are some tests that need to be repeated for assurance. The completed tests are listed here:

    - All 300 kg/m2s mass flux tests for saturation temperatures from 30 – 70 oC and for 0-15 oC super heat inlet conditions

    - Tested 50 oC saturation temperature with 400 kg/m2s mass flux and for 0 and 10 oC super heat inlet conditions.

3.	Summary of Project Activities for the Completed Quarter

(As related to stated deliverables in #2.  Include findings, accomplishments, figures, and/or schedule changes in this section)

Table 1. Comparison of refrigerant properties

|  | Tsat ( oC ) | Psat ( kPa) | Density (kg/m3) | Enthalpy (kJ/kg) | Viscosity ((Pa.s) | Surface Tension (mN/m) |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | liquid | liquid | vapor | liquid | vapor |  |
| R-134a | 30 | 770 | 1187.5 | 241.7 | 414.8 | 185.8 | 12.04 | 7.42 |
|  | 70 | 2116 | 996.2 | 304.3 | 428.7 | 106.4 | 14.65 | 2.61 |
| HFE-7100 | 30 | 34.2 | 1455 | 58.8 | 179.6 | 655 | n.a. | 13.0 |
|  | 70 | 138.2 | 1343 | 104.8 | 213.3 | 335.8 | n.a. | n.a |
| R-245fa* | 30 | 179 | 1325.1 | 239.6 | 427.5 | 376.4 | 10.51 | 13.41 |
|  | 70 | 610 | 1204.7 | 295.7 | 456.6 | 226.8 | 12.0 | 8.35 |

The results of R245fa tests show similar trends, as seen above with the results of R-134a. Although these tests were conducted during different times of the year and of the day, they show the effectiveness and accuracy of the system and the repeatability of the tests. Figures 1 through 6 show the results of R245fa. Figures 1 and 2 indicate that the inlet superheat affects the heat transfer coefficient but not the pressure drop, respectively. This is because most the heat transfer occurs at the portion of the flow, where it is represented by annual flow. Therefore, as the inlet superheat increases, the annular flow becomes longer, which then allows more heat to be transferred through the longer condensed film in the case of higher inlet superheat condition. No significant effects of inlet super heat on pressure drop are obvious. That is because the flow patterns in all inlet superheat conditions are similar, since the channel is very small and the condensed film from all four walls of the channel collapses before the condenser outlet. Therefore, the fluid leaves the condenser as saturated liquid in all inlet superheat conditions.

Figure 1. Results of R245fa and the effect of inlet superheat on heat transfer coefficient

Figure 2. Results for R245fa on the effect of inlet superheat on pressure drop

Figure 3 indicates that the heat transfer coefficient decreases with an increase in saturation temperature, primarily due to decrease of latent heat of phase change. At 30oC, the latent heat of phase change is 187.9 kJ/kg whereas at 70oC it is 160.9 kJ/kg. Pressure drop also decreases with an increase in the saturation temperature, shown in Figure 4, as dynamic viscosity decreases. Between 30oC and 70oC saturation temperature, the saturated liquid dynamic viscosity decreases by 40%, as indicated in the comparison Table 1.

Figure 3. Results for R245fa on the effect of saturation temperature on heat transfer coefficient

Figure 4. R245fa results the effect of saturation temperature on pressure drop

The results of Figure 2 are also reflected in Figure 6, showing that the decrease in pressure drop due to inlet superheat is insignificant. However, the increase of pressure drop is due to an increase in the velocity, which is expected. As for the effect of mass flux on heat transfer coefficient at 50oC saturation temperature, Figure 5 shows that there is a noticeable proportional relation between mass flux and heat transfer coefficient. The slight increase in heat transfer between 0 and 10oC inlet superheat conditions is again due to an increase in length of annular flow regime (being longer in the 10oC inlet superheat than in the 0oC inlet superheat condition).

Figure 5. Results for R245fa on the effect of mass flux on heat transfer coefficient

Figure 6. Results for R245fa on the effect of mass flux on pressure drop

4.	Difficulties Encountered/Overcome

- High summer temperatures have restricted some testing conditions, such as the case of 30oC saturated temperature, where the room temperature reaches above 30oC.

- Pump gears are wearing out, causing the worn material to collect at the filter, which in turn causes high pressure drop at the filter. Delays have occurred while the filter is replaced, due to discharging, vacuuming and charging the system again.

5.	Planned Project Activities for the Next Quarter

- Finish all remaining tests for R245fa and R-134a.

- Check leaks in the visualization loop as a preparation for testing the LDV visualization system.

- Collect some visualization tests.

- Build and install a higher capacity sub-cooler for constant quality flow testing

6.	Appendix

6.1	Justification and Background

With the development of new manufacturing technologies and fluid maintenance techniques, miniaturization of heat transfer systems has proven to be possible and to afford great economic benefits.  Two orders of magnitude of reduction in system weight and volume with significant reductions in cost have become feasible. Sufficient data and advanced modeling are available to characterize boiling processes in microchannels. However, such data are lacking for condensing flows in micro-scale passages and are necessary for development of predictive models and correlations in the future.

This project will be conducted in two parts. To investigate local heat transfer with precision, the first part will use the micro-fabricated element-array technique to measure local heat flux and temperature profiles.  This will enable understanding of the flow and condensation process in greater detail than traditional methods have presently allowed. In the second part, flow visualization at the micro-scale will be used to complement the heat transfer experiments to provide data on velocity profiles and flow dynamics that are unobtainable by heat transfer measurements. This combined data set will be used in future predictive models and correlations, which will pave the way for optimization of two-phase, high-performance heat transfer systems.

In the present age of miniaturization, there is a need to understand flow phenomena in compact phase-change-type micro-fluidic systems. In recent years, work has characterized the boiling phenomenon using high-speed optics, micro-heater arrays for local wall temperatures, and heat flux measurements and Particle Image Velocimetry (PIV) techniques. Those techniques significantly improve the understanding of boiling phenomenon. Similar experiments in condensation, particularly micro-array heat flux and temperature experiments combined with PIV studies can provide extremely valuable information for the understanding of the condensation phenomenon in microchannels.

6.2	Approach

UMD-side participation

- (a) Conduct an extensive literature survey for experimental studies on condensation of refrigerants in microchannels of hydraulic diameter 1 mm or less, and extract useful data for heat transfer and pressure drops. (b) Conduct a survey of literature for analytical/numerical models in microchannel condensing flows and study them. Understand inputs typically needed for predictive models. (c)  Work with PI to conduct a survey of literature and vendors for flow visualization of two-phase micro-fluidic systems.

- Based on above literature study, design prototype of a microchannel with a platinum micro-resistors array and experimental loop.

- Develop the processes for micro-array fabrication and microchannel fabrication and make necessary design changes to accommodate technical issues. Finalize experimental prototype design.

- Fabricate prototype and complete instrumentation. Fabricate experimental loop.

- Test experimental loop for various mass flow rates of a suitable refrigerant fluid at different two-phase qualities. Collect test data on local heat fluxes on channel walls, overall pressure drop, and high-speed digital video evidence.

- Work with PI to fabricate the recommended flow-visualization prototype and associated experimental loop parts.

PI-side participation

- Work with UMD to conduct an extended literature survey on the flow visualization on micro-fluidic systems focusing on multi-phase flow.

- Develop the optimum flow visualization system for multi-phase flow inside a microchannel.

- Work with UMD to recommend a design suitable for the optimum visualization technique. Develop requirements and recommendations for a flow-visualization test section that will be fabricated by UMD.

- Conduct flow visualization measurements inside the microchannel prototype designed and fabricated at UMD.

5.	Compare flow-visualization data with UMD micro-array data.

6.3	Two-Year Schedule

UMD-side participation

Year 1.

- Literature review and summary.

- Design of micro-array prototype.

- Investigation of micro-array fabrication.

- Fabrication of experimental setup.

Year 2.

- Final fabrication of micro-array prototype.

- Final fabrication of visualization prototype and loop.

- Experimentation on micro-array.

- Final report.

PI-side participation

Year 1.

- Literature review and summary.

- Development of optimum visualization setup.

Year 2.

- Experimentation on visualization setup designed and fabricated in UMD.

- Final report.

6.4	Key References

1. 	Kim, J., Benton, J., McQuillen and J, Vickerman, M., 2001,”Subcooled Pool Boiling in Microgravity and Hi-g”, Journal of Heat Transfer, vol. 123, iss. 4, pp. 620.

2. 	Lee, J., Kim, J. and Kiger, K. T., 2000, “Time and Space Resolved Heat Transfer Characteristics of Single Droplet Cooling Using Microscale Heater Arrays,” International Journal of Heat and Fluid Flow, Vol. 22, pp. 188.

3.	Begg, E., Khustalev, and D., Faghri, 1999, “Complete Condensation of Forced Convection Two-Phase Flow in a Miniature Tube,” Journal of Heat Transfer, Vol. 121, pp. 904.

4. 	Garimella, S., 2004, “Condensation Flow Mechanisms in Microchannels: Basis for Pressure Drop and Heat Transfer Models,” Heat Transfer Engineering, vol. 25, iss. 3, pp. 204.

5. 	Yang, C.Y. and R.L. Webb, 1996, “Friction Pressure Drop of R-12 in Small Hydraulic Diameter Extruded Aluminum Tubes with and without Micro-Fins,” Int. J. Heat Mass Transfer, vol. 39, iss. 4, pp. 801.

6. 	C. D. Meinhart, S. T. Wereley, J. G. Santiago, 1999, “PIV measurements of a microchannel flow” Exp. In Fluids, vol. 27, pp 414.

Sulfur Recovery from Gas Stream using Flameless and Flame Combustion Reactor UMD Investigators: Prof. Ashwani K. Gupta GRA’s: To be assigned PI Investigator(s): Dr. Mohamed Sassi Start Date: October 2006 Report Date: 30 June 2007

1.	Objective/Abstract

To obtain fundamental information on the thermal process for sulfur recovery from sour gas by conventional flame combustion and flameless combustion using numerical and experimental studies. The ultimate goal is to determine optimal operating conditions for sulfur conversion. Therefore, an experimental study of the flameless versus flame combustion process for the Claus furnace is proposed. In the study we will explore the operating conditions and the exhaust gas analysis of both flame and flameless modes of reactor operation in the process of enhanced sulfur recovery.

Specific objectives will be to provide:

- A comprehensive literature review of the existing flame combustion process for sulfur removal with special reference to sulfur chemistry.

- Near isothermal reactor conditions and how such conditions assist in the enhanced sulfur recovery process.

- CFD simulation of the flame and flameless combustion in the furnace.

- Design of a flameless combustion furnace for experimental verification of the numerical results.

- Measurements and characterization of the flameless combustion furnace using high temperature air combustion principles.

- Experiments with different sulfur content gas streams using the flame and flameless combustion furnace modes of operation.

- Determination of the product gas stream for evaluation of sulfur recovery in the process.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

We have obtained some of the sulfur chemistry data and incorporated it into the Chemkin code for capturing the fate of sulfur under different non-reacting and reacting conditions. Preliminary simulations have been performed under different non-reacting and reacting conditions with different concentrations of H2S in the gas. The goal here has been to determine the behavior of sulfur under different conditions with an attempt to determine the most desirable conditions for sulfur removal.

3.	Summary of Project Activities for the Completed Quarter

(As related to stated deliverables in #2.  Include findings, accomplishments, figures, and/or schedule changes in this section.)

Sample simulation results obtained at low to high concentrations of H2S in the gas under both non-reactive and reactive conditions are given below. There is no schedule change. We have also written a paper for a special issue on air pollution modeling, prevention, and control for the American Journal of Environmental Sciences. The paper is based on the detailed literature review conducted and is entitled “Sulfur Recovery from Acid Gas Using the Claus Process and High-Temperature Air Combustion (HiTAC) Technology.”

Figure 1. Species mole fractions for non reactive case with 2% H2S and 98% CH4

under equilibrium condition

Figure 2. Major sulfide species for non-reactive case with high H2S concentrations of 25% H2S in 75% CH4 under equilibrium condition

Figure 3. S2 concentration for non reacting case at various temperatures with 50% H2S and 50% CH4 mixture under equilibrium conditions

Figure 4. Reacting case with 2% H2S, 98% CH4 at stoichiometric air-to-fuel ratio.

Figure 5. S2, S3 and S4 concentration for reacting case at different temperatures with 2% H2S, 98% CH4 at stoichiometric air-to-fuel ratio. (Note that mole fraction of S8<S7< S6< S5< S4< S3< S2)

Figure 6. H2S concentration at different reactor temperature under reacting case with 50 % H2S and 50% CH4 (i.e., 0.5 CH4+ 0.5 H2S + 1 O2 + 3.76 N2 --( Products)

4.	Difficulties Encountered/Overcome

Obtaining detailed chemistry for higher molecular weight sulfur, for example S8, is an issue. The PI team members are encouraged to have a face-to-face meeting with the UMD team to discuss this issue.

5.	Planned Project Activities for the Next Quarter

Seek detailed chemistry data for higher molecular weight sulfur compounds. Identify parameters for CFD simulations using Fluent.

6.	Appendix

6.1	Justification and Background

Hydrogen sulfide is present in numerous gaseous waste streams from natural gas plants, oil refineries, and wastewater treatment plants, among other processes. These streams usually also contain carbon dioxide, water vapor, trace quantities of hydrocarbons, sulfur, and ammonia. Waste gases with ammonia are called sour gases, while those without ammonia are called acid gases. Sulfur must be recovered from these waste streams before flaring them. Sulfur recovery from sour or acid gas typically involves application of the well-known Claus process, using the reaction between hydrogen sulfide and sulfur dioxide (produced at the Claus process furnace from the combustion of H2S with air and/or oxygen), yielding elemental sulfur and water vapor: 2H2S(g) + SO2(g) = (3/n) Sn(g) + 2H2O(g) with DHr= -108 kJ/mol. Therefore, higher conversions for this exothermic, equilibrium-limited reaction call for low temperatures, which lead to low reaction rates that dictate the use of a catalyst. The catalytic conversion is usually carried out in a multistage, fixed-bed, adsorptive reactor process, which counteracts the severe equilibrium limitations at high conversions. This technology process can convert about 96% to 97% of the influent sulfur in H2S to S. However, higher removal requires critical examination of the process and use of a near isothermal reactor, since the conversion is critically dependent upon the exothermic and endothermic conditions of the reactions.

Flameless combustion has been shown to provide uniform thermal field in the reactor so that the reactor temperature is near uniform. Reactor size can also be reduced, and combustion-generated pollutants emissions can be reduced by up to 50%.  Energy efficiency can be increased by up to 30%. The application of this technology appears to offer great advantages for the processes under consideration. The UAE, which pumps about 2.4 million bpd of crude oil, is also home to the world’s fifth biggest gas reserves at about 200 trillion cubic feet. Abu Dhabi Gas Industries (GASCO), an operating company of the Abu Dhabi National Oil Company (ADNOC), is leading a drive to boost gas production in the UAE from five to seven billion cubic feet per day. This calls for sulfur recovery capacity of over 3,000 metric tons per day with the associated SOx and NOx emissions. Therefore, the adoption and further development of flameless combustion technology for sulfur recovery among other commercial and industrial heating processes is expected to be crucial and beneficial, both economically and environmentally.

The conventional sulfur recovery process is based upon the withdrawal of sulfur by in situ condensation within the reactor. The selective removal of water should, however, be a far more effective technique, as its effect on the equilibrium composition in the mass action equation is much greater. The in situ combination of the heterogeneously catalyzed Claus reaction and an adsorptive water separation seems especially promising, as both reaction and adsorption exhibit similar kinetics, and pressure can be adapted to the needs of the adsorptive separation. Such an adsorptive reactor will lead to almost complete conversion as long as the adsorption capacity is not exhausted. There are numerous possibilities for implementing these two functions, ranging from fixed-beds with homogeneous catalyst/adsorbent mixtures to spatially structured distributions or even fluidized beds. Most of the previous studies have concentrated on the Claus catalytic conversion reactors and the TGTU. However, some previous studies have identified the Claus furnace as one of the most important yet least understood parts of the modified Claus process. The furnace is where the combustion reaction and the initial sulfur conversion (through an endothermic gaseous reaction) take place.  It is also where the SO2 required by the downstream catalytic stages is produced and the contaminants (such as ammonia and BTX (benzene, toluene, xylene) are supposedly destroyed. The main two reactions in the Claus furnace are: H2S + 3/2 O2 = SO2 + H2O, with DHr= -518 kJ/mol, and 2H2S + SO2 = 3/2 S2 + 2H2O, with DHr= +47 kJ/mol. This last endothermic reaction is responsible for up to 67% conversion of the sulfur at about 1200 C. Moreover, many side reactions take place in the furnace; these side reactions reduce sulfur recovery and/or produce unwanted components that end up as ambient pollutant emissions. Therefore, it would be useful to combine the endothermic and exothermic process using an isothermal reactor offered by flameless oxidation combustion.

6.2	Approach

Critical review

We propose to conduct a critical review of the various approaches used for sulfur removal from the sour gas. The emphasis here will be on sulfur chemistry with due consideration to the fate of ammonia. Following the review, an experimental and a CFD numerical study of the flameless oxidation of the fuel will be conducted as follows:

CFD simulation

A numerical simulation study of the flame under normal and flameless oxidation of fuels in the furnace will be conducted using the available codes. Global features of the flow and thermal behavior will be obtained using the Fluent CFD and Chemkin computer codes. These codes provide detailed simulation of the flow, thermal and chemical behaviors (i.e., detailed chemistry) in the reactor flow using gas-phase reactants. The sulfur in the fuel is in gas phase, so we will be able to simulate and monitor the fate of sulfur during various stages of endothermic and exothermic reactions and over a range of temperature regimes, including those covered in the Claus furnace process. The simulation results will also guide the final design of the flameless furnace. The simulations will also help assist in the experimental program for data validation with the eventual goal of implementing the process for sulfur removal.

Experimental study

An experimental study of the flameless vs. normal flame combustion process for the conditions examined in the theoretical study, including that of Claus furnace, will be conducted. We will explore the operating conditions and the exhaust gas analysis under conditions of both flame and flameless modes to determine the extent of sulfur conversion under the two conditions over the temperatures that can simulate endothermic and exothermic conditions in the Claus furnace. The goal is to seek conditions that yield the highest sulfur recovery from a process. To some extent, these conditions will be based on the composition of the acid/sour gas, from sulfur-rich (>50% H2S) to lean (<20%H2S). It is expected that our fundamental information will contribute to the eventual design guidelines of an advanced sulfur recovery process furnace operating under flameless combustion mode.

6.3	Two-Year Schedule

Year 1: (Performing institution)

- Perform detailed literature review and document in a report to the PI (conducted by PI and UMD).

- Perform numerical simulation of the flow and thermal behavior using Fluent code (PI).

- Incorporate sulfur chemistry into the code for capturing the fate of sulfur in the process (UMD).

- Provide preliminary simulations on the chemistry and mechanistic pathways for sulfur and other key transformation and pathways that are considered critical for sulfur recovery (UMD).

- Provide preliminary design considerations for the flameless oxidation and normal flame conditions, and recommend how the conditions can be used to simulate exothermic and endothermic behavior (PI and UMD).

Year 2:

- Perform detailed simulations using the Fluent (PI) and Chemkin (UMD) computer codes with special emphasis on the role of uniform and controlled thermal fields in the reactor on sulfur recovery.

- Assemble a flameless oxidation furnace reactor that can also operate in the normal combustion mode (PI and UMD).

- Conduct experiments using flameless and flame combustion over a range of dynamic conditions determined in the numerical study (UMD).

- Provide a preliminary design of the reactor for enhanced sulfur recovery. Determine the extent of sulfur recovery from different concentrations in the gas stream (PI and UMD).

6.4	Key References

1. 	Elsner, M. P., Menge M., Müller, C. and Agar, D. W.: The Claus process: teaching an old dog new tricks, Catalysis Today, 79–80, 2003. pp. 487–494.

2. 	El-Bishtawi, R. and  Haimour, N.: Claus recycle with double combustion process,  Fuel Processing Technology 86, 2004. pp. 245– 260.

3. 	Cerru, F.G., Kronenburg, A. and Lindstedt, R.P.: Systematically reduced chemical mechanisms for sulfur oxidation and pyrolysis, Combustion and Flame, 146, 2006. pp. 437–455. 4. H. Borsboom, P. van Nisselroy, The EUROCLAUS® Process, Achema 2000, Frankfurt am Main, 2000.

4. 	Tsuji, H., Gupta, A. K., Hasegawa, T., Katsuki, M., Kishimoto, K., and Morita, M.: High Temperature Air Combustion: from energy conservation to pollution reduction, CRC Press, Boca Raton, FL, 2003.

Thermally Enhanced Polymer Heat Exchanger for Seawater Applications UMD Investigator: Prof. Avram Bar-Cohen GRA: Juan Cevallos PI Investigator(s): Dr. Peter Rodgers, Dr. Ahmed Abdala Start Date: October 2006 Report Date: 30 June 2007

1.	Objective/Abstract

The proposed two-year study will address the fundamental thermal performance issues associated with the use of thermal high-conductivity polymer materials, addressing their advantages and limitations and defining the heat exchanger configurations that optimize the unique characteristics of high conductivity polymer materials.

To achieve optimum thermal performance, a clear understanding of the thermal engineering characteristics of fiber-enhanced polymer tubes/channels and the fundamental thermo-fluid predictive relations that underpin heat exchange in such configurations will be developed.

Successful completion of this effort will provide fundamental thermofluid modeling relations for thermally enhanced polymer tubes and channels; it will also provide the basis for determining the environmental, weight, and cost advantages resulting from future applications of this technology to seawater heat exchangers for shipboard heat exchangers and for the petroleum and power industries.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

Task 1:

Conduct literature review on: (i) the strengths and weaknesses of various commercially available heat exchanger designs and (ii) current usage of polymer heat exchangers (PHX’s). – UMD

- The literature review compiled in quarter one has been developed further on the strengths and weaknesses of commercially available heat exchanger designs.

Task 2:

Assess the thermal, chemical, and mechanical properties of thermally enhanced polymer materials suitable for use in liquid-to-liquid heat exchangers. – UMD /PI

- Recent developments in commercially available thermally conductive polymeric materials have been reviewed, with candidate materials identified based on mechanical and thermal properties.

- Questionnaire circulated on HX usage to ADNOC OpCo managers to enquire on the specifics of HX usage and potential interest in the adoption of polymer-based HX designs.

Task 3:

Assess theoretical performance limit of polymer candidate materials and configuration(s). – UMD.

- The thermo-fluid performance of a liquid-to-liquid counterflow parallel-plate heat exchanger module was modeled and evaluated through parametric analysis.

- Thermal performance characterized in terms of COP (defined as ratio of total heat transfer to pumping power) for low-k polymer (0.25 W/m.K), high-k polymer (20 W/m.k) and aluminum alloy (168 W/m.K), with main findings outlined in Section 3.0.

Task 4:

Design and construct laboratory-scale test apparatus at UMD for thermal characterization of “building block” tube/channels. – UMD/PI

- Laboratory scale test apparatus at PI has been refined to permit higher flow rates for tube bank characterization.

Task 5:

Develop new polymer-nanocomposite materials: PI

- Polyphenylene sulfide (PPS) and polycarbonates have been selected as the polymer matrices for the polymer-graphite nanocomposite materials based on thermal, chemical and mechanical considerations.

- Graphite nanosheets have been prepared via thermal exfoliation of graphite oxide.

- The morphologies of both graphite oxide and exfoliated graphite oxide were characterized using X-ray diffraction (XRD) and a scanning electron microscope (SEM), with the latter analysis presented in Figure 1.

- PPS-graphite oxide and PPS-exfoliated graphite oxide composites have been prepared by coating graphite nanosheets with polymer chains.

- The thermal degradation behaviors of PPS, graphite oxide, and their composite have been characterized by thermal gravimetric analysis (TGA), with results shown in Figure 2.

| Figure 1. SEM images of: (a) natural flake graphite, (b) 0.5 mm thick graphite oxide film, and (c) thermally exfoliated graphite oxide. |
| --- |
| (a) Polyphenylene sulfide (PPS), graphite oxide (GO) and their composite (85% PPS, 15% GO). | (b) Polyphenylene sulfide (PPS), thermally exfoliated graphite oxide (TEGO) and their composite (90% PPS, 10% TEGO). |
| Figure 2. Thermal gravimetric analysis. |

3.	Summary of Project Activities for the Completed Quarter (As related to stated deliverables in #2.  Include findings, accomplishments, figures, and/or schedule changes in this section.)

- Identified current use and applications of low-k polymer heat exchangers in the cooling processes of highly corrosive or chemically aggressive fluids whose chemical inertness is beneficial; these heat exchangers are also used in other applications such as automotive intercoolers, ventilations systems and electronics cooling.

- Identified the few companies that produce thermally-conductive polymers, and identified the polymers’ pertinent material properties.  These material producers include Cool Polymers, GE Plastics, PolyOne, Ticona, and Saint Gobain.  The materials offered vary in thermal conductivity from 1 W/m.K to 20 W/m.K.

- Modeled the thermo-fluid performance of a parallel heat exchanger module, consisting of a double-finned plate, using basic equations from heat exchanger theory.

- Evaluated the performance of double-finned polymer heat exchanger modules, from un-enhanced (k=0.25W/m.K) through thermally enhanced polymer (k=20W/mK), and compared their performances to the thermal performance of an aluminum module (k=150W/mK) over a range of liquid velocities from 0.5 m/s to 0.5 m/s.  In the parametric range studied, the results are as follows:

  - At maximum flow velocities, thermal conductivities of 0.25 W/m.K and 20 W/m.K yield 86% and 36% degradation, respectively, relative to the thermal performance of aluminum (168 W/m.K).

  - The addition of fins to the un-enhanced, low conductivity polymer produces an adverse effect on performance, while for higher conductivities (~20 W/m.K) the addition of fins to the plates leads to an improvement in thermal performance.

  - Least-material optimization can be used to improve the thermal performance of a double-finned polymer heat exchanger module, when the thermal conductivity is in the range of 20 W/m.K.  If the conductivity is substantially lower, no benefit is derived from such an optimization.

  - COP thermal performance findings for low-k polymer (0.25 W/m.K), high-k polymer (20 W/m.k), and aluminum alloy (168 W/m.K) are illustrated in Figure 3.

| (a) Low-k polymer (0.25 W/m.K), | (b) High-k polymer (20 W/m.k) |
| --- | --- |
| Note: Hot fluid velocity = 0.5 m/s |
| (c) Aluminum alloy (168 W/m.K) |
| Figure 3. COP of a double-finned polymer heat exchanger module as function of thermal conductivity, fin thickness and cold fluid velocity. |

4.	Difficulties Encountered/Overcome

- Material property information and other technical data for the thermally conductive polymers are often proprietary and not generally disclosed. An accumulated database of reported properties is helping to overcome this limitation.

5.	Planned Project Activities for the Next Quarter

- Continue literature review on (i) the strengths and weaknesses of various commercially available heat exchanger designs and (ii) current usage of polymer heat exchangers.

- Continue assessment of the theoretical performance limit of polymer candidate materials and configuration(s).

- Characterize the thermal conductivity of the polymer nanocomposite materials developed so far.

- Construct laboratory-scale test apparatus for thermal characterization of polymer heat exchanger “building block” tube/channels and characterize thermal properties

- Mr. Juan Cevallos, UMD graduate student, will work at PI from June 19 to July 20 on the following tasks:

  - Prepare a forthcoming publication relating to the research undertaken to date on the HX project.

  - Help design and construct a pilot-scale test facility for characterizing polymer heat exchanger thermal performance.

  - Visit ADNOC facilities to obtain insight into existing heat exchanger designs and their potential for replacement with thermally enhanced polymer-based designs.

6.	Appendix

6.1	Justification and Background

High thermal-conductivity polymer heat exchangers could play an important role in seawater-based cooling systems for the power industry, naval applications, and coastal petroleum refineries. Such advanced heat exchangers could facilitate the more direct use of seawater in these applications, while providing reduced weight, greater resistance to corrosion and fouling, reduced energy consumption, and greater geometric flexibility and ease of manufacturing, relative to the technology in use today.

While conventional metal heat exchangers are generally incapable of providing reliable long-term service with salt water (and other corrosive fluids), to date the cost, complexity, and the restricted availability of exotic corrosion-resistant materials have limited the design and application of seawater heat exchangers.

Compact, high performance heat exchangers fabricated of high thermal-conductivity polymers offer a promising alternative to these exotic materials in refineries and power plants located along the coast, where seawater is the primary coolant.

6.2	Approach

1.	Review the available compact liquid-liquid heat exchanger concepts, e.g., shell-in-tube and plate-coil, and identify their strengths and weaknesses.

2.	Define the relevant heat exchange metrics, e.g., kW/m3 and COP (kW heat/kW pumping, and rank the concepts by these metrics.

3.	Review and tabulate the thermal, chemical, and mechanical properties of thermally enhanced polymer materials suitable for use in liquid-to-liquid heat exchangers.

4.	Apply the selected metrics to conventional polymer and thermally enhanced polymer heat exchangers, and re-rank the heat exchanger concepts.

5.	Develop new polymer nanocomposite materials and compare their thermal, chemical, and mechanical properties to the best-known thermally enhanced polymeric materials.

6.	Select the most promising polymer materials and configuration(s) for seawater heat exchange and determine the theoretical performance limits for these configurations/materials.

7.	Fabricate and test polymer tube/channel heat exchanger “building blocks” to determine the pressure drop and heat transfer coefficients achievable.

8.	Correlate baseline thermofluid data for “building block” tube/channels and compare to theoretical predictions.

9.	Develop a test loop for testing of pilot scale polymer heat exchangers, representative of industrial applications.

10.	Develop recommendations for seawater-cooled, thermally enhanced polymer heat exchangers for specific applications, such as in the power industries, refineries, and aboard ships.

6.3	Two-Year Schedule

Year 1:

- Conduct literature review on: (i) the strengths and weaknesses of various commercially available heat exchanger designs and (ii) current usage of polymer heat exchangers.

- Assess the thermal, chemical, and mechanical properties of thermally-enhanced polymer materials suitable for use in liquid-to-liquid heat exchangers.

- Assess theoretical performance limit of polymer candidate materials and configuration(s).

- Construct laboratory-scale test apparatus for thermal characterization of polymer heat exchanger “building block” tube/channels.

- Fabricate polymer nanocomposite materials suitable for polymer heat exchangers.

- Characterize thermal properties of polymer “building block” tube/channel heat exchanger test vehicles.

- Correlate baseline thermofluid data for “building block” tube/channel with theoretical predictions.

Year 2:

- Construct a test loop for thermal characterization of pilot scale polymer heat exchangers representative of industrial applications.

- Characterize thermal properties of pilot-scale polymer heat exchangers.

- Recommend seawater-cooled, thermally enhanced polymer heat exchangers for specific applications.

6.4	Key References

1.	Zaheed, L., and Jachuck, R.J.J., 2004, “Review of polymer compact heat exchangers, with special emphasis on a polymer film unit,” Applied Thermal Engineering, Vol. 24, No. 16, pp. 2323-2358.

2.	Bahadur, R., and Bar-Cohen, A., 2005, “Thermal Design and Optimization of Polymer-Based Pin Fin

Natural Convection Heat Sinks,” IEEE Transactions on Components and Packaging Technologies, Volume 28, Issue 2, pp 238-246.

3.	Zweben, C., 2003, “Emerging High-Volume Commercial Applications for Thermally Conductive Carbon Fibers,” Sixth International Business Conference on The Global Outlook for Carbon Fiber, San Diego, California, USA, November 5 – 7.

4. 	Tsuji, H., Gupta, A. K., Hasegawa, T., Katsuki, M., Kishimoto, K., and Morita, M.: High Temperature Air Combustion: from energy conservation to pollution reduction, CRC Press, Boca Raton, FL, 2003.

Undergraduate Design and Best Educational Practices UMD Investigators: Prof. Linda Schmidt GRA’s: To be assigned PI Investigator(s): Dr. Rocky Kubo Start Date: November 2006 Report Date: 30 June 2007

1.	Objective/Abstract

Dr. Schmidt will partner with PI design faculty to (1) assess existing PI curriculum to profile the design content and (2) compare the design content level to that of a top-ranked, ABET-accredited, US institution; and, (3) prepare design modules and recommend their selected placement within existing PI courses.

The ultimate goal in Year 2 is to create a semester-long project design course that challenges student teams in the same manner as the Mechanical Engineering Senior Capstone Design Experience. Two different design projects will be selected for up to four PI design teams. The PI Design Course Instructor will manage the PI teams, with Dr. Schmidt serving as a consultant and a final project referee. The projects will be the design of mechanical devices to meet a current petroleum engineering challenge.  That is, PI students will have actual customers to consult with at their site. The UM teams will use existing web-based asynchronous communication tools to interact with the same customers served by students at PI.  The PI students (who will be further ahead in the projects) will assist UM students in this communication.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

- Dr. Schmidt’s visit to PI to describe Capstone Design Course

- Dr. Schmidt’s visit PI’s women’s campus

3.	Summary of Project Activities for the Completed Quarter

  - Dr. Kubo allocated a half-day of his April 27th visit to meet with Dr. Schmidt

  - Dr. Kubo’s activities:

    - Reviewed UM Capstone Design Course materials with Dr. Schmidt

    - Attended a course lecture on prototyping projects

    - Attended a lab section for presentation of 3-team progress reports covering design of key project subsystems

    - Toured DesignME Lab facilities (including prototyping equipment) with current Capstone Design Student

4.	Difficulties Encountered/Overcome

Dr. Schmidt’s visit to PI was cancelled due to her involvement in an automobile accident on March 11, 2007.  Her back injury prohibited travel for the planned visit. Dr. Schmidt is currently undergoing physical therapy. The prognosis is good and Dr. Schmidt should be able to resume her normal work schedule in mid- July

5.	Planned Project Activities for the Next Quarter

- Dr. Kubo and Dr. Schmidt will schedule Schmidt visit to PI for capstone design planning for Year Two

- Dr. Schmidt will visit PI’s women’s campus and provide feedback to PI personnel

6.	Appendix

6.1	Justification and Background

6.2	Approach

- Compare the following design aspects: a. Design experience prior to capstone b. Design methods to which students are exposed prior to capstone course. c. Level of original design content expected in projects. d. Constraints of typical projects. e. Degree of student team interaction with mentors f. Evaluation criteria and practices in place.

- Determine the design course content that can be used to enrich each institution’s courses. This will include material from the best prior projects and course examples.

- Identify challenges in collaboration on teams due to differences in institutions and project types.

- Plan a phased faculty interaction in design course at partner institution to prepare for collaborative team-work.

- Identify projects that could be done at both institutions to ascertain the difference in student approaches.

- Plan collaborative projects that would be done by teams of students spanning both institutions.

6.3	Two-Year Schedule

Year 1:

- Exchange senior design course syllabi and sample projects for comparison purposes.

- Site visit by Prof. Schmidt in March 2007 in conjunction with Participation in METSMaC 2007: “Active Teaching, Active Learning”, March 17-19, 2007.

- Participate in partner design course evaluation at the level of reviewing printed deliverables.

- Plan more complete phased participation.

Year 2:

- In Year 2, the team will make broader comparisons of curriculum design content to expectations of ADNOC employers (as this the group that will be employing most PI grads) and produce refined design modules.

- Implement a team collaboration capstone design project.

6.4	Key References

Waste Heat Utilization in the Petroleum Industry UMD Investigators: Professor Reinhard Radermacher, Dr. Yunho Hwang GRA’s: Paul Kalinowski, Cara Martin PI Investigator(s): Dr. Saleh Al Hashimi, Dr. Peter Rodgers, Mr. Amir H. Mortazavi Start Date: 1 December 2006 Report Date: 30 June 2007

1.	Objective/Abstract

Utilize waste heat to minimize overall energy consumption.

2.	Milestones/Deliverables Scheduled for the Completed Quarter

- Report assessment of WH sources and utility requirements

- Model thermal systems that serve as waste heat sources and/or users

3.	Summary of Project Activities for the Completed Quarter

(As related to stated deliverables in #2.  Include findings, accomplishments, figures, and/or schedule changes in this section.)

In this section preliminary waste heat analysis is presented for the ADNOC plants at ASAB and ADGAS.

3.1 ASAB plant

The propane chillers, the gas turbine, and a single-stage ammonia-water absorption refrigeration unit (ARU) were modeled to analyze the potential application of a waste-heat powered ARU instead of conventional propane refrigeration. The engineering equation solver (EES) software was used for modeling.

3.1.1 Propane Chiller Models

The propane chillers were modeled to determine the cooling load required for the NGL recovery at the gas plant. Figure 10 shows the schematic of the conventional refrigeration system at the gas plant.

Figure 10. Schematic of the conventional propane refrigeration at the gas plant

The following assumptions were made for the chiller models:

- Compressor power input: 1 MW

- Compressor efficiency: 60 %

- Heat rejection temperature: 50 °C

- Saturated vapor at the compressor inlet

- Saturated liquid at the condenser outlet

Pressures at the compressor outlets were taken from Figure 10.

Figure 11 and Figure 12 show p-h diagrams and state points for the first and second chilldowns, respectively. All major results for the chillers are summarized in Table 2.

|  | State points 1 – Compressor inlet 2 – Condenser inlet 3 – Condenser outlet 4 – Evaporator (chiller) outlet |
| --- | --- |

Figure 11: P-h diagram and state points for the first chilldown.

|  | State points 1 – Compressor inlet 2 – Condenser inlet 3 – Condenser outlet 4 – Evaporator (chiller) outlet |
| --- | --- |

Figure 12. P-h diagram and state points for the second chilldown

Table 2. Major results for the propane chiller models

|  | 1st Chilldown | 2nd Chilldown |
| --- | --- | --- |
| Propane flow rate | 15.45 kg/s | 4.49 kg/s |
| Cooling capacity | 3,921 kW | 847 kW |
| COP | 3.921 | 0.8474 |

3.1.2 Gas Turbine Model

The 9 MWe gas turbine was modeled to determine the amount of waste heat and the air mass flow rate. The irreversible (real) air-standard analysis was used to study the gas turbine. Two assumptions were made: (1) the working fluid is air, which behaves as an ideal gas, and (2) heat transfer from an external source, rather than combustion, produces the temperature rises.

The initial conditions (15 °C at 1.013) were set according to the ASME Performance Test Code on Gas Turbines (ASME PTC 22).  The pressure ratio, the turbine inlet temperature, and exhaust temperature were taken from the manufacture’s (GHH Borsig Turbomaschinen GmbH) data sheet of the gas turbine THM 1304-D, which produces 8,963 kWe (~9 MWe) [3]. The compressor efficiency was assumed to be 85%. The generator and gear box efficiencies were taken from the MAN TURBO’s data sheets [4]. Table 2 summarizes the assumption for the model.

Table 3. Assumptions for the gas turbine model

| Pressure ratio | 10 |
| --- | --- |
| Turbine inlet temperature | 975 °C |
| Exhaust temperature | 508 °C |
| Isentropic compressor efficiency | 85 % |
| Generator efficiency | 97.5 % |
| Gear box efficiency | 98.5 % |

|  | State points 1 – Compressor inlet 2 – Compressor outlet 3 – Turbine inlet 4 – Turbine outlet |
| --- | --- |

Figure 13. T-s diagram and state points of the gas turbine model

Table 4. Major results of the gas turbine model

| Cycle thermal efficiency | 29.56 % |
| --- | --- |
| Air mass flow rate (ambient) | 17.58 kg/s |
| Volume flow rate (ambient) | 14.35 m3/s |
| Added heat | 12,803 kW |
| Rejected heat | 9,019 kW |

    - Single-Stage Ammonia-Water Refrigeration Cycle Model

Two single-stage ammonia-water absorption cycles were used to investigate the potential application of the ARU (

Figure 14). The following assumptions were made for the models:

- No pressure changes except through the expansion valves and the pumps

- Expansion valves are adiabatic (hin = hout)

- Pumps are isentropic (sin = sout)

- Heat losses to the surrounding are negligible

- Saturated liquid at the outlet of the condensers, the absorbers, and generators

- Saturated vapor at the rectifier outlet

Figure 14. Single-stage ammonia-water absorption refrigeration cycles

The evaporator outlet temperatures were taken from Figure 10. The condenser and absorber outlet temperatures are 50 °C. The effectiveness of the solution and refrigerant heat exchangers is 80%. The isentropic efficiency of the pumps is 85%. The vapor concentration at the rectifier outlets is 0.999. The absorbers have 10% concentration change. The mass flow rate of the weak ammonia-water solution was changed until the cooling capacity of the evaporators accomplished higher cooling loads than those calculated in the chiller models. The major results of the single-stage ammonia-water absorption refrigeration cycles are summarized in Table 5.

Table 5. Major results for the single-stage absorption refrigeration models

|  | 1st Chilldown | 2nd Chilldown |
| --- | --- | --- |
| Cooling Capacity | 3932 kW at 18 °C | 873 kW at - 42 °C |
| Solution Flow Rate | 20.2 kg/s | 7.5 kg/s |
| COP | 0.634 | 0.212 |
| Max. Pressure | 2035 kPa | 2035 kPa |
| COPsystem | 0.466 |

The exhaust from the gas turbine is cooled down from 508 °C to 400 °C in the second generator and then from 400 °C to 232 °C in the first generator.

    - Conclusions

At least one of the compressors can be replaced by an absorption system using waste heat from the gas turbine providing power to the plant.

The power consumption of the gas plant can be reduced by 1.75 MWe.

  - ADGAS plant

To quantify the amount of waste heat and find suitable systems for recovering it, the MS5001 gas turbine and single-stage water/lithium bromide absorption cycle are modeled in this section.

3.2.1 MS5001 gas turbine model

The operation of the MS5001 gas turbine was modeled to estimate waste heat quantities at both design and partial load conditions, for a range of ambient temperatures. Analysis assumptions are:

- Air is the working fluid with air-side pressure drop neglected.

- The combustion process is modeled by transferring heat from an external source.

To compare the results with the manufacture’s performance data [5], ambient temperature and pressure are set to 16 0C and 1 atm, respectively. These levels are not representative of current operating conditions, but will suffice for comparison purposes. Compressor pressure ratio, turbine inlet temperature, and air mass flow rate are given in Table 5.

Table 5. Gas turbine modeling assumptions.

| Pressure ratio [5] | 10.5 |
| --- | --- |
| Turbine inlet temperature [5] | 943 °C |
| Compressor isentropic efficiency | 82 % |
| Turbine isentropic efficiency | 85 % |
| Air mass flow [5] | 425000 kg/hr |

A schematic diagram of the gas turbine model is shown in Figure 6, with the corresponding T-s diagram shown in Figure 7.

Figure 6.  Schematic diagram of the gas turbine.

State points

1 – Compressor inlet

2 – Compressor outlet

3 – Turbine inlet

4 – Turbine outlet

Figure7. T-s diagram and state points of the gas turbine model.

Gas turbine modeling results and corresponding vendor performance data are given in Table 6.

Table 6. Gas turbine modeling results and corresponding vendor performance data.

| Variable | Result |
| --- | --- |
|  | Vendor [5] | Model |
| Cycle thermal efficiency | 28.1 % | 28.12 % |
| Air mass flow rate (ambient) | 17.58 kg/s | 17.58 kg/s |
| Volume flow rate (ambient) | 118.1 m3/s | 118.1 m3/s |
| Mechanical output power | 24600 kW | 22199 kW |
| Input energy | 87477.8 kW | 78935 kW |
| Exhaust temperature | 484 0C | 479.2 0C |

By comparing modeling data with corresponding vendor performance data [5], it is observed that the efficiency and exhaust temperature are within 1%, and mechanical power output and input energy are within 10% of vendor performance data. The discrepancy for the latter two variables may be related to the simplifying assumption of the combustion process. It is modeled as a heat addition process; therefore mass flow through the modeled gas turbine is constant, whereas in a real gas turbine the mass flow rates of the compressor and turbine are not equal. The mass flow rate of the actual turbine is greater, owing to the fact that during the combustion process fuel is added to the air.

3.2.2 Single-stage water/lithium bromide absorption cycle model

Here, the H2O / Li-Br absorption is modeled to estimate COP of absorption cycle for the desired condition. The modeling assumptions are as follows:

- System pressure drops are neglected.

- Rich solution leaving the generator is considered to be saturated liquid.

- Lean solution leaving the absorber is considered to be saturated liquid.

- Water vapor temperature leaving the generator is considered to be equal to the lean solution temperature entering the generator.

- Water vapor entering the absorber is considered to be saturated vapor.

A schematic diagram and modeling results of the H2O/Li-Br absorption cycle are shown in Figure 8 and Table 7, respectively.

Figure 8. Schematic diagram of the H2O/Li-Br absorption cycle.

Table 7. Modeling results of the H2O / Li-Br absorption cycle.

| COP | 0.73 |
| --- | --- |
| Evaporator temperature | 10 0C |
| Condenser outlet temperature | 45 0C |
| Absorber outlet temperature | 45 0C |
| Desorber outlet temperature | 94.4 0C |
| Solution concentration at the inlet of absorber | 62% |

Calculated COP is realistic based on the fact that actual H2O/Li-Br absorption systems have COP around 0.7 [2] for the same conditions as modeled. The predicted solution concentration indicates that crystallization will not occur, as it is below the crystallization threshold of 66% for modeled conditions.

4.	Difficulties Encountered/Overcome

Developing an advanced ammonia-water ARU using as few components as possible to reduce manufacturing cost and to increase the overall efficiency of the entire system might be more challenging than expected.

5.	Planned Project Activities for the Next Quarter

The following activities are to be conducted in the next quarter:

- Assessment of waste heat sources

- Assessment of utility needs

- Design CHP systems with specific focus on use in the plant to be selected

- Development of the software to optimize waste heat utilization.

6.	Appendix

6.1	Justification and Background

The petroleum industry is a big energy consumer itself. Using waste heat skillfully meets some of the demands placed on utilities, leading to significant energy savings.

CEEE at the University of Maryland has extensive experience in the design and implementation of integrated CHP (combined cooling heating and power) projects. The faculty at PI has experience in the design and operation of petroleum processing plants. Jointly, the team is excellently suited to address the challenge posed by this project.

6.2	Approach

- Assess waste heat (WH) sources (PI)

- Assess WH conversion processes (UMD)

- Assess utility requirements (PI)

- Match WH sources/processes and utility requirements (PI, UMD)

- Develop/implement of software for system analysis (PI, UMD)

- Rank and propose implementation of 1 or 2 preferred systems (PI, UMD)

- Define additional R&D as needed (PI, UMD)

6.3	Two-Year Schedule

June 1, 2007	Report assessing WH sources and utility requirements

June 1, 2007	WH conversion options report

Oct. 1, 2007	Useful version of software

Apr. 31, 2008	Ranking of systems and selection

Nov. 31, 2008	Report recommended steps forward

6.4	Key References

- Alefeld, Radermacher, Heat Conversion Systems, CRC Press 1994.

- Herold, Radermacher, Klein, Absorption Chillers and Heat Pumps CRC Press 1996.

- Giampaolo, T., 2003, The gas turbine handbook: principles and practices, 2nd edition, The Fairmont Press, Lilburn, GA.

- MAN Turbo AG, THM turbine familily: performance data, 2007, Available at http://www.manturbo.com/en/500/500_brochures.php

- Daiber,P.C, Performance  and Reliability Improvements for the MS5001 Gas Turbines, GER-4196, GE Power Systems, Available at http://www.gepower.com/prod_serv/products/tech_docs/en/gas_turbines.htm

Last access on 06/10/2007.

# Text boxes

x

y

Top View

Perspective Drawing

Top View

Perspective

Drawing

Model IV: 4DOF and 5DOF models

Model  III

Torsional and bending motions of drill string

Models I and II

I: Lateral  Motion & II: Torsional Motion

Fc

Ff

x

y

t

z

u

4

t

k2’

k2

k2’

r

z

u

3

z

L

Z

Z

O

O2

Section I

Section II

mb

X

Y

O

Z

Section II

X

X

Y

O

O2

Y

e

Dc Motor

Upper disc

Lower disc

String

Frame

Springtor

Shell

Actuator

Lateral shaker

Application of static longitudinal force

Application of static longitudinal force during rotation

Application of dynamic longitudinal force during rotation

Two sections with relative displacement

-

Air-Water Mixture

HV Power Supply

Ultrasonic Droplets Generator

Air Flow

Ф 5 cm

L

Metal Tube

(Collector Electrode)

+

Needle

(Discharge Electrode)

Insulator

To

APS

For room air:

CVC is independent of flow rate

- Separator Length 28 cm

- Separator Diameter 5 cm

- Imax 80 µA

- Voltage applied 15 kV

- Voltage applied 15 kV

2

1