Energy Education and Research Collaboration

Third Quarterly Report

July 1, 2007-September 30, 2007

###### Prepared by

Prof. Nariman Farvardin, Provost

Principal Investigator and EERC Project Director

Prof. Avram Bar-Cohen, Chair

EERC Project Deputy Director

Dr. Azar Nazeri

EERC Research Manager

A.J. Clark School of Engineering

University of Maryland, College Park, MD 20742-3035

Prepared for

The Petroleum Institute

Abu Dhabi, United Arab Emirates

September 30, 2007

EERC Key Contributors

##### University of Maryland – College Park, MD, USA

Sami Ainane

Shapour Azarm

Balakumar Balachandran

Avram Bar-Cohen

John Cable

Serguei Dessiatoun

Nariman Farvardin

Ashwani K. Gupta

Ali Haghani

Yunho Hwang

Greg Jackson

Mohammad Modarres

Linda Schmidt

Reinhard Radermacher

##### Petroleum Institute – Abu Dhabi, UAE

Ali Almansoori

Ahmed Abdala

Tareq Al Ameri

Saleh Al Hashimi

Valerie Eveloy

Afshin Goharzadeh

Mansour Karkoub

Rocky Kubo

Michael Ohadi

Peter Rodgers

Mohamed Sassi

Abdennour Seibi

Table of Contents

List of EERC Key Contributors	ii

Executive Summary	1

Introduction	5

Individual Project Reports	10

Fundamentals of Engineering Education	11

S. Ainane (UMD), P. Rodgers (PI)

International Student Exchange Initiative	13

S. Ainane (UMD)

Robust Optimization of Petrochemical Systems	15

S. Azarm (UMD), S. Al Hashimi (PI), T. Al Ameri (PI)

Dynamics and Control of Drill Strings on Fixed and Floating Platforms	23

B. Balachandran (UMD), M. Karkoub (PI), Y. Abdelmagid (PI)

Thermally Enhanced Polymer Heat Exchanger for Seawater Applications	39

A. Bar-Cohen, P. Rodgers, A. Abdala

An EHD-Enhanced Gas/Liquid Separator	47

S. Dessiatoun (UMD), M. Ohadi (PI), A. Goharzadeh (PI)

Force-Fed Cooling of Photovoltaic Arrays for High Efficiency Solar Energy Conversion Systems	53

S. Dessaitoun (UMD) M. Ohadi (UMD)

Study of Condensing Flows in a Micro-scale Channel with a Micro-element Array and Visual Techniques	60

S. Dessiatoun (UMD), A. Shooshtari (UMD), A. Goharzadeh (PI)

Sulfur Recovery from Gas Stream using Flameless and Flame Combustion Reactor	70

Prof. A.K. Gupta (UMD), M. Sassi (PI)

Development and Delivery of Course Material for Engineering Project Management Courses	89

A. Haghani (UMD), J. Cable (UMD)

Solid Oxide Fuel Cells for CO2 Capture and Enhanced Oil Recovery	91

G. Jackson (UMD), S. Dessaitoun (UMD), V. Eveloy (PI), A Almansoori (PI)

Development of a Probabilistic Model for Degradation Effects of Corrosion-Fatigue-Cracking

in Oil and Gas Pipelines

M. Modarres (UMD), A. Seibi (PI)	104

Waste Heat Utilization in the Petroleum Industry	116

R. Radermacher (UMD), Yunho Hwang (UMD), S. Al Hashimi (PI), P. Rodgers (PI)

Undergraduate Design and Best Educational Practices	129

L. Schmidt (UMD), R. Kubo (PI)

Executive Summary

The following is a summary of the major project activities that have taken place over the completed quarter.  For more details, see the individual reports in the last section of this report.

Fundamentals of Engineering Education

S. Ainane (UMD), P. Rodgers (UMD)

Objective: To design a review course to prepare PI students for Fundamentals of Engineering examination; to prepare and grade “practice” Fundamentals of Engineering examination for PI students; and to use the practice exam results to identify the program strengths/weaknesses.

Progress:

- Dr. Ainane and Dr. Rogers initiated discussions with NCEES (National Counsel of Examiners for Engineering and Surveying) and with AMIDEAST (America-Mideast Educational and Training Services, Inc.) to bring the real FE exam to the UAE.

International Student Exchange Initiative

S. Ainane (UMD)

Objective: Strengthen the relationship between the PI and UMD by providing the opportunity for the PI and UMD students to study at each other’s institutions.

Progress:

- Dr. Ainane initiated discussions between Dr. Ohadi and Jane Fines, Director of Special Programs at the A. James Clark School of Engineering. These discussions resulted in the signing of an agreement for a Student Exchange Program between the PI and UMD.

- Dr. Ainane will meet with interested students to provide details of the program during his next visit to the PI.

- UMD will propose that ENES472: International Business Cultures for Engineering & Technology be offered at the PI in Winter 2009 (the course will be offered in Sydney Australia in Winter 2008).   The course, which is required for the minor in International Engineering, will be available to the PI and UMD students.

Robust Optimization of Petrochemical Systems

S. Azarm (UMD), S. Al Hashimi (PI), T. Al Ameri (PI)

Objective: The objective of this study is to develop a framework for robust optimization the design of a distillation column, while considering the net profit effect at the plant level.

Progress:

- Mr. Genzi Li successfully defended his dissertation on July 16, 2007, entitled: “Online and Offline Approximations for Population Based Multi-Objective Optimization.”

- A new GRA, Mr. Wei Wei Hu, joined our group in early August 2007.

- Began to formulate the robust optimization problem.

- Updated the distillation tower model to include two cost functions. However, the optimization results have so far produced no trade-offs between the two cost functions.

- Completed and submitted a joint paper to the Journal of Structural and Multidisciplinary Optimization.

Dynamics and Control of Drill Strings on Fixed and Floating Platforms

B. Balachandran (UMD), M. Karkoub (PI), Y. Abdelmagid (PI)

Objective: To develop and analytically and numerically study control-oriented models for drill strings; to investigate control of an under-actuated nonlinear system (drill string) with complex interactions with the environment; and to build a drill-string testbed at the PI/UMD to test the theoretical findings.

Progress:

- Refined a four degree-of-freedom (DOF) model used to study motions of a drill string when an external torque is applied. Simulation results have also been generated.

- Refining a five degree-of-freedom model. Simulations with an initial five degree-of-freedom model have also been initiated.

- Designed an experiment arrangement with sensors, controls, and other units.

Thermally Enhanced Polymer Heat Exchanger for Seawater Applications

A. Bar-Cohen (UMD), Dr. Peter Rodgers (PI), Dr. Ahmed Abdala (PI)

Objective: To address the fundamental thermal performance issues associated with the use of thermal high-conductivity polymer materials in heat exchangers.

Progress:

- Continued literature review on: (i) the strengths and weaknesses of various commercially available heat exchanger designs and (ii) current usage of polymer heat exchangers.

- Continued assessment of the theoretical performance limit of polymer candidate materials and configuration(s).

- Developed new polymer nano-composite materials.

- Constructed laboratory-scale test apparatus for thermal characterization of polymer heat exchanger “building block” tube/channels, and characterized thermal properties.

- Prepared a forthcoming publication relating to the project research undertaken to date.

- Visited ADNOC facilities to obtain insight into existing heat exchanger designs and their potential for replacement with thermally enhanced polymer-based designs.

An EHD-Enhanced Gas/Liquid Separator

S. Dessiatoun (UMD), M. Ohadi (PI), A. Goharzadeh (PI)

Objective: To study hybrid inertia-EHD gas-liquid separation phenomena for electrically conductive and nonconductive liquid particles suspended in a moving gaseous medium.

Progress:

- Continued literature survey.

- Summarized governing equations and identified non-dimensional parameters.

- Designed an experimental test setup and identified needed components and instruments.

- Developed a numerical methodology to simulate the electric field effect on particle separation.

Force-Fed Cooling of Photovoltaic Arrays for High-Efficiency Solar Energy Conversion Systems

S. Dessaitoun (UMD), M. Ohadi (UMD)

Objective: To create a database on the available cooling techniques for high heat flux solar concentrator arrays necessary for efficient conversion of solar energy to electric power, and to design and fabricate an experimental prototype and associated setup to verify the feasibility of this concept and the capacity for force-fed cooling.

Progress:

- Continued literature survey and prepared a summary.

- Calculated the range of expected heat load needed to be removed by proposed cooling technique.

- Successfully performed a trial round of the microfabrication process to assess feasibility of the procedure.

- Developed a numerical model for microchannel design and determined the optimum design.

Study of Condensing Flows in a Micro-scale Channel with a Micro-element Array and Visual Techniques

S. Dessiatoun (UMD), A. Shooshtari (UMD), A. Goharzadeh (PI)

Objective: To investigate the fundamentals of the two-phase condensing flow phenomenon in a sub-millimeter microchannels.

Progress:

- Continued to conduct experiments based on the test matrix.

- Conducted several visualization tests using mini-laser doppler velocimetery and a high-speed camera.

- Developed an image processing technique to quantitatively characterize the observed states and liquid-bubble interactions.

Sulfur Recovery from Gas Stream using Flameless and Flame Combustion Reactor

Prof. A.K. Gupta (UMD), M. Sassi (PI)

Objective: To obtain fundamental information on the thermal process for sulfur recovery from sour gas by conventional flame combustion and flameless combustion using numerical and experimental studies. The ultimate goal is to determine optimal operating conditions for sulfur conversion.

Progress:

- Determined the equilibrium chemistry using equilibrium code.

- Performed detailed chemistry using chemical kinetics code.

- Performed flow dynamic simulations using Fluent code.

- Presented a technical paper at the 5th Mediterranean Combustion Symposium

Development and Delivery of Course Material for Engineering Project Management Courses

A. Haghani (UMD), J. Cable (UMD)

Objective: To develop and deliver course material for an Engineering Project Management program at PI, develop and deliver a short course for GASCO, and perform a feasibility study of establishing a graduate program in Engineering Project Management at PI.

Progress:

- UMD/PM delivered a draft survey to PI on 24 July 2007.

- PI requested two additional graduate courses from the Project Management Program to be delivered next spring:  ENCE 422 Project Cost Accounting & Economics and ENCE 423 Project Planning, Scheduling and Control.

Solid Oxide Fuel Cells for CO2 Capture and Enhanced Oil Recovery

G. Jackson (UMD), S. Dessaitoun (UMD), V. Eveloy (PI), A. Almansoori (PI)

Objective: This multi-faceted project will investigate the feasibility of implementing advanced solid oxide fuel cell (SOFC) technology for producing power from oil well off-gases while providing a source of concentrated CO2 for sequestration and enhanced oil recovery.

Progress:

- Finalized fabrication protocol for high-power density cells with thin electrolytes and metal-doped CeO2 anodes.

- Completed preliminary UMD studies comparing operation of SOFC’s with syngas and with humidified and dry hydrocarbons (no larger than n-C4H10).

- Completed purchase and acquisition of supplies and equipment for PI SOFC test facility and began assembly of test rig.

- Completed development of hydrocarbon electrochemical models (CeO2 and Ni) and studied optimal anode architectures for hydrocarbons with 1-D through-the-MEA models.

- Developed a down-the-channel model at UMD and began study of SOFC operation with high fuel utilization and various inlet fuel compositions.

- Began development of SOFC and balance of plant models in Aspen or Hisys at PI.

Development of a Probabilistic Model for Degradation Effects of Corrosion-Fatigue-Cracking in Oil and Gas Pipelines

M. Modarres (UMD), A. Seibi (PI)

Objective: To propose and validate a probabilistic model for health management of oil pipelines in process plants.

Progress:

- Approached Professor Wei to act as a consultant for the establishment of the corrosion-fatigue laboratory in the PI.

- Gathering information on the foundation of corrosion and corrosion fatigue.

- Found appropriate generic data to build and run the computer routine Matlab for corrosion fatigue according to Wei’s superposition model.

- Developed simple empirical parametric models estimated from curve fitting of data obtained from the computer simulation.

- PI approved $103K for procuring the corrosion-fatigue equipment for the proposed fatigue-corrosion lab at PI.

- PI designated a space for the corrosion-fatigue lab in the new Takreer Technology Center building scheduled to be completed at end of 2008.

Waste Heat Utilization in the Petroleum Industry

R. Radermacher (UMD), Yunho Hwang (UMD), S. Al Hashimi (PI), P. Rodgers (PI)

Objective: To utilize waste heat in petroleum processing plants to minimize overall energy consumption.

Progress:

- The propane chillers, the gas turbine, and a single-stage ammonia-water absorption refrigeration unit (ARU) were modeled to analyze the potential application of a waste heat powered ARU instead of conventional propane refrigeration.

Undergraduate Design and Best Educational Practices

L. Schmidt (UMD), R. Kubo (PI)

Objective: To partner with PI design faculty to (1) assess existing PI curriculum to profile the design content and (2) compare the design content level to that of a top-ranked, ABET-accredited, US institution; and, (3) prepare design modules and recommend their selected placement within existing PI courses.

Progress:

- Dr. Schmidt was unable to conduct project activities because of an intense course of physical therapy (May through July) arising from her car accident on March 11th and a separate rib injury sustained on UM’s campus on July 6th that required a two-week absence followed by a reduced schedule of activities.

Introduction

In line with its mission to provide world-class education to the citizens of the United Arab Emirates in engineering and the applied sciences, the Petroleum Institute (PI) of Abu Dhabi, UAE, has entered into a long-term collaborative effort with the University of Maryland (UMD) to enhance its own undergraduate, graduate studies/research, and continuing education practices. The PI was founded by Emiri decree in 2001 under the direction of H.H. Sheikh Khalifa bin Zayed Al-Nahyanand.  It is sponsored by a consortium of Abu Dhabi National Oil Company (ADNOC) and its international partners (Shell, BP, Total, and Japan Oil Development Company.

The PI and UMD recognize the many potential benefits for both institutions that could result specifically from collaborative educational and research activities in the field of Energy Sciences and Engineering.  The Energy Education and Research Collaboration (EERC) has been created within the A.J. Clark School of Engineering at the University of Maryland to provide the administrative structure and academic oversight for these collaborative efforts.

During this third quarter of the EERC’s funded effort, partnerships between UMD and PI faculty have been further solidified, and significant progress has been made on the collaborative research projects.

EERC New Research Manager

In July 2007 Dr. Azar Nazeri joined the Mechanical Engineering department as the Research Manager for the EERC.  Dr. Nazeri has over 17 years of basic science research and program management experience at the corporate laboratory of the United States Navy, Naval Research Laboratory. In her position as EERC Research Manager, Dr. Nazeri will coordinate collaborative activities between PI and UMD faculty, students, and staff.  It is hoped that her experience and leadership will ensure closer collaboration between PI and UMD. Dr. Nazeri has a B.S. Degree in Mechanical Engineering and earned a Ph.D. in Materials Science and Engineering from UCLA in 1989.

Collaborative Activities

Progress made on the EERC research projects during the third quarter of activity is summarized below:

In this quarter, there has been steady progress on the majority of the 13 projects as evident from individual reports, while some projects have encountered challenges. UMD/PI collaborators in the Fuel Cell project have been working hard to resolve a few issues through continuous correspondence and conference calls, which intensified in the month of September. Unfortunately, the outcome of this process was not to the satisfaction of both sides and therefore this quarterly report reflects only the efforts of the UMD side. It has been agreed by the PI and UMD that the efforts of both sides will be reflected in the next quarterly report.

The other project facing problems has been the Undergraduate Design project. As explained in this quarter's report, the problem has been due to a few consecutive unfortunate events that have resulted in serious health problems for Professor Linda Schmidt, which have rendered her unable to perform her duties. At this point Professor Schmidt has fully recovered and is ready to embark on this activity.  However, it has been concluded that the framework of the program needs to be revised.  More discussion between the PI & UMD is needed to finalize the scope and details of such plans. Needless to say, Professor Schmidt has not withdrawn any funding from EERC during this period.

On the positive side, a new initiative for an exchange student program between PI and UMD has established an official Student Exchange Program. Last but definitely not least, this quarter our collaboration has produced two joint publications and one presentation in international journals and conferences.

I.  Collaborative research projects

Each research project is reported in detail in the next section.

II.  	EERC faculty and graduate student visits

Face-to-face meetings have continued to prove useful to the various projects.  Visits this quarter included:

- Juan Cevallos to PI from June 19 – July 20.  He and Peter Rodgers attended a one-day information session run by Dr. Nashaat M. Mohamed of ADGAS, who provided an extensive overview of the seawater-cooled systems used at the Das Island gas liquification plant.

- Dr. Afshin Goharzadeh and Dr. Ali Almansoori to UMD.  Their detailed trip reports are included in their project reports.

III.	Joint monthly meetings via video-conference

Joint monthly meetings have continued as an effective means for faculty members to present their research to the entire group. The last video-conference (VC) was conducted on September 11, 2007, and was chaired by Dr. Azar Nazeri, EERC Research Manager. This was the only VC in this quarter due to summer vacations at PI & UMD. The agenda of the meeting was as follows:

| Time | Presentation | Presenter |
| --- | --- | --- |
| 09:00 | Welcome/Introduction–UMD | Dr. Bar Cohen |
| 09:05 | Welcome–PI | Dr. Ohadi |
| 09:10 | Welcome/announcements/introduction of students | Dr. Azar Nazeri |
| 09:15 | Condensing Flows in Micro-Scale Channels, PI Investigator Dr. Goharzadeh | Ebrahim Al-Hajri |
| 09:30 | Visualization Techniques/Recent Visit to UMD | Dr. Goharzadeh |
| 09:45 | FE Exam & Student Exchange | Dr. Sami Ainane |
| 09:55 | Wrap Up | Dr. Nazeri/Dr. Bar Cohen |

Twenty-three members of the faculty and graduate students at UMD attended this VC. All of the students had a chance to introduce themselves and their affiliated projects. A constructive discussion ensued after the VC between PI & UMD on how to improve the quality of this important interaction. It was agreed by both sides that to overcome the IT issues of the conference, one IT person should be assigned to the task during the conference at PI to assure the readiness of the setup and to address the technical issues that can easily arise.

IV.	PI Distance Learning Students

The table below shows a list of graduate students currently working on EERC projects, their advisors at UMD, and PI collaborating faculty.  The table also includes the degrees sought and the students’ funding source.

| UMD Professor | PI Professor | Student | Degree | Funding Source |
| --- | --- | --- | --- | --- |
| Modarres | Seibi (TCM) | Mohamed Chooka | Ph.D. | ADNOC |
|  |  | Mohamed Nefati | Ph.D. | EERC |
| Balachandran | Karkoub (TCM)*, Abdelmagid | Chien-Min Liao | Ph.D. | EERC |
| Dessiatoun | Ohadi, Goharzadeh, Kubo | Mohamed Alshehhi | Ph.D. | ADNOC |
|  |  | Ebrahim Al-Hajri | Ph.D. | ADNOC |
|  |  | Elnaz Kermani | M.S. | EERC |
| Azarm | Al Hashimi, Al Ameri | Genzi Li | Ph.D. (graduated 8/2007) |  |
|  |  | Wei Wei Hu | Ph.D. | EERC |
| Gupta | Sassi | Hatem Selim | Ph.D. | EERC |
| Bar-Cohen | Rogers, Abdala | Juan Cevallos | M.S. | EERC |
|  |  | Patrick Luckow | M.S. | EERC |
| Radermacher | Al Hashimi, Rodgers, Mortazavi | Ali Alalili | Ph.D. | ADNOC |
|  |  | Ahmed Alshehhi | M.S. | ADNOC |
|  |  | Chris Somers | M.S. | ADNOC |
|  |  | Paul Kalinowski | M.S. (graduated 9/2007) | Mannheim, Germany |
| Schmidt | Kubo | Ramzi Alsaari | Ph.D. | ADNOC |
| Jackson | Eveloy (TCM), Almansoori (TCM)* | Paul Jawlik | M.S. | EERC |
|  |  | Siddharth Patel | M.S. | EERC |

* = To be assigned

TCM = Thesis Committee Member

CA = Co-advisor

- At this point there are nine Ph.D. students and seven M.S. students at UMD.

- The Ph.D. student of Dr. Shapour Azarm, Genzi Li, graduated in August with a Ph.D. under the support of EERC.

- Paul Kalinowski, an exchange student at UMD who worked with Dr. Radermacher on Waste Heat Utilization at the PI, received his master’s degree from the University for Applied Sciences in Mannheim, Germany.

- Seven of the total sixteen students are supported by ADNOC and the rest by EERC.

- Many faculty members at UMD have started the process of assigning PI faculty as either Co-Advisors (CA) or Thesis Committee Members (TCM) for their students. It is our hope that this process will be completed in the fourth quarter.

- Dr. Abdennour Seibi has been officially assigned as a Thesis Committee Member (TCM) for Mohamed Chooka’s Ph.D. thesis committee. He is Dr. Mohammad Modarres’s student.

- Dr. Valerie Eveloy is the TCM for Paul Jawlik’s M.S. thesis. Paul Jawlik is Dr. Greg Jackson’s student.

V.	International Exchange Student Initiative

To further strengthen the collaboration between PI and UMD, a new initiative by Dr. Ainane will provide the opportunity for both PI and UMD students to study at each other’s institutions.

There are already several programs available for Engineering students at UMD to study abroad during their college careers. At present, students can study or work abroad in many countries around the world including Europe, Asia, Australia, and North and South America. Through this new initiative, which resulted in signing an agreement between PI and UMD for an official Student Exchange Program, PI will be added to the list of destinations for UMD students. Likewise, PI students will have the opportunity to study for a semester or two at UMD. This program will be advertised at UMD and PI, and Dr. Ainane will meet with interested students at PI during his next visit to PI (November 2007).

UMD will also propose that ENES472: International Business Cultures for Engineering & Technology be  offered at the PI in Winter 2009 (the course will be offered in Sydney Australia in Winter 2008).  This course, which is required for the minor in International Engineering, will be available to PI and UMD students.

Collaborative Publications and Presentations

The collaboration has thus far produced two publications and one presentation, listed below.

Publications

1. 	Li, G., M. Li, S. Azarm, N. Al Qasas, T. Al Ameri, and S. Al Hashimi, “Improving Multi-Objective Genetic Algorithms with Adaptive Design of Experiments and Online Metamodeling,” Structural and Multidisciplinary Optimization (submitted).

2.	Sassi, M., and Gupta, A. K., “Sulfur Recovery from Acid Gas Using the Claus Process and High Temperature Air Combustion (HiTAC) Technology,” Special Issue of the American Journal of Environmental Sciences, March 2007 (submitted).

Presentations

1.	Sassi, M., BenRejab, S., and Gupta, A. K., “CFD Simulation of Combustion in the Claus Furnace of a Sulfur Recovery Plant,” 5th Mediterranean Combustion Symposium (MCS-5), Monastir, Tunisia, September 9-13, 2007.

Quarterly Report Schedule

Because the first quarterly period expanded to fill nearly five months, an adjusted quarterly schedule is now in place.  UMD will provide quarterly reports to the PI on the following dates:

| Quarter 2 | June 30, 2007 |
| --- | --- |
| Quarter 3 | September 30, 2007 |
| Quarter 4 | December 15, 2007 |
| Quarter 5 | February 29, 2008 |
| Quarter 6 | May 15, 2008 |
| Quarter 7 | July 31, 2008 |
| Quarter 8 | October 31, 2008 |

Individual Progress Reports

Fundamentals of Engineering (FE) Examination UMD Investigators: Dr. Sami Ainane PI Investigator: Dr. Peter Rodgers Start Date: June 2006 Report Date: 30 September 2007

1.	Objective

- Design a review course to prepare PI students for the Fundamentals of Engineering Examination (FE Exam).

- Prepare and grade “practice” FE Exam for PI students.

- Use the practice FE Exam results to identify engineering program strengths/weaknesses.

- Determine whether an official NCEES FE Exam can be undertaken at the PI.

2.	Deliverables

- Update FE Exam tutorial material for PI student use.

- Develop new FE Exam to be administered to PI senior students on December 1, 2007, with discipline-specific afternoon tests in chemical, electrical and mechanical engineering.

3.	Summary

## Dr. Ainane and Dr. Rogers have continued discussions with NCEES (National Counsel of Examiners for Engineering and Surveying) and with AMIDEAST (America-Mideast Educational and Training Services, Inc.) to bring the real FE exam to the UAE.

## It was decided to rerun the FE Exam in quarter four for all PI senior students graduating at the end of this semester, with the retake exam scheduled for December 1.  Twenty-six students will retake the exam, having all previously taken it in spring 2007.

## To prepare the students for this exam, nine tutorial revision sessions will be offered, having a total of 24 contact hours, and will cover Mathematics (3 hours), Probability and Statistics (3 hours), Chemistry (3 hours), Statics/Dynamics (3 hours), Mechanics of Materials/Material Science (3 hours), Electric Circuits (3 hours), Economics (2 hours), Thermodynamics (2 hours), and Fluid Mechanics (2 hours).

## Dr Ainane will be at PI from November 18 – 24 and will give six of these tutorials.

- FE exam will take place on December 1, with discipline-specific afternoon tests in chemical, electrical and mechanical and engineering offered.

4.	Difficulties Encountered/Overcome

- PI student attendance for the FE Exam review sessions conducted in Spring 2007 was low.

- Even though a monetary award was offered to PI students who passed the FE exam [Grade A ($2,725), Passing grade ($1,362)], the majority of the students did not appear willing to put in the effort to pass the practice FE Exam.

- By offering discipline-specific afternoon tests in chemical, electrical and mechanical engineering, it is believed that the PI students, especially non-ME majors, will be more motivated in passing the FE Exam.

5.	Deliverables for the Next Quarter

- Dr. Ainane will conduct six FE Exam tutorial review sessions at the PI from November 18 – 24.

- Rerun of FE exam will take place at PI on December 1, with discipline-specific afternoon tests in chemical, electrical and mechanical and engineering offered.

- PI will continue discussions with AMIDEAST to determine whether an official NCEES FE Exam can be undertaken at the institute.

Appendix

Justification and Background

The National Council of Examiners for Engineering and Surveying (NCEES), which is the official body that administers the FE exam, has detailed statistics on the results for examinees who undertake the FE exam and have attended EAC/ABET-accredited college/university engineering programs.

Apart from the FE exam process serving as a possible academic assessment metric at PI, ADNOC wishes to explore the possibility of introducing professional engineering (PE) licensing within its operations.  The starting point for such a licensing process is the passing of the FE exam.

Approach

Tutorial sessions are developed to prepare PI students for undertaking trial FE exam, which covers the following topics:

- Mathematics, probability and statistics

- Statics, dynamics, strength of materials and materials science

- Thermodynamics and fluid mechanics

- Electrical circuits and computers

- Engineering economics

- Chemistry

- Ethics and business practices

This material is reviewed in 43 hours of tutorials, given in three hour sessions. The revision materials are primarily supplied by UMD, supplemented by PI faculty input.

Two-Year Schedule

Year 1:

- Design review course to prepare PI students for Fundamentals of Engineering examination.

- Prepare and grade “practice” Fundamentals of Engineering examination for PI students.

- Establish if an official NCEES FE Exam can be undertaken at PI in 2008.

Year 2:

- Modify and revise review course to prepare PI students for Fundamentals of Engineering examination based on Year I experience.

- Prepare and grade “practice” Fundamentals of Engineering examination for PI students.

Key References

An overview of the FE exam process can be obtained at http://www.ncees.org, which is the official website for The National Council of Examiners for Engineering and Surveying (NCEES), which administers the FE exam.

International Student Exchange Program UMD Investigators: Dr. Sami Ainane PI Investigator: Start Date: September 2007 Report Date: 30 September 2007

1.	Objective

Strengthen the relationship between the PI and UMD by providing the opportunity for the PI and UMD students to study at each other’s institutions.

2.	Milestones/Deliverables

- Number of students from the PI and UMD who will enroll in the program

3.	Summary

Dr. Ainane initiated discussions between Dr. Ohadi and Jane Fines, Director of Special Programs at the A. James Clark School of Engineering. These discussions resulted in the signing of an agreement for a Student Exchange Program between the PI and UMD.

4.	Difficulties Encountered/Overcome

None.

5.	Deliverables for the Next Quarter

- The program will be advertised at UMD.

- Dr. Ainane will meet with interested students to provide details of the program during his next visit to the PI.

- UMD will propose that ENES472: International Business Cultures for Engineering & Technology be   offered at the PI in Winter 2009 (the course will be offered in Sydney Australia in Winter 2008).   The course, which is required for the minor in International Engineering, will be available to the PI and UMD students.

Appendix

Justification and Background

The University of Maryland currently sponsors programs in France, England, Australia, Spain, Germany, Denmark, and The Netherlands. In addition, UM has exchange agreements with a number of overseas universities.  Students are directly enrolled as full-time students at the host institution of their choice. Exchange students are expected to be independent and interested in a true immersion experience during their semester abroad.

Exchange Programs offer a wonderful opportunity to study abroad independently and to assimilate into the culture. On a traditional exchange, students pay tuition at their home institution and swap places with a student overseas.

The Clark School of Engineering also offers a  “Minor in International Engineering.” This requires 15-20 credits depending on the combination of 3 and 4 credit courses a student might choose to complete.

    - International Business Cultures for Engineering & Technology (ENES472/SLLC472)

    - An engineering study, work or research experience abroad.

    - Foreign language, culture studies, internationally-related studies or international engineering-related courses.

Approach

Key References

Information on the UMD and A. James Clark school of Engineering International Programs is available at :http://www.international.umd.edu/studyabroad/ and http://www.ursp.umd.edu/international/index.html

Robust Optimization of Petrochemical Systems UMD Investigator: Dr. Shapour Azarm PI Investigators: Dr. Saleh Al Hashimi and Dr. Tareq Al Ameri UMD’s GRA: Mr. Genzi Li (Graduated with Ph.D. in Summer 2007); PI’s GRA: Ms. Naveen Al Qasas Start Date: October 2006 Report Date: 30 September 2007

1.	Objective/Abstract

The objective of this study is to develop a framework for robust optimization the design of a distillation column, while considering the net profit effect at the plant level. The investigation will mainly focus on engineering decisions but will also consider the effects of these decisions on business objectives while maintaining the required product specifications. The investigation will also explore tradeoffs between engineering objectives versus expected profit and other business goals when there is uncertainty.

2.	Deliverables

- Perform robust optimization with interval uncertainty.

- Update distillation tower model, i.e., cost model, and subsequently the optimization.

- Complete the joint journal paper on the new MOGA with distillation column design optimization

3.	Summary

- Mr. Genzi Li successfully defended his dissertation on July 16, 2007, entitled: “Online and Offline Approximations for Population Based Multi-Objective Optimization.” Mr. Li left the US on August 10, 2007, for China to work in a manufacturing firm in Bejing, China.

- A new GRA, Mr. Wei Wei Hu, joined our group in early August 2007.

- We began to formulate the robust optimization problem.

- We updated the distillation tower model to include two cost functions. However, the optimization results have so far produced no trade-offs between the two cost functions.

- We completed and submitted a joint paper to the journal of Structural and Multidisciplinary Optimization, i.e.,

Li, G., M. Li, S. Azarm, N. Al Qasas, T. Al Ameri, and S. Al Hashimi, “Improving Multi-Objective Genetic Algorithms with Adaptive Design of Experiments and Online Metamodeling,” Structural and Multidisciplinary Optimization (submitted).

Select portions of this paper are given in the following.

Abstract:

Applications of Multi-Objective Genetic Algorithms (MOGAs) in engineering optimization problems often require numerous function calls. One way to reduce the number of function calls is to use approximation. An approximation involves two steps: Design of Experiments (DOE) and metamodeling. This paper presents a new approach where both DOE and metamodeling are integrated with a MOGA. In particular, the DOE method reduces the number of generations in a MOGA, while the metamodeling reduces the number of function calls in each generation. In the present approach, the DOE locates a subset of design points that is estimated to better sample the design space, while the metamodeling assists in estimating the fitness of design points. Several numerical and engineering examples are used to demonstrate the applicability of this new approach. The results from these examples show that the proposed improved approach requires significantly fewer function calls and obtains similar solutions compared to a conventional MOGA and a recently developed metamodeling-assisted MOGA.

4.1. Distillation Column Design Example

Distillation columns (or towers) are commonly used in the chemical process industries to separate a mixture of two or more chemicals based on the difference in their volatilities. A simplified scheme of a binary distillation tower is given in Figure 6.

The symbols used in Figure 6 are defined as follows: D and B are the flow rates of the distillate and bottom products respectively; F is the feed flow rate per unit time and is fixed (100 mol/hour); L is the liquid reflux flow rate sent back to the column from the condenser to improve the overall separation power of the unit; N1 is the number of stages in the rectifying section (upper section, above the feed plate); N2 is the number of stages in the stripping section (bottom section, below the feed plate); P is the pressure of the column, which is fixed (1 atm); R is the reflux ratio defined as L/D; T is the temperature of the feed stream and is assumed to be fixed (30(C); V is the vapor flow rate of the stream leaving the partial boiler and entering the bottom of the column; VB is the vapor boil-up ratio defined as V/B; XB is the composition of the more volatile component, benzene, in stream B; XD is the composition of the more volatile component in stream D; and XF is the mole fraction of the more volatile component, benzene, in the feed, which is fixed (0.45). The concentrations of the liquid and vapor leaving the trays within the column (refer to Fig 6) are defined as follows for each tray N in the column. XN is the mole fraction of the more volatile component, benzene, in the liquid leaving tray N; and YN is the mole fraction of more volatile component, benzene, in the vapor leaving tray N.

Figure 6. Binary distillation column

In this example a mixture of toluene and benzene is fed to a distillation column where the two chemicals are separated into two high-purity streams. The stream recovered at the top is called the distillate and contains mostly the more volatile component benzene. The liquid recovered at the bottom is called the bottoms and would contain mostly the less volatile component, toluene. In addition to the column, which mainly consists of trays that aid in establishing contact between the rising gases and the descending liquid to facilitate mass transfer, the separation system involves a total overhead condenser and a bottoms reboiler. The overhead total condenser condenses all the vapors from the top of the column. The liquid formed is then partially returned to the top of the column as reflux, again to facilitate gas-liquid contact and thus enhance mass transfer, and the balance liquid is drawn as the distillate D. The bottoms reboiler draws liquid from the bottom of the column and partially evaporates this stream, which is returned to the bottom of the column as vapor, again to facilitate gas-liquid contact and to enhance mass transfer.  The remaining liquid is drawn as the bottoms product B. Jeankoplis (1993) as well as Seader and Henley (2006) provide a more detailed description of the distillation towers.

The attained purity of the distillate and bottoms depends on many design variables. In this simplified version of the distillation tower, the design variables are N1, N2, R and VB. Especially the latter two design variables reflect the quantity of liquid and vapor returned to the column respectively (e.g., Douglas, 1988). The discussion here attempts to give an idea of how the design variables affect the intended separation process. Typically, as the number of trays in the column increases, gas-liquid contact increases, and therefore mass transfer is enhanced, causing the distillate to become richer in the more volatile component (benzene in this case) and the bottoms to become richer in the less volatile component (toluene in this case). Therefore, as N1 and N2 increase, XD increases and XB decreases. Also, any increase in the gas-liquid traffic in the column increases the mass transfer coefficients, leading to an enhancement in the separation process.  Thus, an increase in R and VB would increase XD and decrease XB (e.g., Douglas, 1988; Seader and Henley, 2006).

The distillation column in Figure 6, although simplified, still involves reflux streams that are directly linked in quality to the distillate and bottoms product qualities, which are output variables of the distillation model (refer to Figure 7). With reference to Figure 6, the reflux stream L has a composition equal to that of the distillate, and the vapor boil-up stream V has a composition derived (via the equilibrium relationship, Eq.(11)) from the bottoms product composition XB. Since the compositions for the reflux L and the boil-up stream are essential for the stage-to-stage calculations, and they can be determined only from the output of the model, an iterative approach must be used.

Parameters, design variables, and the output variables are portrayed in Figure 7 and Figure 8. Figure 8 shows a flowchart on how the model finds a solution for the output variables D, B, XD and XB  for a given set of parameters F and XF and design variables N1, N2, R and VB. First, the values of the variables XB and XD are assumed. Overall mass balance Eq. (7) and Eq. (8) can then be used to calculate values of B, the bottoms product flow rate, and D, the distillate product flow rate:

(7)

(8)

The operating equation relates the mole fraction of benzene leaving stage N, XN, to the vapor mole fraction leaving plate N+1, as shown in Eq. (9) (Refer to Figure 6, plate N) (Seader and Henley, 2006).

There are two operating lines, one for the rectification section and the other for the stripping section, as each has different liquid-vapor traffic profiles within the column. So, for any plate above the feed plate (rectification section), Eq. (9) can be used to calculate YN+1 from XN.  For any plate below the feed plate (stripping section), Eq. (10) can be used. The equilibrium relationship Eq. (11) relates both the liquid stream composition leaving plate N, XN, to the vapor phase composition leaving the same plate YN.

The rectification operating line, the stripping operating line, and the equilibrium equations are given as follows:

(9)

(10)

(11)

where K is the equilibrium constant (see, e.g., Seader and Henley, 2006).

The rectification operating line and the equilibrium line equations can be used to perform stage-to-stage calculations on each tray starting from the top plate until the feed plate,  N1+1, is reached, where the vapor composition leaving  the feed plate, , is calculated. The same calculations can be used from the last plate N1+N2+1, upward through the column, using the stripping operating line Eq. (10) and the equilibrium line Eq. (11) until the liquid composition leaving the feed plate  is calculated. These calculated concentrations at the feed plate are compared against those calculated from the feed composition via a simple error function, Error (1) and Error (2) as defined by Eq. (12) and Eq. (13):

(12)

(13)

where equil(XF) is the concentration of a vapor that is in equilibrium with a liquid stream of mole fraction XF. These errors are minimized by varying the chosen value of XB and XD until the errors are within the required tolerance.

Figure 7 is a schematic black box model that identifies the parameters in this distillation design problem, which are the values of feed composition XF and feed flow rate F, which are fixed;  the design or input variables N1, N2, R and VB; and the output variables XD, XB, D and B.

Figure 7. Inputs (left), fixed parameters (top) and outputs (right) for an analysis model for a distillation column

The objectives of this problem are to simultaneously maximize the product yield (D) and purity (XD), which are conflicting objectives. There are four design variables, N1, N2, R, VB, and three parameters, F, XF and P. The lower and upper bounds of the four design variables are given, and the parameters are fixed (see Eq. (14)). A multi-objective optimization model with two design objectives and several constraints is constructed:

(14)

This optimization model is solved using the conventional MOGA and the improved MOGA. Figure 8 shows the obtained optimization results.

Figure 8. Pareto solutions for distillation column design using the conventional MOGA and the improved MOGA

It is observed from Figure 8 that the Pareto frontiers from both approaches agree with each other. Figure 8 also shows that as the purity and therefore the quality of the distillate improves (higher XD) it reduces the quantity of the final product D available for sale. A high purity also affects the total number of stages, requiring a larger number of stages to be able to handle the sharper purification.

5. CONCLUSIONS

The main contribution of the approach developed in this paper is that, for the first time in the literature, online metamodeling for both fitness estimation and reproduction has been integrated and used to significantly reduce the number of function calls in a MOGA. As shown in the examples and test results, this improved MOGA has resulted in significant savings in terms of the number of function calls while obtaining solutions that are similar to those obtained from a conventional MOGA.

There are two main features in the improved MOGA. These are: i) online metamodeling for fitness evaluation, and ii) adaptive DOE for reproduction. These two features work in concert with the kriging metamodeling in different phases of the MOGA as follows.

In the fitness evaluation, kriging metamodeling is used to estimate the response for some design points to save the number of function calls. This is feasible because the responses for the design points do not have to be calculated precisely using the simulation. Instead, an estimate of their simulation response can be used only if the associated error does not change the domination status. In the reproduction phase, kriging metamodeling is used to predict the Pareto frontier in every generation and thus help MOGA to converge faster. As MOGA solutions are evolved, the predicted Pareto frontier approaches the Pareto frontier. Thus, when some design points are selected from the predicted optima and their responses are evaluated and added to the next population, the number of non-dominated design points is increased more quickly, so that eventually the Pareto frontier is obtained in fewer generations than with a conventional MOGA.

Seven examples of both numerical and engineering types and with different degrees of difficulty have been used here to demonstrate the applicability of the improved MOGA. The results confirm that this new optimization approach is indeed able to estimate the Pareto frontier with comparable quality to a conventional MOGA approach, while significantly reducing the number of function calls. For the seven examples, it was observed that using the improved MOGA saved an average of 70% of function calls compared to the conventional MOGA.

The fitness estimation and adaptive DOE techniques proposed in this paper are not restricted to a specific MOGA approach. In fact, these techniques can be integrated with other population-based stochastic multi-objective optimization methods with schemes for fitness evaluation and new population generation, such as the particle swarm optimization (e.g., Kennedy and Eberhart, 1995). This aspect can be further investigated as part of an extension to this paper.

ACKNOWLEDGEMENTS

The work presented in this paper was supported in part by the Office of Naval Research. It was also supported in part by The Petroleum Institute (PI), Abu Dhabi, United Arab Emirates, as part of the Education and Energy Research Collaboration (EERC) agreement between the PI and University of Maryland, College Park. Such support does not constitute an endorsement by the funding agency of the opinions expressed in the paper.

4.	Difficulties Encountered/Overcome

Problems with the cost model: Optimization results do not show trade-offs between the cost functions under consideration. New component data (Propane/Propylene) were added to the model to overcome the difficulties faced using the Benzene/ Toluene system, since the Propane/ Propylene system is much more difficult to separate. The new modified Matlab will be tested during the next quarter.

5.	Deliverables for the Next Quarter

- Explore solution space and obtain robust optimum solutions.

- Resolve problems with the cost model.

- Consider extensions to the robust optimization model.

Appendix

Justification and Background

Optimization-based design of distillation towers needs to be better understood, particularly when significant variability exists during the operation of these systems in a refinery plant.

A preliminary review of the literature has revealed that previous methods in design and/or operation of petrochemical systems have been mainly based on either engineering decisions or business decisions.  The literature is sparse for the cases when these two types of decisions are integrated sequentially. However, given that operating decisions are based on engineering and business considerations simultaneously, these methods should be further developed and tuned to actual conditions of real plants to increase profitability.

Approach

There are two main tasks in the proposed approach. Both tasks will begin after a literature review in the respective domain is performed.

Task 1 (PI):

Develop and implement engineering analysis models for a petrochemical system:

- Task 1.1: Develop a MATLAB-based multi-input, multi-output analysis model for a distillation column.

- Task 1.2: Extend the above analysis model for the distillation column to include: (i) additional complexity, (ii) subsystem details; or, expand the model to include other subsystems in a plant. The ultimate goal is to develop an integrated multi-subsystem petrochemical analysis model for a plant or a group of units in the plant.

Task 2 (UMD):

Develop and implement a robust optimization approach:

- Task 2.1: Develop and implement a MATLAB-based multi-objective and reliability-based robust optimization approach for the above analysis models.

- Task 2.2: Extend the robust optimization approach to consider the case when: (i) the upper and lower bounds for the known range of inputs include quantifiable variability, (ii) for a subset of uncertain inputs, their probability distribution is available, while for the remaining inputs the range is given.

Two-Year Schedule

Tasks 1 and 2 will begin in the first year. Tasks 1.1 and 2.1 are expected to be completed by the end of the first year. Tasks 1.2 and 2.2 will begin toward the end of the first year and are expected to be completed by the end of the second year.

Key References

- Forbes, R.J., Short History of the Art of Distillation, E.J. Brill, Leiden, 1948.

- Grossmann, I. E., Sargent, R. W. H., “Optimum Design of Chemical Plants with Uncertain Parameters,” AIChE Journal, 24(6): 1021-1028, 1978.

- Halemane K. P., Grossmann I. E., “Optimal Process Design under Uncertainty,” AIChE Journal, 29 (3): 425-433, 1983.

- Inamdar, S. V.; Gupta, Santosh K.; Saraf, D. N, “Multi-Objective Optimization of an Industrial Crude Distillation Unit Using the Elitist Non-Dominated Sorting Genetic Algorithm,” Chemical Engineering Research and Design, 82(5): 611-623, 2004.

- Janak, S. L., Lin, X., Floudas, C. A., “A New Robust Optimization Approach for Scheduling Under Uncertainty: II. Uncertainty with Known Probability Distribution,” Computers and Chemical Engineering, 31, 171-195, 2007.

- Li, M., S. Azarm, and A. Boyars, “A New Deterministic Approach using Sensitivity Region Measures for Multi-Objective and Feasibility Robust Design Optimization,” Trans. ASME, Journal of Mechanical Design, 128 (4), 874-883, 2006.

Lin, X., Janak, S. L., Floudas, C. A., “A New Robust Optimization Approach for Scheduling Under Uncertainty: I. Bounded Uncertainty,” Computers and Chemical Engineering, 24, 1069-1085, 2004.

Dynamics and Control of Drill Strings on Fixed and Floating Platforms UMD Investigators: B. Balachandran GRA’s: Chien-Min Liao (started in SPRING 2007) PI Investigator(s): Mansour Karkoub and Youssef Abdelmagid Start Date: 12/01/2006 Report Date: 30 September 2007

1.	Objective

Research objectives are the following: i) develop and analytically and numerically study control-oriented models for drill strings, ii) investigate control of an under-actuated nonlinear system (drill string) with complex interactions with the environment, and iii) build a drill-string testbed at  PI & UMD to validate  the analytical findings and suggest possible strategies to mitigate drill-string failures.

2.	Deliverables

On the modeling, analysis, and simulation front, the following are being addressed:

- Reduced-order models, which can be used to study bending and torsion motions of the drill string when it is subjected to lateral and axial applied forces, are being examined.

- Contact between drill string and outer shell and interactions at the bottom of the drill string are also being considered.

On the experimental front, the following are being addressed:

- Application of static/dynamic force to introduce bending motions in the string while it is rotating

- Relative displacement between two sections due to an applied lateral force

- Contact between drill string bottom and the well

- Application of longitudinal force to the drill string

- Measurement of drill string motions

3.	Summary of Project Activities for Completed Quarter

Accomplishments:

- A four degree-of-freedom (DOF) model has been refined and used to study motions of a drill string when an external torque is applied. Simulation results have also been generated.

- A five degree-of-freedom model is being refined, and simulations with an initial five degree-of-freedom model have also been initiated.

- An experimental arrangement has been designed with sensors, control, and other units.

In the following sections, the project progress is briefly detailed over four sections.  The model derivation is outlined in Section 3.1; the results obtained with the four degree-of-freedom model are presented and discussed in Section 3.2; the results obtained with the five degree-of-freedom model are presented and discussed in Section 3.3; and the experimental arrangement is treated in Section 3.4.

3.1: Derivation of equations of motion for the 4DOF system

As shown in Figure 3.1.1, the drill string system is modeled as a system with two rotating sections and four degrees of freedom. Here, ρ is the radial displacement, θ is the rotation of the first section, φ is the bending angle along the tangential direction, and α is the torsion angle of the second section. In addition, is the unbalanced mass located at a distance e from the axis of rotation of the second section, as shown in Figure 3.1.2.  In the rest of this section, the four degree-of-freedom model obtained by UMD is presented along with a model reported in the literature by Melakhessou, Berlioz, and Ferraris (2003).  Details on how the contact has been modeled at UMD are also presented.

Figure 3.1.1: Drill string modeled as a system with two sections.

Figure 3.1.2: Illustration for unbalanced mass in Section II.

For this system, the kinetic energy can be constructed as

(1)

where the different inertia parameters are appropriately defined (see Section 6.4).  The potential energy is constructed as

(2)

where the different stiffness constants are appropriately defined and λ  is a contact parameter.  It is zero when there is no contact and 1 when there is contact.   The virtual work associated with the external forces and moments is given by

(3)

The work done by the external moment differs from that provided in the work of Melakhessou et al. (2003).  The definitions of the different quantities used in Eqs. (1)-(3) are provided in Section 6.4.

4DOF model of Melakhessou et al. (2003):

Melakhessou et al. (2003) obtained the following equations after neglecting the rotary inertia associated with the unbalanced mass  and considering the work done by  as instead of how it is shown in Eq. (3).

(4)-(7)

where .

4DOF model of UMD:

After  using the Extended Hamilton’s principle and Eqs. (1)-(3), the following governing equations of motion are obtained:

(8)-(11)

It is noted that the UMD form of the 4DOF model is different from that presented in the earlier work of Melakhessou et al. (2003).

Contact between the drill string and outer shell

At UMD, the stick-slip interactions between the drill string and the outer shell are modeled along the lines of the work of Leine et al. (2002).  The different cases considered are as follows: i) no contact between the outer edge of the string and the shell (i.e., λ = 0 in this case) and the normal contact force  is zero in this case, ii) when there is contact and there is only rotation and no sliding, as shown in Figure 3.1.3, and iii) when there is contact and there is pure sliding and no rotation.

The equations used to determine and describe the contact between the drill string and the outer shell are given in Eqs. (12)-(17), and the tangential force to be used in the governing equations is determined from Eqs. (15).    The parameter δ is the radial separation between the shell and the drill string, and this parameter is used to judge whether there is contact or not.    The relative velocity between the two contacting surfaces is used to determine whether there is sliding or not.

(12)

(13)

(14)

(15)

(16)

(17)

Figure  3.1.3:  Illustrations of two contact scenarios between string and shell.

3.2: Simulation results for four-DOF model with constant, external torque:

The parameter values used in the work of Melakhessou et al. (2003) are used to conduct simulations with Eqs. (4)-(7) to provide a flavor for the qualitative aspects of the drill-string dynamics.   These values are also provided in Section 6.4.   It is recalled that the ratio of mb to m is 0.5/2.05, which means the unbalanced mass is close to 25% of the section mass.  The magnitude of the torque is 5 units.  Representative results obtained for two different values of the coefficient of friction are shown in Figures 3.2.1 to 3.2.4.  The initial position of the string is close to the outer shell in both cases. It is noted that the stiffness of the outer shell is orders of magnitude larger than that of the drill string itself.

Case I:  High friction coefficient=0.9

| (a) | (b) |
| --- | --- |
| (c) | (d) |

Figure 3.2.1: Phase portraits:  a) radial displacement of Section II versus radial speed, b) rotation angle of Section I versus rate of change of rotation angle, c)  bending angle of Section II versus rate of change of bending angle, and d) rotation angle of Section II versus rate of change of rotation angle.

| (a) | (b) |
| --- | --- |

Figure 3.2.2: Trajectory of the center of Section II in horizontal plane:  a) in polar coordinates (ρ, θ) and b) in Cartesian coordinates.

Case II:  Low friction coefficient=0.1

| (a) | (b) |
| --- | --- |
| (c) | (d) |

Figure 3.2.3: Phase portraits: a) radial displacement of Section II versus radial speed, b) rotation angle of Section I versus rate of change of rotation angle , c)  bending angle of Section II versus rate of change of bending angle, and d) rotation angle of Section II versus rate of change of rotation angle.

| (a) | (b) |
| --- | --- |

Figure 3.2.4: Trajectory of the center of Section II in horizontal plane:  a) in polar coordinates (ρ, θ) and b) in Cartesian coordinates.

Comparing the results obtained in Cases I and II, it is clear that when the coefficient of friction is high, the trajectory of the drill string stays closer to the center for longer periods than in the other case, when the drill string bounces from one end to the other.   The results compare well with those presented in the work of Melakhessou et al. (2003).  Results obtained by using the UMD model will be included in a future report.

3.3:  5DOF model of PI and simulation results for constant, external torque:

A five degree-of-freedom model has been developed at PI.  In addition to the four coordinates that were used in the 4DOF model, namely, the radial displacement ρ, the rotation of first section or Section I θ, the bending angle along the tangential direction φ, the torsion angle of the second section or Section II α, the additional coordinate is a tilt angle ψ, which is controllable angle at the bottom of the drill string.  The equations of motion can be determined as previously outlined for the 4DOF model.  They are of the following form:

(18)-(22)

The parameter values used to conduct the simulations with Eqs. (18)-(22) are also provided in Section 6.4.   It is recalled that the ratio of mb to m is 0.2/2.05, which means the unbalanced mass is close to 10% of the section mass.  The magnitude of the torque is 2 units.  Representative results obtained for two different values of the coefficient of friction are shown in Figures 3.3.1 and 3.3.2.  The initial position of the string is close to the outer shell in both cases. It is noted that the stiffness of the outer shell is orders of magnitude larger than that of the drill string itself.

Case III:  High friction coefficient=0.9

| (a) | (b) |
| --- | --- |
| (c) | (d) |
| (e) | (f) |

Figure 3.3.1.: a) radial displacement of Section II versus radial speed, b) rotation angle of Section versus rate of change of rotation angle, c) bending angle of Section II versus rate of change of bending angle, and d) rotation angle of Section II versus rate of change of rotation angle, e) tilt angle of the Section II versus rate of change of tilt angle, and f) trajectory of the center of Section II in horizontal plane,  in polar coordinates (ρ, θ).

Case IV:  Low high friction coefficient=0.1

| (a) | (b) |
| --- | --- |
| (c) | (d) |
| (e) | (f) |

Figure 3.3.2:  a) radial displacement of Section II versus radial speed, b) rotation angle of Section versus rate of change of rotation angle, c) bending angle of Section II versus rate of change of bending angle, and d) rotation angle of Section II versus rate of change of rotation angle, e) tilt angle of the Section II versus rate of change of tilt angle, and f) trajectory of the center of Section II in horizontal plane,  in polar coordinates (ρ, θ).

From the results of the simulations shown in the 5DOF case, it is clear that the motions appear to be aperiodic for the two different values of friction considered.  The drill string motions appear to exhibit sliding motions, without the stick and slip aspects seen in the system with 4DOF.   The results obtained are being currently studied to better understand them.

3.4: Experimental arrangement:

3.4.1 Description

To facilitate the analysis of the drill string axial, whirl and stick-slip vibrations, a drill string structure with sensors and actuators is being constructed at UMD to simulate real working conditions.  This arrangement complements the arrangement at PI, which can be used to study different control strategies.  At this stage, a detailed design has been carried out.   As shown in Figure 3.4.1, a slender metal rod is to be driven by a DC motor from the top of the rigid frame, which represents the drill string under the ground.  Spring and damper combination and actuators are used at the bottom of the structure to simulate rock conditions. Due to the eccentricity of the mass distribution in the drill string, whirling motions are expected to occur at high speeds.  For large lateral motions, it is expected that the drill string will collide with the outer pipe, and stick-slip vibrations are expected.  Sensors are to be placed along the string to measure the axial, lateral, and rotational vibrations of the drill string.  Measurements will also include the tilt angle between the drill string and the outer pipe.  The structure will be assembled in the coming weeks.

Figure 3.4.1: Experimental arrangement to study bending-torsion Vibrations (on the left) with details at the bottom (on the right).

3.4.2  Equipment

| Item | Description | Figure |
| --- | --- | --- |
| DC Motor | A DC motor will be used to derive the drill-string system. This motor has the following features; i) maximum speed of 4000 rpm, ii) peak torque of 22.5 oz-in, and iii) a built-in rotary encoder. | 3.4.2 |
| Rotating Disks | The arrangement has an upper disk and a lower disk. The upper disk represents the rotary table of the drill string, and the lower disk represents the combination of the drill collar and drill bit. The diameters of the upper disk and lower disk are 12 inches and 6 inches, respectively. | 3.4.3 |
| Encoder | Absolute rotary encoders are to be used to measure the rotation angles of the disks. These encoders have a resolution of 360 pulses per revolution. | 3.4.4 |
| Actuator | An electro-magnetic actuator will be used to realize an axial loading in the 0-2.5kHz frequency range. This actuator is to be used to simulate the bearing capacity of the soil as well as to provide control input to the system. | 3.4.5 |
| Laser Displace-ment Sensor | A laser sensor is to be used to measure the lateral movement of the bottom end of the drill string. This end is connected to the lower rotating disk and brake housing. | 3.4.6 |
| Optical Sensor | An optical sensor is to be placed on the brake housing to measure the tilt angle of the lower rotating disk. | 3.4.7 |

Table 3.4.1 Components of the experimental arrangement

Figure 3.4.2: DC Motor scale diagram (Ref. Anaheim Automation)

Figure 3.4.3: Rotating Disk (Ref. Encoder Product Inc.)

Figure 3.4.4: Encoder Model 960 (Ref. Encoder Product Inc.)

Figure 3.4.5: Electro-Magnetic Actuator (Ref. ETREMA Inc.)

Figure 3.4.6: Laser Displacement Sensor (Ref. Acuity Laser Measurement)

Figure 3.4.7: Optical Sensor (Ref. Philtec Inc.)

- Difficulties Encountered/Overcome

- Modeling and implementation of the contact between the drill string and the outer shell needed considerable attention.  There are still discrepancies between models published in the literature and the models developed in this work that need to be ironed out. An appropriate oil well model has not been identified yet.

- The detailed design of the experiment needed attention for simulating realistic conditions. Availability of components such as encoders and sensors also posed problems and prompted the search for alternative arrangements in the design.

- Deliverables for the Next Quarter

i) Modeling, Simulation, and Analysis:

Ongoing studies on the reduced-order models will be continued to better understand the different 4DOF models, as well as the PI 5DOF model, and the UMD 5DOF model that will be presented in a future report.  The efforts will be focused on resolving the differences amongst these different models.

ii) Experiments:

In the work of Mihajlovic et al. (2007), a series of experiments have been conducted on understanding friction-induced vibrations and self-sustained lateral vibrations caused by a mass unbalance in an experimental rotor system.  The results of this work will be used as a foundation for the planned experiments at UMD.  The experiments will be conducted with a focus on the following: i) drill-string performance on the bottom end section, ii) interaction between the rotating disk and stick-slip phenomena, and iii) rotating system subjected to an axial force.

Appendix

Justification and Background

Drill-string dynamics need to be better understood to control drill strings and steer them to their appropriate location in oil wells, in particular, for applications such as geosteered drilling.

Although a considerable amount of work has been carried out on oil-well rotary drilling (for example, Spanos et al. 2003), the nonlinear dynamics of this system are not well understood given that the drill string can undergo axial, torsional, and lateral vibrations, and operational difficulties include sticking, buckling, and fatiguing of strings.

Approach

A combined analytical, numerical, and experimental approach will be pursued at the University of Maryland (UMD/PI). Specifically, the drill string is to be modeled as a nonlinear dynamical system consisting of interconnected structural components (e.g., tubes) with joints. Appropriate attention will also be paid to the soil conditions. Finite element methods are to be used for developing computational models. The experiments at UMD/PI will be tailored to address specific aspects of the drill-string dynamics that may complement the scaled, steerable drill-string model experiments being planned at PI.  Actuator and sensor choices will also be explored to determine how best to control the system dynamics. The studies will be initiated with drill strings located on fixed platforms and later will be extended to systems located on floating platforms.

Two-Year Schedule

January 1, 2007 to July 31, 2007:  Modeling of drill-string dynamics, computational models; analytical and numerical studies; identification of appropriate oil-well model

August 1, 2007 to October 31, 2007:  Analytical and experimental studies and initiation of experimental studies

November 1, 2007 to January 31, 2008:  Completion of preliminary control design studies

February 1, 2008 to July 31, 2008: Studies on “optimal” actuator and sensor configurations for control of drill-string dynamics, and investigations into the need for vibration isolation schemes

August 1, 2008 to October 31, 2008: Studies on drill-string systems located on floating platforms

Nomenclature and Values Used for Simulations

| Symbol | Analytical model definition | Variable/Simulation value |
| --- | --- | --- |
|  | Radial displacement | Variable |
|  | Rotation angle of Section I | Variable |
|  | Bending angle along the tangential direction | Variable |
|  | Rotation angle of Section II | Variable |
| ψ | Tilt angle of Section II | Variable |
|  | Mass moment of inertia of Section I | 100 units |
|  | Mass moment of inertia of Section II | 100 units |
|  | Mass moment of inertia of Section II (tilting angle) | 50 units |
|  | Radial distance to unbalanced mass | 0.5 units |
|  | Initial displacement of Section II | 1.45 units |
|  | Mass of Section II | 2.05 units |
|  | Unbalanced mass | 0.5 or 0.2 units |
|  | Bending stiffness in radial direction | 0.5 units |
|  | Bending stiffness in tangential direction | 0.5 units |
|  | Torsion stiffness of Section II | 0.03 units |
|  | Contact stiffness of Section II | 5000 units |
|  | Contact determination term; equals to 1 when there is contact and 0 otherwise | 0 or 1 |
| μ | Friction coefficient | 0.1 or 0.9 |
|  |  | -- |
|  | Separation from Section II to the outer wall at initial position | -- |

Key References

1. 	Leine, R. I., van Campen, D. H., and Keultjes, W. J. G. (2002). “Stick-Slip Whirl Interaction in Drill String Dynamics,” ASME Journal of Vibration and Acoustics, Vol. 124 (2), pp. 209-220.

2. 	Melakhessou, H., Berlioz, A., and Ferraris, G. (2003). “A Nonlinear Well-Drillstring Interaction Model,” ASME Journal of Vibration and Acoustics, Vol. 125 pp. 46-52.

3. 	Nayfeh, A. H. and Balachandran, B. (1995). Applied Nonlinear Dynamics: Analytical, Computational, and Experimental Methods, Wiley, New York.

4. 	Spanos, P. D., Chevallier, A. M., Politis, N. P., and Payne, M. L. (2003). “Oil and Gas Well Drilling: A Vibrations Perspective,” Shock and Vibration Digest Vol. 35(2), pp. 85-103.

5. 	Mihajlović, N., van Veggel, A. A., van de Wouw, N., and Nijmeijer, H. (2004)  “Analysis of friction-Induced Limit Cycling in an Experimental Drill-String System,”  ASME Journal of Dynamic Systems, Measurement, and Control, Vol. 126(4), pp. 709-720.

6. 	Mihajlović, N., van de Wouw, N., Rosielle, P.C.J.N., and Nijmeijer, H. (2007) “Interaction between torsional and lateral vibrations in flexible rotor systems with discontinuous friction,” Nonlinear Dynamics, published online.

Thermally Enhanced Polymer Heat Exchanger for Seawater Applications UMD Investigator: Prof. Avram Bar-Cohen GRA(s): Juan Cevallos, Patrick Luckow PI Investigator(s): Dr. Peter Rodgers, Dr. Ahmed Abdala Start Date: October 2006 Report Date: 30 September 2007

1.	Objective

The proposed two-year study will address the fundamental thermal performance issues associated with the use of thermal high-conductivity polymer materials, addressing their advantages and limitations and defining the heat exchanger configurations that optimize the unique characteristics of high conductivity polymer materials.

To achieve optimum thermal performance, a clear understanding of the thermal engineering characteristics of fiber-enhanced polymer tubes/channels and the fundamental thermo-fluid predictive relations that underpin heat exchange in such configurations will be developed.

Successful completion of this effort will provide fundamental thermofluid modeling relations for thermally enhanced polymer tubes and channels; it will also provide the basis for determining the environmental, weight, and cost advantages resulting from future applications of this technology to seawater heat exchangers for shipboard heat exchangers and for the petroleum and power industries.

2.	Deliverables

- Continue literature review on (i) the strengths and weaknesses of various commercially available heat exchanger designs and (ii) current usage of polymer heat exchangers.

- Continue assessment of the theoretical performance limit of polymer candidate materials and configuration(s).

- Develop new polymer nano-composite materials.

- Characterize the thermal conductivity of the polymer nano-composite materials developed so far.

- Construct laboratory-scale test apparatus for thermal characterization of polymer heat exchanger “building block” tube/channels and characterize thermal properties.

- Mr. Juan Cevallos, UMD graduate student, to work at PI from June 19 to July 20 on the following tasks:

  - Prepare a forthcoming publication relating to the project research undertaken to date.

  - Visit ADNOC facilities to obtain insight into existing heat exchanger designs and their potential for replacement with thermally enhanced polymer-based designs.

3.	Summary

- Continued literature review on: (i) the strengths and weaknesses of various commercially available heat exchanger designs and (ii) current usage of polymer heat exchangers.

  - Compiled polymer heat exchangers catalog, and updated it with the details of new polymer heat exchangers, including their vendor specified performance limits, that have recently been introduced to the market.

  - Identified metallic materials that are most commonly used in heat exchangers that use corrosive fluids.  The properties of these materials (Table 1) can be used to assess the performance of thermally conductive thermoplastics.  For seawater applications, Cu-Ni alloys and titanium are the most commonly used heat exchanger metals.

Table 1  Commonly used metals for heat exchangers having corrosive fluids.

| Material | Density (x10−3 kg/m3) | Specific heat (J/kg.K) | Thermal Conductivity (W/m.K) | Yield Strength (MPa) | Tensile Strength (MPa) | CTE (x106 m/m.K) | Melting range (oC) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| SS 304 | 7.92 | 502 | 16 | 207 | 586 | 4.4 | 1399-1454 |
| SS 316 | 8.08 | 502 | 16 | 276 | 621 | 4.9 | 1371-1399 |
| Titanium | 4.51 | 582 | 17 | 517 | 621 | 2.6 | 1691 |
| Cu-Ni 90/10 | 8.9 | 377 | 50 | 140 | 320 | 17 | 1100-1145 |
| Cu-Ni 70/30 | 8.95 | 377 | 29 | 170 | 420 | 16 | 1170-1240 |

- Continued assessment of the theoretical performance limit of polymer candidate materials and configuration(s).

  - The mechanical and thermal properties of commercially available thermally conductive polymers have been compiled (Table 2).  This data can be used to assess the performance limits of candidate polymeric materials for heat exchanger applications.

Table 2  Commercially available thermally conductive polymeric materials.

| Company | Resin | Thermal Conductivity | Tensile Strength | Tensile Modulus | Density | HDT (oC) |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | (W/m K) | (MPa) | (MPa) | (g/cc) | @ 1.8 MPa |
| Cool Polymers | PPS | 20 | 45 | 13000 | 1.7 | 260 |
| Cool Polymers | PP | 5 | 25 | 5200 | 1.38 |  |
| GE Plastics | PA 6 | 1.1 | 81 | 10160 |  | 174 |
| GE Plastics | PA 6/6 | 1.2 | 95 | 11920 | 2.04 | 226 |
| GE Plastics | PPS | 7/2.2 | 139 | 27586 | 1.74 | 270 |
| PolyOne | PPS | 10-11 | 100 | 26200 | 1.82 | 282 |
| PolyOne | PA 6/6 | 10-12 | 60.7 | 14479 | 1.58 | 254 |
| PolyOne | LCP | 18-20 | 103.4 | 20684 | 1.82 | 277 |
| PolyOne | PA 12 | 20-25 | 39.3 | 14479 | 1.68 | 185 |
| RTP | LCP | 18.01 | 45 | 24132 | 1.7 | 232 |
| RTP | PPS | 2.31 | 62 | 26201 | 1.7 | 260 |

Note: HDT = heat deflection temperature.

- Developed new polymer nano-composite materials

  - Polycarbonate-exfoliated graphite oxide composites have been prepared with different loading of exfoliated graphite oxide, i.e. 0.5, 1, 2, 3, 4, 5, and 10% (by weight).

  - The thermal stability of these composite samples where characterized using thermal gravimetric analysis (TGA) to estimate the operating range of the polymer composite, as shown in Figure 1.  Differential scanning calorimetry (DCS) analysis was also performed to assess glass transition and melting behavior.  These analyses revealed:

    - The temperature onset for thermal degradation of the polymer and polymer composite samples is 325°C.

    - The glass transition temperature of the polymer and the composite samples is approximately 140°C.

  - The polymer composite samples are currently being processed to produce test samples to characterize both the mechanical behavior and thermal conductivity.

Figure 1. Thermal gravimetric analysis traces of polycarbonate and polycarbonate-thermally exfoliated graphite oxide composites with different loading of thermally-exfoliated graphite (0%, 1%, 3%, 10% by weight).

- Characterizing the thermal conductivity of the polymer nano-composite materials developed so far remains to be done.

  - Due to the unavailability of necessary equipment for measuring thermal conductivity, this task will be completed during the next quarter.

- Constructed laboratory-scale test apparatus for thermal characterization of polymer heat exchanger “building block” tube/channels and characterized thermal properties

  - Prior to building a test apparatus, the impact of molding the candidate materials on the mechanical and thermal characteristics of the heat exchanger must be assessed.  To this end, the following activities have been completed:

    - Approximated the range of rheological characteristics (flow length vs. thickness) of thermally conductive thermoplastics despite the lack of data provided by the vendors.  This information is crucial for manufacturing of these new materials, given that the melt viscosity and melt thermal conductivity are expected to be significantly different from common resins.

  - Injection molding simulation software, Moldflow(, was identified to assist in assessing three fundamentals issues: ability to fill the mold, occurrence of weld and meld lines, and shrinkage and warpage of the part.

- Prepared a forthcoming publication relating to the project research undertaken to date.

  - Drafted a finalized report, which will be made into a conference publication that includes the following topics:

    - A review of commercially available polymer heat exchangers to assess the current applications and performance limitations.

    - A review of thermally conductive polymeric materials, including their thermal and mechanical characteristics, to assess their potential as new candidate polymeric heat exchanger materials.

    - A doubly finned counterflow plate heat exchanger analytical model, which was developed to parametrically analyze thermal performance in terms of heat transfer rate and pumping power (Figures 2 and 3 below show graphical representations of this parametric analysis).

| (a) Heat Transfer Rate | (b) Coefficient of Performance |
| --- | --- |
| Figure 2 Doubly finned counterflow heat exchanger performance as a function of fin spacing and fin thickness (tb = 1 mm, H = 10 mm, W = L = 1 m, u1 = u2 = 2 m/s, turbulent flow) |

| (a) Heat Transfer Rate | (b) Coefficient of Performance |
| --- | --- |
| Figure 3 Parametric optimization of heat transfer rate and COP within a set rectilinear volume (k = 20 W/m-K, tb = 1 mm, H = 10 mm, W = L = 1 m, u1 = u2 = 2 m/s, turbulent flow). |

- Visited ADNOC facilities to obtain insight into existing heat exchanger designs and their potential for replacement with thermally enhanced polymer based designs.

  - During his visit to the Petroleum Institute, Juan Cevallos, along with Dr. Peter Rodgers, attended a one-day information session run by Dr. Nashaat M. Mohamed of ADGAS, who provided an extensive overview of the seawater cooled systems used at the Das Island gas liquefaction (LNG) plant.  The relevant points of these systems are summarized:

    - Many types of fouling exist in these heat exchangers: crystallization, corrosion, biological, and particulate.

    - Shell-and-tube surface condenser heat exchangers are the primary users of cooling seawater, i.e. they utilize 75% of the pumped seawater.

    - The heat exchangers are constructed from several materials due to different performance requirements and applications:

      - Cu-Ni alloys (70/30 and 90/10)

      - Titanium (all surface condensers use this expensive metal)

      - Carbon steel

      - Exotic alloys (Avista 250)

    - Flow velocity inside heat exchanger tubes is usually 2 to 3 m/s. The tubes are typically ¾ - 1 inch in diameter, having 1 to 2 mm thick walls.  The surface area of the tube bundles ranges from 10 – 800 m2.

    - Shell length does not exceed 6 m.

  - These new findings serve as motivation to repeat the parametric analysis previously undertaken for a plate heat exchanger for shell and tube heat exchangers. Preliminary calculations are currently in progress.

- Design and construct a pilot scale test facility for characterizing polymer heat exchanger thermal performance has been postponed.

  - This task will be postponed until the aforementioned laboratory-scale apparatus has been constructed and tested, following the injection molding simulations and analysis.

4.	Difficulties Encountered/Overcome

- Rheological properties of thermally conductive thermoplastics are not available from vendors. Approximating the melt viscosity and thermal conductivity and changing the property values of the base resins in the Moldflow simulation can help overcome this limitation.

5.	Deliverables for the Next Quarter

- Continue thermal-fluidic analysis of shell and tube heat exchange design, conducting a literature review of the design of shell and tube heat exchangers and comparing coefficient of performance to work previously done on doubly-finned counterflow heat exchanger.

- Conduct analysis of energy content of thermally conductive polymer and develop appropriate metrics to compare energy used in polymer heat exchangers as compared to conventional heat exchangers.

- Optimize heat exchanger design for greatest environmental, weight, and cost savings over conventional designs via a parametric analysis of the metrics developed in the previous task.

- Assess the impact of molding thermally conductive thermoplastics on the thermal and mechanical characteristics of the heat exchanger by simulating the injection molding process in Moldflow(. In this simulation the following tasks will be done:

  - Evaluate the geometrical limitations in the injection molding process inherent in thermally conductive thermoplastics.

  - Design an optimized runner and gate system to avoid the occurrence of weld lines that could compromise the structural stability of the system, and to ensure that the mold is filled completely.

  - Investigate the alignment of fibers in order to achieve the highest thermal conductivity in the plane in which conduction occurs.

  - Assess the effects of shrinkage and warpage on the final product

- Characterize the thermal conductivity of the polymer nano-composite materials developed so far.

- Construct laboratory-scale test apparatus for thermal characterization of polymer heat exchanger “building block” tube/channels and characterize thermal properties

Appendix

Justification and Background

High thermal-conductivity polymer heat exchangers could play an important role in seawater-based cooling systems for the power industry, naval applications, and coastal petroleum refineries. Such advanced heat exchangers could facilitate the more direct use of seawater in these applications, while providing reduced weight, greater resistance to corrosion and fouling, reduced energy consumption, and greater geometric flexibility and ease of manufacturing, relative to the technology in use today.

While conventional metal heat exchangers are generally incapable of providing reliable long-term service with salt water (and other corrosive fluids), to date the cost, complexity, and the restricted availability of exotic corrosion-resistant materials have limited the design and application of seawater heat exchangers.

Compact, high performance heat exchangers fabricated of high thermal-conductivity polymers offer a promising alternative to these exotic materials in refineries and power plants located along the coast, where seawater is the primary coolant.

Approach

1.	Review the available compact liquid-liquid heat exchanger concepts, e.g., shell-in-tube and plate-coil, and identify their strengths and weaknesses.

2.	Define the relevant heat exchange metrics, e.g., kW/m3 and COP (kW heat/kW pumping), and rank the concepts by these metrics.

3.	Review and tabulate the thermal, chemical, and mechanical properties of thermally enhanced polymer materials suitable for use in liquid-to-liquid heat exchangers.

4.	Apply the selected metrics to conventional polymer and thermally enhanced polymer heat exchangers, and re-rank the heat exchanger concepts.

5.	Develop new polymer nanocomposite materials and compare their thermal, chemical, and mechanical properties to the best-known thermally enhanced polymeric materials.

6.	Select the most promising polymer materials and configuration(s) for seawater heat exchange and determine the theoretical performance limits for these configurations/materials.

7.	Fabricate and test polymer tube/channel heat exchanger “building blocks” to determine the pressure drop and heat transfer coefficients achievable.

8.	Correlate baseline thermofluid data for “building block” tube/channels and compare to theoretical predictions.

9.	Develop a test loop for testing of pilot scale polymer heat exchangers, representative of industrial applications.

10.	Develop recommendations for seawater-cooled, thermally enhanced polymer heat exchangers for specific applications, such as in the power industries, refineries, and aboard ships.

Two-Year Schedule

Year 1:

- Conduct literature review on: (i) the strengths and weaknesses of various commercially available heat exchanger designs and (ii) current usage of polymer heat exchangers.

- Assess the thermal, chemical, and mechanical properties of thermally-enhanced polymer materials suitable for use in liquid-to-liquid heat exchangers.

- Assess theoretical performance limit of polymer candidate materials and configuration(s).

- Construct laboratory-scale test apparatus for thermal characterization of polymer heat exchanger “building block” tube/channels.

- Fabricate polymer nanocomposite materials suitable for polymer heat exchangers.

- Characterize thermal properties of polymer “building block” tube/channel heat exchanger test vehicles.

- Correlate baseline thermofluid data for “building block” tube/channel with theoretical predictions.

Year 2:

- Construct a test loop for thermal characterization of pilot scale polymer heat exchangers representative of industrial applications.

- Characterize thermal properties of pilot-scale polymer heat exchangers.

- Recommend seawater-cooled, thermally enhanced polymer heat exchangers for specific applications.

Key References

- Zaheed, L., and Jachuck, R.J.J., 2004, “Review of polymer compact heat exchangers, with special emphasis on a polymer film unit,” Applied Thermal Engineering, Vol. 24, No. 16, pp. 2323-2358.

- Bahadur, R., and Bar-Cohen, A., 2005, “Thermal Design and Optimization of Polymer-Based Pin Fin Natural Convection Heat Sinks,” IEEE Transactions on Components and Packaging Technologies, Volume 28, Issue 2, pp 238-246.

- Zweben, C., 2003, “Emerging High-Volume Commercial Applications for Thermally Conductive Carbon Fibers,” Sixth International Business Conference on The Global Outlook for Carbon Fiber, San Diego, California, USA, November 5 – 7.

- Shah, R.K., 2006, “Advances in science and technology of compact heat exchangers,” Heat Transfer Engineering, vol. 27, no. 5, pp. 3-12.

- Pugh, S. J., et al, 2005, “Fouling During the Use of Seawater as Coolant—the Development of a User Guide,” Heat Transfer Engineering, vol. 26, no. 1, pp. 35-43.

- Zweben, C., 2004, “Emerging High-Volume Commercial Applications for Advanced Thermally Conductive Materials,” SAMPE 49th International Symposium and Exhibition, Long Beach, California.

An EHD-Enhanced Gas-Liquid Separator UMD Investigators: Dr. Serguei Dessiatoun, Dr. Amir Shooshtari GRA’s: Mohamed Alshehhi PI Investigator(s): Dr. Michael Ohadi, Dr. Afshin Goharzadeh Start Date: October 2006 Report Date: 30 September 2007

1.	Objective/Abstract

To study hybrid inertia-EHD gas-liquid separation phenomena for electrically conductive and nonconductive liquid particles suspended in a moving gaseous medium. This is useful in a variety of applications including petrochemical and process industries, refrigeration and cryogenics, and micron/sub micron air filtration and clean room applications.

2.	Deliverables

- Literature review (continued)

- Visualization test setup

- Experimental test setup

- Numerical modeling to study effect of EHD on separating liquid particles from gas

3.	Summary

- Literature Review:

  - Reviewing major gas/conductive liquid separation techniques

  - Summarizing all governing equations for numerical modeling

In order to extend the understanding of EHD-enhanced separation mechanism, all the governing equations, including fluid flow, electric field and particle trajectory equations, were summarized, and the dimensionless variables were identified. Different scenarios of charging particles, including the diffusion charging and the field charging, were studied. The importance of each term in the governing equations was assessed. Equation 1 represents the trajectory of a particle (a liquid droplet in this case) due to charge accumulation and under the influence of the electric field.

where:

- µ = Gas Viscosity (N.s/m2)

- CD = Drag Coefficient

- Re = Reynolds Number

- u = Gas Velocity (m)

- up = Particle Velocity (m)

- g =  Gravity Force (N)

- ρ = Gas Density (kg/m3)

- ρp = Particle Density (kg/m3)

- e = Electron Charge (1.6 E -19 C)

- E = Field Strength (V/m)

- dp = Particle Size (m)

- ρp = Particle Density (kg/m3)

- k = Boltzmann Constant (1.38 E -23 m2.kg/s2.K)

- T = Temperature (K)

- KE = Constant (9.0 E 9 N.m2/C2)

- Ci = Ions Mean Thermal Speed (240 m/s)

- ρi = Charge Density (C/m3)

- t = Time (s)

- ε = Relative Permittivity

- Zi = Ions mobility (0.00015 m2/V.s)

- Experimental Test Setup (Fig. 1):

  - Major equipment needed for the test loop was finalized

  - Aerodynamic Particle Sizer was purchased (needed to measure separation efficiency)

  - Water mist generator (fog maker) was purchased

Figure 1: Sketch of the experimental set-up

- Visualization Test Setup (Fig. 2):

  - A preliminary setup was constructed to show the effect of EHD on separating water vapor from air (Fig. 2, movie 1).

Figure 2: Sketch of the visualization test setup

Movie 1: Visualization test setup

- Numerical Modeling

The main focus of the last three months was the development of a numerical model to understand the EHD separation process and to compare it to experimental results that were reported in the last EERC quarterly report. The Fluent platform was used for the numerical modeling. The main challenges in this part were to introduce the EHD as a body force, compile, and link it to the main solver, since Fluent did not have a built-in solver for the electrical field and charging process. Custom C++ code describing the particle charging mechanism and EHD body force was written and incorporated in Fluent (Shooshtari, A.).

This numerical modeling will help to understand the following parameters that affect the separation process:

- Separator Geometry

- Particle Size

- Fluid Temperature

- Fluid Pressure

- Fluid Flow Rate

- Applied EHD force (voltage of discharge electrode)

Also, this part will give a clear understanding of the behavior of liquid particles of different diameter size and different injection positions when they are affected by the EHD force. Moreover, the minimum time and separation area required to collect liquid droplets will be provided.

The numerical modeling is still being tested and modified.

4.	Difficulties Encountered/Overcome

Some challenges in the design of gas-and-conductive liquid separator can be identified as:

  - Prevention of charge leakages and/or shortages due to the conductive nature of fluid

  - Power supply design and control mechanisms

5.	Deliverables for the Next Quarter

  - Continue numerical modeling and determine the effects of some parameters such as flow rate and temperature on separation efficiency.

  - Design first generation air-water separator.

  - Start building test loop.

  - Plan a visit to meet with the relevant ADNOC companies in UAE to present the research and to seek where new applications might be possible.

Appendix

Justification and Background

Separation comprises a significant part of the oil and natural gas production process.  In many stages of this process, electrostatic separation significantly increases the efficiency and often decreases the cost of production. Most of the oil producers, including ADNOC, operate where the climate is hot and therefore use refrigeration and air-conditioning equipment.  The efficiency and reliability of this equipment appreciably suffers due to mal-distribution of lubricant oil in the system. Electrostatic separation can correct this mal-distribution and improve the efficiency of this refrigeration and air-conditioning equipment.   Similarly, vapor compression equipment with lubricant circulation is also used in oil refinery processes. This circulation can be significantly improved using EHD separators to increase heat-pumping efficiency. UMD has already developed a working prototype for gas-and-non-conductive droplet separation. However, the fundamentals of this separation mechanism must be better understood to enable optimization of the working design. There is also a need to explore the feasibility of separation of gas-and-conductive liquid mixtures, which poses additional challenges.

Conventional gas/liquid separators are based on inertial and gravitational forces. They have poor efficiency when separating micron-size particles in the flow due to low gravitational and inertial forces acting on small particles. In contrast, electro-hydrodynamic (EHD) forces strongly affect particles of such size. The combination of a conventional separator with EHD allows us to create the most effective and lowest pressure-drop particle separator, with potential applications to separation of electrically conductive and non-conductive liquid particles. The separation of electrically conductive particles like water-air mixtures (fog) imposes significant design constraints on separator electrode design and high-voltage power supply selection.

Approach

Detailed analysis and identification of the phenomena and the design challenges involved in effective implementation of the mechanism. Parametric study of existing and improved separators. Design iterations, including numerical flow and field simulations, fabrication, and testing. Creation of database and engineering design correlations.

Two-Year Schedule

Year 1:

- Conduct literature review to study current technologies for separation of solid or liquid particles from gas flows by electrostatic and electro-hydrodynamic (EHD) forces.

- Evaluate existing technologies and assess their applicability to flow separation of gas-and-liquid-droplet mixtures.

- Evaluate and optimize current designs of UMD EHD separators for non-conductive liquid particles in gas flow.

- Design and fabricate a two-phase gas-liquid droplet separator capable of operating with conductive fluids. Conduct a parametric study of separators for different conductive fluids, concentrations, and gas flow rates.

Year 2:

- Continue optimization and numerical study of hybrid gas-and-non-conductive liquid droplet separator. Continue parametric experimental study of gas-and conductive separator.

- Design iterations and implementation.

- Experiment on different designs.

- Present the best design to ADNOC group of companies.

- Develop design correlation.

- Prepare report.

Key References

- Mo, B., M.M. Ohadi, and S.V. Dessiatoun, "Liquid vapor separation and thermal management in an EHD-enhanced capillary pumped loop,” Heat Transfer 1998, Proceeding of 11th International Heat Transfer Conference, Vol. 2, Taylor & Francis Inc., Levittown, PA, pp.63-68.

- Electrohydrodynamic Liquid-Vapor Separator USA Pat.# 6,582,500

- Schrage, D.S., J.M. Shoemaker, and J. McQuillen, 1998, “Passive two-phase fluid separation,” AIAA 36th Aerospace Sciences Meeting & Exhibit, Reno, NV, Jan. 1998, AIAA-98-0731

- Balachandran, W., Machowski, W., Ahmad, C.N. “Electrostatic atomization of conducting liquids using AC superimposed on DC fields” Industry Applications, IEEE Transactions on Volume 30, Issue 4, July-Aug. 1994 Page(s):850 - 855 Digital Object Identifier 10.1109/28.297899

- Shooshtari, A., 2004, “Experimental and computational analysis of an electrohydrodynamic mesopump for spot cooling applications,” Mechanical Engineering, College Park, University of Maryland

Force-Fed Cooling of Photovoltaic Arrays for High-Efficiency Solar Energy Conversion Systems UMD Investigators: Dr. S. Dessaitoun, Dr. Amir Shooshtari GRA’s: E. Kermani, PI Investigator(s): Dr. M. Ohadi Start Date: March 2007 Report Date: 30 September 2007

1.	Objective/Abstract

The proposed project will create, based on a survey of available literature, a database on the available cooling techniques for high heat flux solar concentrator arrays necessary for efficient conversion of solar energy to electric power. The typical cooling load necessary for optimum radiation concentration and optimum photovoltaic conversion efficiency will be identified, and a novel force-fed cooling technique that has been developed at UMD will be applied to contain this cooling load. An experimental prototype and associated setup will be designed and fabricated to verify the feasibility of this concept and the capacity for cooling by this technique. Based on these experimental results, the radiation concentration levels acceptable to this cooling capacity will be redefined. The type of fluid and its flow rate, the temperature of the surface where solar radiation is incident, and the uniformity of temperature on this active area are the main issues that will be addressed in this proposed project. The scalability of this technique for uniform cooling of industry-scale extended area panels will be a guiding parameter for the design and development of the heat exchanger prototype proposed here.

2.	Deliverables

- Literature survey:

The literature survey compiled in the previous quarter was extended further to include the following subjects:

  - Various types of concentrating solar systems

  - Range of concentration practically being used

  - Maximum achievable concentration

  - PV-cell efficiency under high concentration

  - Optimum cell efficiency

  - PV-thermal technology

- Assessment of solar cell heat load under concentration:

To assess the range of heat load to be removed by the force-fed cooling technique, a series of calculations was carried out and the following parameters were estimated for 100 and 500 concentrations:

  - Solar cell temperature

  - Solar cell efficiency as a function of cell temperature

  - Electricity production

  - Heat rate dissipated by natural convection

  - Needed cooling power

- Microfabrication of channels:

A trial process of microfabrication on a silicon wafer using the Deep Reactive Ion Etching technique was successfully performed. It was concluded that this technique can be used to fabricate the desired design.

- Design of microchannels:

A numerical model was used to determine the optimum microchannel design in terms of various parameters, including channel aspect ratio, channel thickness, wall thickness, etc. The results were compared against available published data. As a result, several designs were selected to be fabricated and evaluated experimentally. The microfabrication technique will be used to construct the channels.

3.	Summary

- Literature review:

  - Various types of concentrating solar systems

  - Range of concentration practically being used

  - Maximum achievable concentration.

  - Cell efficiency under concentration.

  - Optimum cell efficiency.

  - PV-thermal technology.

The main goal of this literature survey is to find the behavior of the PV-cell under high concentration. First we need to find out the maximum achievable concentration and how it will affect the cell parameters.  We also need to review the methods for concentrating sunlight. With modern techniques, sunlight has been concentrated experimentally to 84,000 levels. Solar cell efficiency will increase by concentration level; however, there is an optimum concentration level for a solar cell, which depends on PV-cell parameters such as temperature, short-circuit current and series resistance.

Fig.1: Solar cell efficiency versus concentration for a single cell based on numerical calculation.

Figure 1 shows the theoretical relationship between the solar cell efficiency and the concentration of sunlight. As seen, the efficiency increases with the concentration. However, it should be mentioned that efficiency will not increase infinitely. In fact after a certain concentration (which depends on cell parameters such as temperature, short circuit current, and series resistance), the theoretical prediction does not hold anymore and a decline in the efficiency is expected. This behavior is due to power losses, mainly through series resistance. From this figure it can be concluded that increasing the concentration up to the optimum point can result in higher efficiency. However, higher concentrations require more effective cooling of PV cells to prevent any negative impact of high temperature.

- Heat load calculations:

The aim of these calculations is to assess the range of heat load that must be removed by the force-fed cooling technique. Energy balance equations were written between heat generated at the cell, electricity generated at the cell, and total energy received by the PV-cell..  Cell temperature was derived by adding efficiency and convection heat transfer equations. Sun irradiance during the time of day was also modeled by sinusoidal curve. These calculations were first done for a PV-cell without concentration to find the temperature rise in a solar cell. Based on that calculation, calculations for solar cells under different level of concentrations were done.

Fig. 2: Electricity production and heat removal by microchannel from a solar cell during a day with 500 sun concentration.

Figure 2 shows the result of a case study for a solar cell under 500 sun concentration with cell reference efficiency of 0.28% and cell temperature coefficient of 0.005 1/K during a sample day in which temperature varied between 298K and 309K. This curve shows the total heat produced at the cell and the heat that should be removed by the force-fed cooling technique.  The curve accounts for heat removal by natural convection. It can be seen that at this level of concentration natural convection cooling is not sufficient, and a more effective method of cooling is needed.

The calculations were carried out for different levels of concentration and solar cell initial parameters.

- Microfabrication:

  - Photolithography

  - Deep reactive ion etching

  - Dicing system

  - SEM system

Microfabrication, the fabrication of micrometer-sized components, is needed for the microchannels of this project. We went through a complete trial process to assess the feasibility of the techniques for the design part of the project. In this trial all the techniques, such as photolithography to transfer a geometric pattern on the silicon wafer, deep reactive ion etching to create deep, steep-sided channels in a silicon wafer, and a dicing machine to cut the wafer to small size, were examined. Finally, an SEM picture capable of producing high-resolution images of a microchannel surface was taken to check the mircochannel surfaces.

Fig. 3: SEM picture of the silicon microchannel.

Figure 3 shows an SEM picture of an experimental silicon microchannel fabricated using DRIE at the University of Maryland microfabrication lab. The depth of channels is 155 micrometers.

- Design of the microchannel:

Modeling of different designs of manifolds and microchannels in FLUENT was conducted to study the effect of various geometrical parameters and to identify the optimum design. A parametric study on the number of manifolds per centimeter, the number of channels per centimeter, the channel aspect ratio, fin thickness, channel wall thickness, and inlet and outlet dimension was performed. Other parameters, such as inlet and outlet flow temperature, heat transfer coefficient, volumetric flow rate, and pumping power, were calculated. It was found that by increasing the number of manifolds per centimeter we could reach a much more uniform temperature on the cell surface, which is one of the main concerns in designing cooling techniques for solar cells under high concentration. The results from different designs with the same initial values were compared against each other in terms of channel base temperature, required pumping power of the system, and coefficient of performance. A number of designs were selected for fabrication and were evaluated experimentally. Final results will be presented in next quarterly report.

4.	Difficulties Encountered/Overcome

- Lack of literature about the optimum solar cell efficiency under different levels of concentration.

- Lack of literature about solar cell heat load, especially under different concentration levels.

- Lack of literature on manifold designs and optimization of the manifold microchannels.

5.	Deliverables for the Next Quarter

- Prepare the first draft of a journal paper based on the literature reviewed.

- Finalize the design of microchannel and manifold.

- Prepare the mask layout for microchannel and manifold design.

- Purchase the required materials including silicon wafers.

- Continue on microfabrication of the channels and manifolds.

- Develop an appropriate packaging technique.

Appendix

Justification and Background

The abundance of solar energy in Middle Eastern countries provides significant opportunity for development of eco-friendly power generation technologies essential in the modern world. Several decades of research have produced significant knowledge and innovations in design of economically viable, silicon-based photovoltaic (PV) panels and mirrors for concentration of solar radiation and its conversion to electric power. One of the outstanding challenges in this field is the active and uniform cooling of these large-area, high heat flux solar concentrator arrays, because the conversion efficiency is heavily dependent on device temperatures and drops significantly with an increase in temperature. If an appropriate cooling technique is possible, these solar panels will become more effective and commercially viable, which could pave the way for a rapid transition of the current power generation industry towards eco-friendly alternatives for local use, increasing currently available export resources and also creating a base for future energy export technologies.

Among several techniques enabling the use of solar energy, solar photovoltaics exhibit significant potential for economic and eco-friendly process for power generation industry. After five decades of research and development, photovoltaic energy production is growing exponentially across global markets. Northern Europe and Japan currently lead in the research and commercialization of PV technology. Solar panels on the facades and roofs of commercial and residential buildings are common pictures in these countries, where solar energy is used in every aspect of utilities, including heating, cooling and lighting needs. Most of those countries have climates with high cloudiness and low intensity direct sunlight, limiting the energy conversion effect. The static PV arrays that work well with dispersed sun light have already been developed. These cells are used in the static arrays and are simple silicon-based cells with poor conversion efficiency.

Progress has been made on decreasing the cost and consumption of solar array material by using thin film PV cells. Daytime tracking of the sun by sensor-enabled drives offers significant benefit in increasing solar array effectiveness. Also, in the recent decade, works have been published on the concentration of solar radiation by parabolic mirrors and lens structures onto smaller sized solar panels, which greatly reduce the cost and increase conversion efficiency by increasing specific power. The US Department of Energy has recently reported exceeding 40% efficiency level with concentrated arrays compared to 8.5% for static arrays. The efficiency of the array increases with the level of concentration if array temperature is kept at a low constant value. The same low array cost compared to the total system cost will allow updating to current technology. The radiation concentration up to 80,000 times is theoretically possible but currently just 400 to 500 times is feasible due to high heat dissipation requirement on the PV concentrator arrays.

Approach

UMD-side participation

- Conduct extensive literature survey on PV radiation concentrators. Summarize available cooling technologies for these arrays with notes on their cost, size and other scalability issues.

- Evaluate cooling loads, taking into account recent advances in radiation concentration technologies and conversion efficiencies.

- Develop a force-fed heat exchanger prototype capable of rejection of this expected heat flux. Explore the possibility of MEMS fabrication techniques for creating micro-grooves integrated with solar panels. Also identify possible fluid choices and pumps to meet the demand.

- Conduct experimental study on force-fed-based single- and two-phase processes to determine cooling capacity.

- Based on outcome of experiments, design, fabricate, and test a complete PV converter and cooler package in the field.

- Make recommendations for a radiation concentration that is commensurate with this thermal management technique.

PI-side participation

- Provide information and symbiotic assistance to the UMD team regarding current concentrator designs, available cooling techniques and expected heat loads.

- Prepare a solar concentrator to be packaged with UMD-made heat exchanger for final testing.

- Corroborate UMD testing of the concentrator and cooling element in UAE desert conditions

- Provide contributions to the preparation of final project report and recommendations.

Two-Year Schedule

UMD-side participation

Year 1

- Literature review and summary

- Design of force-fed cooler for PV array

- Fabrication of experimental prototype and experimental loop

Year 2

- Finalized experimental setup

- Experimental results

- Recommendations for optimized PV converters with respect to developed cooling capacity

- Final report

PI-side participation

Year 1

- Input on literature review and summary

- Discussion and assistance in design of test prototype

- Concentrator design

Year 2

- Discussion and assistance in experimentation

- Concentrator fabrication or participation in fabrication

- Testing of concentrator and cooling system in UAE conditions

- Input on final report and recommendation

Key References

- Muresan, C., Menezo, C., Bennacer, R., Vaillon, R., ’ Numerical Simulation of a Vertical Solar Collector Integrated in a Building Frame : Radiation and Turbulent Natural Convection Coupling’, Heat Transfer Engineering, vol. 27(2), pp. 29-42, 2006.

- Konnttinen, P., Lund, P.D., ‘Thermal Stability and Moisture Resistance of C/Al2O3/Al solar absorber surfaces,’ Solar Energy Materials and Solar Cells, vol. 82, pp. 361-383, 2004.

- Ramanathan, K., Keane, J., Koufi, R.,’Properties of High-Efficiency CIGS Thin-Film Solar Cells,’ Proceedings of 31st IEEE Photovoltaics Specialists Conference and Exhibition, Lake Buena Vista, FL, January, 2005.

- Han, D., ‘Microscopic Mechanism of Staebler-Wronski Effect in a-Si Films and High Efficiency Solar Cells,’ Final Subcontract Report prepared under subcontract no. ADJ-1-30630-09, National Renewable Energy Laboratory, 2004.

- Bakirov, M., ‘ Photoelectric and Radiation Characteristics of Silicon Solar Cells at High Illumination Levels and Elevated Temperatures,’ Semiconductors, vol. 31(5), pp. 439-440, 1997.

Study of Condensing Flows in a Micro-scale Channel with a Micro-element Array and Visual Techniques UMD Investigators: Dr. S. Dessiatoun, Dr. A Shooshtari GRA’s: Ebrahim Al-Hajri PI Investigator(s): Dr. A. Goharzadeh Start Date: December 2006 Report Date: 1 September 2007

1.	Objective/Abstract

The proposed two-year study will investigate, by different experimental techniques, the fundamentals of the two-phase condensing flow phenomenon in a sub-millimeter microchannel. In order to understand the mechanism of the flow, local measurements of heat flux, temperature and flow velocities are necessary. The present project intends to use an optimum flow-visualization technique to measure heat flux distribution and local fluid- and vapor-phase velocities, respectively.

2.	Deliverables Scheduled for the Completed Quarter

- Continued parametric testing of condensation in minichannels with R-134a

- Tested a mini-LDV system for velocity profile measurements.

- Conducted flow visualization in minichannels with high-speed camera.

- Developed a preliminary Matlab code for high-speed image processing.

- Processing high speed of condensation in minichannel using Matlab code.

3.	Summary

Condensation Results

After completing all tests for R245fa in the previous reporting period, several of the remaining tests of R-134a (Table 1) were conducted. Some previous tests were also repeated for data repeatability verification. The test results of the study of the effect of saturation temperature on both heat transfer and pressure drop are shown in Figures 1 and 2, respectively.

Table 1: The remaining test for R-134a.

| # | Test # | Tsat | Mass Flux | Inlet Super Heat |
| --- | --- | --- | --- | --- |
| 1 | 31 | 30 C | 300 kg/m2S | 0 C |
| 2 | 36 | 30 C |  | 10 C |
| 3 | 5 |  | 300 kg/m2S | 0 C |
| 4 | 6 |  |  | 5 C |
| 5 | 7 | 50 C |  | 10 C |
| 6 | 8 |  |  | 15 C |
| 7 | 13 |  | 400 kg/m2S | 0 C |
| 8 | 14 |  | 500 kg/m2S |  |
| 9 | 19 |  | 400 kg/m2S | 10 C |
| 10 | 20 |  | 500 kg/m2S |  |
| 11 | 24 | 60 C | 200 kg/m2s | 0 C |
| 12 | 25 | 70 C |  |  |
| 13 | 29 | 60 C |  | 10 C |
| 14 | 30 | 70 C |  |  |
| 15 | 34 | 60 C |  | 0 C |
| 16 | 35 | 70 C | 300 kg/m2S |  |
| 17 | 39 | 60 C |  | 10 C |
| 18 | 40 | 70 C |  |  |

Figure 1 indicates that as the saturation temperature increases the heat transfer coefficient decreases. This trend agrees with our previous results of R-134a and R245fa; however, the values of average heat transfer coefficient are quite higher, and the values of pressure drop (Figure 2) are lower, than what was anticipated. Also, the repeated test results are not in agreement with the previous results. This difference in heat transfer and pressure drop could be the result of different methods of flow measurement. In the previous tests a micro pump with a flow rate indicator was used to set up the refrigerant flow rate and to measure the flow rate based on the gear rotation speed. At some point it was realized that actual flow rate is lower than the flow reading on the pump. From that point calorimetric flow measurement, in which flow is determined by required heat input for 100% refrigerant quality change, was used. The results will be verified further after a newly received Coriolis flow meter is installed in the heat transfer loop.

Figure 1. The effect of saturation temperature on average heat transfer coefficient for R-134a

Figure 2. The effect of saturation temperature on pressure drop for R-134-a

Visualization Tests

With the participation of PI co-investigator Dr. Afshin Goharzadeh, several visualization techniques were used for flow visualization, such as Mini-Laser Doppler Velocimetry (Mini-LDV), two different high-speed cameras, and a video recorder. As for the Mini-LDV, we were able to measure the velocity of the liquid successfully and accurately.

Mini-Laser Doppler Velocimetry

Mini-Laser Doppler Velocimetry, an integrated and portable miniature laser diagnostics system, was tested inside the micro-channel. As shown in Figure 3, the MiniLDV crosses two beams of collimated, monochromatic laser light in the microchannel containing the single-phase flow. As micron-sized liquid or solid particles entrained in the fluid pass through the intersection of two laser beams, the scattered light received from the particles fluctuates in intensity. The frequency of this fluctuation is equivalent to the Doppler shift (Fig. 4) between the incident and scattered light, and is thus proportional to the component of particle velocity, which lies in the plane of the two laser beams and is perpendicular to their bisector.

| Figure 3: Flow visualization with Mini-LDV | Figure 4: Typical Doppler Signal obtained from laser beams |
| --- | --- |

The Mini LDV was used inside the microchannel for measuring the local velocity of particles inside the liquid phase. As shown in Figure 5, the histogram of velocity represents a maximum value corresponding to the velocity of liquid particles (290 mm/s) inside the micro channel. Additionally, for two-phase flows the Doppler signals from the bubble and the particles showed a larger spectrum. Figure 6 represents a histogram of velocities for the multiphase flow (liquid-bubbles). The histogram of the velocity illustrates a larger spectrum and contains the velocity of both liquid and bubbles. Unfortunately, it is very difficult to separate these two signals.

The instantaneous local velocity of a single liquid phase was measured accurately inside the micro-channel using the Mini-LDV. However, it failed to detect the velocity of the gas (bubbles) as the flow became two-phase flow. Additionally, the Mini-LDV system doesn’t provide a complete 2D overview of the flow inside the micro-channel. Therefore, the 2D flow was also characterized using a CCD camera.

Figure 5: Histogram of the velocities for the single-phase flow (liquid flow)

Figure 6: Histogram of the velocities for the multiphase flows

Photron 1024 Ultima high speed

A Photron 1024 Ultima high speed, high resolution (resolution 1024 x 1024 and 3000 fps) camera was used to observe the flow inside the channel (Fig. 7). However, the camera’s optics were not adequate to observe the flow further inside the channel. We were only able to see the two-phase flow at the upper glass surface on the channel; the view of the flow was not very visible.

Figure 7: Flow visualization with a Photron 1024 Ultima high-speed camera

Combination of a CCD camera and a microscope

A combination of a Sony (Model XCD-X710CR) high-speed camera with a maximum 30 frame-per-second shutter speed and a microscope was also used for visualization (Fig. 8). A microscope was placed to look into the channel from the top, and a light source was directed from the bottom of the channel. The high speed camera was mounted and fixed to the microscope to record the action inside the channel. This technique gave the best results of all the techniques we tried. With this technique we were able to capture several clear videos of the two phase flow inside the channel. The videos were then used to extract single photos of bubbles passing in the flow. The entire region of interest, the liquid-bubble area, was recorded. Full-frame images of 175 x 950 pixels were acquired and transferred to a computer. The photos were then processed in an image processing code written in Matlab under the supervision of Dr. Goharzadeh to further clarify and distinguish the gas phase from the liquid phase, and to determine bubble size and velocity.

Figure 8: Flow visualization using a CCD camera combined with a microscope

Image Processing

In order to quantitatively characterize the observed states and the liquid-bubble interactions, an image processing method using Matlab software was developed. The different steps of the image processing program are illustrated in Figure 9. The colored image was first transformed to a grayscale level and filtered in order to remove noises. The intensity of the filtered grayscale image was adjusted and used to identify the position of the water-air interface.

Figure 9: Image processing using Matlab software

The original and the post-processing images, respectively, are represented in Figures 10 and 11.

Figure 10: Original image

Figure 11: Final image after image processing

Results

Several clarifications can be done to distinguish the borders of the bubble to measure the bubble size. A contour of the image can be seen in Figure 12-(a), which shows a clear border of the bubble. Since the channel width is known to be 0.4 mm, which is also the width of the bubble, the length of the bubble can be measured (L = 1.05 mm) and then the volume of the bubble can be calculated (≈ 1.176 mm3). Figure 12-(b) represents a profile of the light intensity along the x-axis in the middle of the microchannel. The intensity profile provides information about the structure and dynamic of the bubbles (length, size, position, velocity and acceleration).

(a) Contoured image of the original image

(b) Profile of the light intensity along x axis

Figure 12: Results obtained after Image processing

4.	Difficulties Encountered/Overcome

- Difficulties in the flow rate measurement using pump and calorimetry, which resulted in inaccurate outcomes. Therefore, a Coriolis flow meter was purchased to measure the flow accurately; however, the flow meter took eight weeks to arrive at our lab. Once the Coriolis flow meter was received, it was installed it in the system.  However, the device had a problem and had to be sent back to the provider for service.

- Due to the aging of the setup, the components’ failure frequency has been increasing. Also, measurement instruments’ calibration drifted from the initial calibration; therefore, recalibration of instruments is required to keep the uncertainty within +/- 15%.

- The visualization loop had an insufficient sub-cooler; therefore, a sub-cooler was designed and built to overcome the problem.

5.	Deliverables for the Next Quarter

- Finish all remaining tests for R-134a.

- Improve the Matlab code for image processing.

- Conduct a number of visualization tests and analyze the outcome.

- Test the feasibility of the Micro-PIV system for two-phase flow systems and choose the optimal system for purchasing.

- Find applications related to ADNOC interests and present results to ADNOC (Fall 2007).

- Joint conference paper and/or article.

- Final report.

Appendix

Justification and Background

With the development of new manufacturing technologies and fluid maintenance techniques, miniaturization of heat transfer systems has proven to be possible and to afford great economic benefits.  Two orders of magnitude of reduction in system weight and volume with significant reductions in cost have become feasible. Sufficient data and advanced modeling are available to characterize boiling processes in microchannels. However, such data are lacking for condensing flows in micro-scale passages and are necessary for development of predictive models and correlations in the future.

This project will be conducted in two parts. To investigate local heat transfer with precision, the first part will use the micro-fabricated element-array technique to measure local heat flux and temperature profiles.  This will enable understanding of the flow and condensation process in greater detail than traditional methods have presently allowed. In the second part, flow visualization at the micro-scale will be used to complement the heat transfer experiments to provide data on velocity profiles and flow dynamics that are unobtainable by heat transfer measurements. This combined data set will be used in future predictive models and correlations, which will pave the way for optimization of two-phase, high-performance heat transfer systems.

In the present age of miniaturization, there is a need to understand flow phenomena in compact phase-change-type micro-fluidic systems. In recent years, work has characterized the boiling phenomenon using high-speed optics, micro-heater arrays for local wall temperatures, and heat flux measurements and Particle Image Velocimetry (PIV) techniques. Those techniques significantly improve the understanding of boiling phenomenon. Similar experiments in condensation, particularly micro-array heat flux and temperature experiments combined with PIV studies can provide extremely valuable information for the understanding of the condensation phenomenon in microchannels.

Approach

UMD-side participation

- (a) Conduct an extensive literature survey for experimental studies on condensation of refrigerants in microchannels of hydraulic diameter 1 mm or less, and extract useful data for heat transfer and pressure drops. (b) Conduct a survey of literature for analytical/numerical models in microchannel condensing flows and study them. Understand inputs typically needed for predictive models. (c)  Work with PI to conduct a survey of literature and vendors for flow visualization of two-phase micro-fluidic systems.

- Based on above literature study, design prototype of a microchannel with a platinum micro-resistors array and experimental loop.

- Develop the processes for micro-array fabrication and microchannel fabrication and make necessary design changes to accommodate technical issues. Finalize experimental prototype design.

- Fabricate prototype and complete instrumentation. Fabricate experimental loop.

- Test experimental loop for various mass flow rates of a suitable refrigerant fluid at different two-phase qualities. Collect test data on local heat fluxes on channel walls, overall pressure drop, and high-speed digital video evidence.

- Work with PI to fabricate the recommended flow-visualization prototype and associated experimental loop parts.

PI-side participation

- Work with UMD to conduct an extended literature survey on the flow visualization on micro-fluidic systems focusing on multi-phase flow.

- Develop the optimum flow visualization system for multi-phase flow inside a microchannel.

- Work with UMD to recommend a design suitable for the optimum visualization technique. Develop requirements and recommendations for a flow-visualization test section that will be fabricated by UMD.

- Conduct flow visualization measurements inside the microchannel prototype designed and fabricated at UMD.

5.	Compare flow-visualization data with UMD micro-array data.

Two-Year Schedule

UMD-side participation

Year 1.

- Literature review and summary.

- Design of micro-array prototype.

- Investigation of micro-array fabrication.

- Fabrication of experimental setup.

Year 2.

- Final fabrication of micro-array prototype.

- Final fabrication of visualization prototype and loop.

- Experimentation on micro-array.

- Final report.

PI-side participation

Year 1.

- Literature review and summary.

- Development of optimum visualization setup.

Year 2.

- Experimentation on visualization setup designed and fabricated in UMD.

- Final report.

Key References

1. 	Kim, J., Benton, J., McQuillen and J, Vickerman, M., 2001,”Subcooled Pool Boiling in Microgravity and Hi-g,” Journal of Heat Transfer, vol. 123, iss. 4, pp. 620.

2. 	Lee, J., Kim, J. and Kiger, K. T., 2000, “Time and Space Resolved Heat Transfer Characteristics of Single Droplet Cooling Using Microscale Heater Arrays,” International Journal of Heat and Fluid Flow, Vol. 22, pp. 188.

3.	Begg, E., Khustalev, and D., Faghri, 1999, “Complete Condensation of Forced Convection Two-Phase Flow in a Miniature Tube,” Journal of Heat Transfer, Vol. 121, pp. 904.

4. 	Garimella, S., 2004, “Condensation Flow Mechanisms in Microchannels: Basis for Pressure Drop and Heat Transfer Models,” Heat Transfer Engineering, vol. 25, iss. 3, pp. 204.

5. 	Yang, C.Y. and R.L. Webb, 1996, “Friction Pressure Drop of R-12 in Small Hydraulic Diameter Extruded Aluminum Tubes with and without Micro-Fins,” Int. J. Heat Mass Transfer, vol. 39, iss. 4, pp. 801.

6. 	C. D. Meinhart, S. T. Wereley, J. G. Santiago, 1999, “PIV measurements of a microchannel flow” Exp. In Fluids, vol. 27, pp 414.

Sulfur Recovery from Gas Stream using Flameless and Flame Combustion Reactor UMD Investigators: Prof. Ashwani K. Gupta GRA’s: Hatem Selim and PI Investigator(s): Dr. Mohamed Sassi Student: Sami Sami Ben Rejeb Start Date: October 2006 Report Date: 30 September 2007

1.	Objective/Abstract

To obtain fundamental information on the thermal process for sulfur recovery from sour gas by conventional flame combustion and flameless combustion using numerical and experimental studies. The ultimate goal is to determine optimal operating conditions for sulfur conversion. Therefore, an experimental study of the flameless versus flame combustion process for the Claus furnace is proposed. In the study we will explore the operating conditions and the exhaust gas analysis of both flame and flameless modes of reactor operation in the process of enhanced sulfur recovery.

Specific objectives will be to provide:

- A comprehensive literature review of the existing flame combustion process for sulfur removal with special reference to sulfur chemistry.

- Near isothermal reactor conditions and how such conditions assist in the enhanced sulfur recovery process.

- CFD simulation of the flame and flameless combustion in the furnace.

- Design of a flameless combustion furnace for experimental verification of the numerical results.

- Measurements and characterization of the flameless combustion furnace using high temperature air combustion principles.

- Experiments with different sulfur content gas streams using the flame and flameless combustion furnace modes of operation.

- Determination of the product gas stream for evaluation of sulfur recovery in the process.

2.	Deliverables

Seek detailed chemistry data for higher molecular weight sulfur compounds. Identify parameters for CFD simulations using Fluent.

3.	Summary

- Determined the equilibrium chemistry using equilibrium code

- Performed detailed chemistry using chemical kinetics code.

- Performed flow dynamic simulations using Fluent code. Each code has provided its own merits and provides unique information associated with our goal to capture sulfur and to improve efficiency of the Claus process. The results obtained from the three different simulation codes are provided in the following.

4. 	Presented a technical paper at the 5th Mediterranean Combustion Symposium entitled “CFD Simulation of Combustion in the Claus Furnace of a Sulfur Recovery Plant” by M. Sassi, S. Ben Rejab and A. K. Gupta. Conference held in Monastir, Tunisia, September 10-13, 2007.

1. Equilibrium Calculations

Our objective here was is to calculate the equilibrium products’ temperature and composition in the Claus furnace under different operating conditions.  We have used the STANJAN Code to explore the influence of varying some parameters (H2S content, combustion temperature, inlet temperature, and O2 content in the air) on the sulfur recovery in the Claus furnace. The considered equilibrium species were H2S, CO2, O2, N2, H2O, SO2, S2, SO, OH, CO, H2 and NO. Variation in content of H2S in the acid gas feed streams was considered with a mixture of H2S and CO2. Oxygen enrichment and high temperature air combustion were considered as means of improvement.

1.1 Variation of H2S Content in Gas Stream

We examined the role of H2S content in the inlet sour gas when the H2S was increased from 25% to 100% in incremental steps of 5%. The evolution of the chemical equilibrium state was determined for that condition. Figure 1 shows H2S recovery as a function of inlet H2S content. The results show an increase in sulfur conversion with a decrease in CO2.

1.2. Effect of Varying Process Temperature

We examined the role of varying the reactor temperatures from 900K to 3000K on H conversion using a mixture of 50% H2S and 50% CO2 reacting with air (21% O2 and 79% N2) in the furnace. The results are shown in Figure 2, which reveals the sulfur recovery as a function of the furnace temperature.

These results clearly show that optimum sulfur recovery is obtained at a furnace temperature of around 1500K. The recovery decreases at lower and especially at higher temperatures. This narrow window of temperature is ideal for colorless high temperature air combustion (also called flameless combustion furnace), which can offer a nearly isothermal condition close to 1500K.

1.3 Effect of Varying Inlet Temperature

By keeping the gas stream (50% H2S / 50% CO2 mixture) reacting with normal air (21% O2 / 79% N2) we analyzed the role of varying the inlet temperature. The mixture is the same as that used for Figure 2.  The variation of sulfur recovery as a function of inlet temperature is shown in Figure 3.

The increase in inlet temperature decreases the sulfur recovery. Above the equilibrium temperature of 1500K the sulfur recovery decreases, as also shown in Figure 2. The equilibrium optimal temperature for sulfur recovery, above 1500K, referring to Figure 2, will decrease the H2S conversion.

1.4   Effect of Varying Oxygen Content in the Air

Finally, we varied the oxygen content in the air, starting from 21% to 100% in steps of 5%. It was allowed to react with a 50% H2S and 50% CO2 mixture with an inlet temperature equal to 300K.  Figure 4 shows the variation of sulfur recovery as a function of O2 content. Even though the oxygen enrichment was expected to increase recovery, one can notice that H2S conversion decreases due to the increase in the furnace equilibrium temperature.

1.5. CFD Simulation of Flow Field in the Furnace

## The Fluent 6.2 CFD package was used to simulate the burner of a Claus process furnace. The k-( turbulence model along with the EDC turbulence/chemistry interaction model have been used to capture the finite rate nature of the Claus equilibrium limited reaction. The thermal stage of the Claus furnace burner was studied by considering four cases of acid gas and air or oxygen combustion. Also, the exchange between fuel and oxidant injection ports was explored in addition to co-flow pre-heating. Pure oxygen into a co-flow of pre-heated 50%H2S 50%CO2 was used, which was also used for the equilibrium calculations. Figure 2 shows a very high H2S conversion of 73% obtained at a furnace temperature of 1500K.  The conversion drops sharply at both lower and higher temperatures. Therefore it is important to operate the furnace near uniform temperature of 1500 K, which can only be offered by high temperature air combustion technology, also called colorless or flameless combustion. It is important to perform CFD simulation of flame and flameless combustion in the Claus furnace to explore the optimal conditions for the highest sulfur recovery.

1.51.   CFD Simulation of The Claus Furnace

Fluent software is for simulating the fluid flow, heat and mass transfer, and a host of related phenomena involving turbulence, reactions, and multiphase flow in a flow. Therefore, it is suitable for simulating the combustion reaction in the Claus furnace.

1.52. The Geometry

Since the combustor’s configuration is symmetric, we will focus only on its half. This requires only 2D calculations (cut of the cylinder) to observe the results (see Figure 5).

A small nozzle placed at the centre of the upstream circular face-plate of the cylinder allows introducing fuel into the combustor. The ambient air enters coaxially with the fuel flow. A 2D cross-section of the geometry is shown in Figure 6.

The meshed geometry is shown below in Figure 7.

Figure 7.  The meshed geometry

We used the Standard  model. It consists of a two-equation model in which the solution of two separate transport equations allows the turbulent velocity and length scales to be independently determined. In fact the standard  model in Fluent is the workhorse of many practical engineering flow applications. Robustness, economy, and reasonable accuracy for a wide range of turbulent flows explain its popularity in industrial flow and heat transfer simulations. It is a semi-empirical model, and the derivation of the model equations relies on phenomenological considerations and empiricism.”

1.53.  CFD Results

Fluent simulation permits one to visualize the behavior of the combustion process inside the Claus furnace. Four cases were considered, as shown below in Table 1. The operating conditions for each case are listed in this table.

Table 1. The cases examined using Fluent CFD code

| Case 1 Air inlet: Temp. 300K, Vel. 0.1 m/s H2S Inlet: Temp: 300K, Vel 85 m/s | Case 2 Oxygen inlet: Temp. 300K, Vel. 100 m/s H2S Inlet: Temp: 300K, Vel. 0.1 m/s |
| --- | --- |
| Case 3 Oxygen inlet: Temp. 300K, Vel.100 m/s H2S Inlet: Temp: 300K, Vel 0.2 m/s | Case 4 Air inlet: Temp. 300K, Vel. 100 m/s H2S Inlet: Temp: 1000K, Vel. 0.66 m/s |

Case 1: The CFD results for this case are shown in Figure 8.

## Case 2: CFD results of this case are shown in Figure 9.

## Case 3: The CFD results of this case are shown in Figure 10.

Case 4: The CFD results of this case are shown in Figure 11.

The simulated four cases have been selected to explore the influence of the composition of acid gas, the composition of the oxidant, the exchange of injected gas between fuel and oxidant, and the pre-heating of the co-flow on the flame structure, and to lay grounds for the sulfur recovery process optimization through improved Claus furnace design.

## Figures 9-11 show the simulation results for the four specific cases. The jet and co-flow velocities have been selected to allow for a ratio of 2 to 1 between H2S to O2 that is required by the Claus thermal stage. This also results in a ratio of 2 to 1 between H2S and SO2 that is required by the Claus sulfur recovery reaction. Figure IV.5 shows a conventional flame of H2S burning in co-flow of ambient air featuring localized high temperatures especially in the recirculation zone and low sulfur conversion. Figure IV.6 features a flame of centrally injected oxygen in a co-flow of H2S.

The localized temperature is even higher and the sulfur recovery further decreases. Figure 11 for case 3 shows the flame structure of a central oxygen jet into a co-flow of 50%H2S 50%CO2. The localized high temperature zone is considerably reduced and the sulfur recovery is much more uniform across the burner tube. Figure 12 for case 4 shows the effect of preheating the sour gas stream. This seems to widen the high temperature zone, and it is probably important to consider injecting ambient air rather than pure oxygen in the center to improve sulfur recovery conditions.

## Although preliminary, these simulation results reflect well the conversion of H2S into sulfur (S2). They also show some improvement of conversion and capacity increase when pure oxygen is used rather than air; however this point needs further exploration. Especially the thermal field uniformity and the conversion process seem to be better when oxygen is injected into the acid gas rather than the opposite. In addition, the use of pure H2S rather than H2S/CO2 mixtures, as usually is the case, seems to yield much higher temperatures, which could drive the process toward hydrogen production if very excessive quantities of H2S are injected into the furnace.

1.6. Chemical Kinetics Simulation using Chemkin Code

In the following some simulations are presented using CHEMKIN code to determine the effect of reactor temperature and pressure on the reaction kinetics that occurs during the Claus process. The specific focus is on the sulfur chemistry.  Near 400 chemical reactions were considered. The role of reactor temperature is examined first followed by pressure. The results show good promise for colorless combustion for enhanced sulfur recovery.

1.61 Effect of Reactor Temperature

In this section we provide the effect of increase in the reactor temperature on the mole fractions of the various species and its evolutionary behavior in the reactor.

Inlet conditions

Stoichiometric inlet conditions between H2S and air are selected and given as:

Inlet conditions (H2S= 29.58%, O2= 14.79%, and N2= 55.62%)

Flow velocity= 1 cm/s

For one Kmol of the reactants, on a mass basis, this provides:

10.057 Kg.H2S (9.465 Kg. Sulfur, 0.5916 Kg. Hydrogen), 4.732 Kg. Oxygen,

and 15.573 Kg. Nitrogen. Therefore the total mass of the reactants = 30.362 Kg

Figure 12 shows the variations in SO2 mole fraction versus time at different reactor temperatures in the range of 1300 to 1800K. The effect of increase in the reactor temperature on the evolutionary behavior of SO2 mole fraction shows an increase in the reaction rate. At high temperatures one can reach the asymptotic behavior faster than at lower reactor temperatures, which is unfavorable for S2 conversion since there must be some H2S remaining to participate reaction with the SO2. In contrast, the detailed view close at the reactor entrance indicates that the reaction can reach 90% of the asymptotic value close to a time of 0.25mS. But, the higher temperatures do not always give the higher molecular weight sulfur since SO2 has to react with H2S to form S2.  The amount of SO2 must be related to the presence of H2S, otherwise sulfur dioxide will not react to form molecular sulfur.

Figure 13 shows the variations of H2S mole fraction versus time at different reactor temperatures. The effect of changing the reactor temperature on hydrogen sulfide mole shows that increasing the temperature decreases the H2S mole fraction. The results show that an increase in reactor temperature results in higher reaction rate. But, the production of S2 depends on the reaction between H2S and SO2.

Figure 14 shows the effect of reactor temperature on variations of S2 mole fraction at different distances or residence times in the reactor. An increase in reactor temperature increases the amount of molecular sulfur at temperatures close to 1600K followed by gradual decrease, as shown in the right figure of Figure 14. This suggests that the optimum temperature is between 1500K and 1600K. The equilibrium values provided are close to 1500K but the detailed calculations suggest 1600K. This will be further examined in our next quarter efforts.  The value of the calculations appears to be 1587K. The mass of the molecular sulfur obtained at this optimum temperature, according to its mole fraction, is 7.032 Kg sulfur. The S2 mole fraction increases to a peak value, and then it decreases, which is due to the weak ratio of SO2 and H2S.

Figure 15 shows the behavior of some of the major chemical species with time. The mole fraction of H2S and O2 decreases with time, since the components are inter-related. However, SO2 mole fraction increases due to the reaction between O2 and H2S. Moreover, S2 mole fraction increases due to the reaction between SO2 and H2S. Also, one can see close a relation between SO2 and S2 mole fraction formation, since SO2 is responsible for the molecular sulfur formation.

1.62 Effect of Reactor Pressure

The effect of reactor pressure (from 1 to 5 bars) was examined to determine its role on the sulfur chemistry. The reactor temperature was held here at 1600K. Figure 17 shows the variations of S2 mole fraction versus time at different reactor pressures. The results show that an increase in the reactor pressure decreases the S2 sulfur mole fraction. This is because of a decrease in the dissociation rate of the hydrogen sulfide with an increase in pressure.

Figure 12. Effect of reactor temperature on SO2 mole fraction.

Figure 13. Effect of reactor temperature on H2S mole fraction.

Figure 14. Effect of reactor temperature on S2 mole fraction.

Figure 15. Evolutionary behavior of some of the major species behavior with time.

Figure 16. Effect of reactor pressure on S2 mole fraction.

4.	Difficulties Encountered/Overcome

None.

5.	Deliverables for the Next Quarter

In the follow-up of this work, we propose to further explore the flame and flameless combustion in the Claus furnace using the CFD code Fluent. Inclusion of more detailed chemistry through the use of the EDC model for turbulence/chemistry interaction, and some other modeling parameters for flameless combustion that have lately appeared in the literature will be used in the next part of this work toward our master thesis.

The kinetics results have shown that although the initial chemical reaction is relatively fast (of the order of few milli-seconds), the time to complete the overall reaction is relatively long (of the order of several seconds).  This then means that equilibrium is reached in a relatively long time. The practical implication of this is long residence in the reactor. We will explore several strategies to identify critical reactions involved that are rate limiting or very fast using Chemkin code in order to enhance our understanding of the process with the detailed chemistry. The goal here is to determine the various mechanistic pathways associated with the fast chemical reactions versus the slow chemical reactions.  Based on these calculations, the preliminary test matrix as well as the design parameters for the experimental facility will be developed.

Appendix

Justification and Background

Hydrogen sulfide is present in numerous gaseous waste streams from natural gas plants, oil refineries, and wastewater treatment plants, among other processes. These streams usually also contain carbon dioxide, water vapor, trace quantities of hydrocarbons, sulfur, and ammonia. Waste gases with ammonia are called sour gases, while those without ammonia are called acid gases. Sulfur must be recovered from these waste streams before flaring them. Sulfur recovery from sour or acid gas typically involves application of the well-known Claus process, using the reaction between hydrogen sulfide and sulfur dioxide (produced at the Claus process furnace from the combustion of H2S with air and/or oxygen), yielding elemental sulfur and water vapor: 2H2S(g) + SO2(g) = (3/n) Sn(g) + 2H2O(g) with DHr= -108 kJ/mol. Therefore, higher conversions for this exothermic, equilibrium-limited reaction call for low temperatures, which lead to low reaction rates that dictate the use of a catalyst. The catalytic conversion is usually carried out in a multistage, fixed-bed, adsorptive reactor process, which counteracts the severe equilibrium limitations at high conversions. This technology process can convert about 96% to 97% of the influent sulfur in H2S to S. However, higher removal requires critical examination of the process and use of a near isothermal reactor, since the conversion is critically dependent upon the exothermic and endothermic conditions of the reactions.

Flameless combustion has been shown to provide uniform thermal field in the reactor so that the reactor temperature is near uniform. Reactor size can also be reduced, and combustion-generated pollutants emissions can be reduced by up to 50%.  Energy efficiency can be increased by up to 30%. The application of this technology appears to offer great advantages for the processes under consideration. The UAE, which pumps about 2.4 million bpd of crude oil, is also home to the world’s fifth biggest gas reserves at about 200 trillion cubic feet. Abu Dhabi Gas Industries (GASCO), an operating company of the Abu Dhabi National Oil Company (ADNOC), is leading a drive to boost gas production in the UAE from five to seven billion cubic feet per day. This calls for sulfur recovery capacity of over 3,000 metric tons per day with the associated SOx and NOx emissions. Therefore, the adoption and further development of flameless combustion technology for sulfur recovery among other commercial and industrial heating processes is expected to be crucial and beneficial, both economically and environmentally.

The conventional sulfur recovery process is based upon the withdrawal of sulfur by in situ condensation within the reactor. The selective removal of water should, however, be a far more effective technique, as its effect on the equilibrium composition in the mass action equation is much greater. The in situ combination of the heterogeneously catalyzed Claus reaction and an adsorptive water separation seems especially promising, as both reaction and adsorption exhibit similar kinetics, and pressure can be adapted to the needs of the adsorptive separation. Such an adsorptive reactor will lead to almost complete conversion as long as the adsorption capacity is not exhausted. There are numerous possibilities for implementing these two functions, ranging from fixed-beds with homogeneous catalyst/adsorbent mixtures to spatially structured distributions or even fluidized beds. Most of the previous studies have concentrated on the Claus catalytic conversion reactors and the TGTU. However, some previous studies have identified the Claus furnace as one of the most important yet least understood parts of the modified Claus process. The furnace is where the combustion reaction and the initial sulfur conversion (through an endothermic gaseous reaction) take place.  It is also where the SO2 required by the downstream catalytic stages is produced and the contaminants (such as ammonia and BTX (benzene, toluene, xylene) are supposedly destroyed. The main two reactions in the Claus furnace are: H2S + 3/2 O2 = SO2 + H2O, with DHr= -518 kJ/mol, and 2H2S + SO2 = 3/2 S2 + 2H2O, with DHr= +47 kJ/mol. This last endothermic reaction is responsible for up to 67% conversion of the sulfur at about 1200 C. Moreover, many side reactions take place in the furnace; these side reactions reduce sulfur recovery and/or produce unwanted components that end up as ambient pollutant emissions. Therefore, it would be useful to combine the endothermic and exothermic process using an isothermal reactor offered by flameless oxidation combustion.

Approach

Critical review

We propose to conduct a critical review of the various approaches used for sulfur removal from the sour gas. The emphasis here will be on sulfur chemistry with due consideration to the fate of ammonia. Following the review, an experimental and a CFD numerical study of the flameless oxidation of the fuel will be conducted as follows:

CFD simulation

A numerical simulation study of the flame under normal and flameless oxidation of fuels in the furnace will be conducted using the available codes. Global features of the flow and thermal behavior will be obtained using the Fluent CFD and Chemkin computer codes. These codes provide detailed simulation of the flow, thermal and chemical behaviors (i.e., detailed chemistry) in the reactor flow using gas-phase reactants. The sulfur in the fuel is in gas phase, so we will be able to simulate and monitor the fate of sulfur during various stages of endothermic and exothermic reactions and over a range of temperature regimes, including those covered in the Claus furnace process. The simulation results will also guide the final design of the flameless furnace. The simulations will also help assist in the experimental program for data validation with the eventual goal of implementing the process for sulfur removal.

Experimental study

An experimental study of the flameless vs. normal flame combustion process for the conditions examined in the theoretical study, including that of Claus furnace, will be conducted. We will explore the operating conditions and the exhaust gas analysis under conditions of both flame and flameless modes to determine the extent of sulfur conversion under the two conditions over the temperatures that can simulate endothermic and exothermic conditions in the Claus furnace. The goal is to seek conditions that yield the highest sulfur recovery from a process. To some extent, these conditions will be based on the composition of the acid/sour gas, from sulfur-rich (>50% H2S) to lean (<20%H2S). It is expected that our fundamental information will contribute to the eventual design guidelines of an advanced sulfur recovery process furnace operating under flameless combustion mode.

Two-Year Schedule

Year 1: (Performing institution)

- Perform detailed literature review and document in a report to the PI (conducted by PI and UMD).

- Perform numerical simulation of the flow and thermal behavior using Fluent code (PI).

- Incorporate sulfur chemistry into the code for capturing the fate of sulfur in the process (UMD).

- Provide preliminary simulations on the chemistry and mechanistic pathways for sulfur and other key transformation and pathways that are considered critical for sulfur recovery (UMD).

- Provide preliminary design considerations for the flameless oxidation and normal flame conditions, and recommend how the conditions can be used to simulate exothermic and endothermic behavior (PI and UMD).

Year 2:

- Perform detailed simulations using the Fluent (PI) and Chemkin (UMD) computer codes with special emphasis on the role of uniform and controlled thermal fields in the reactor on sulfur recovery.

- Assemble a flameless oxidation furnace reactor that can also operate in the normal combustion mode (PI and UMD).

- Conduct experiments using flameless and flame combustion over a range of dynamic conditions determined in the numerical study (UMD).

- Provide a preliminary design of the reactor for enhanced sulfur recovery. Determine the extent of sulfur recovery from different concentrations in the gas stream (PI and UMD).

Key References

1. 	Elsner, M. P., Menge M., Müller, C. and Agar, D. W.: The Claus process: teaching an old dog new tricks, Catalysis Today, 79–80, 2003. pp. 487–494.

2. 	El-Bishtawi, R. and  Haimour, N.: Claus recycle with double combustion process,  Fuel Processing Technology 86, 2004. pp. 245– 260.

3. 	Cerru, F.G., Kronenburg, A. and Lindstedt, R.P.: Systematically reduced chemical mechanisms for sulfur oxidation and pyrolysis, Combustion and Flame, 146, 2006. pp. 437–455. 4. H. Borsboom, P. van Nisselroy, The EUROCLAUS® Process, Achema 2000, Frankfurt am Main, 2000.

4. 	Tsuji, H., Gupta, A. K., Hasegawa, T., Katsuki, M., Kishimoto, K., and Morita, M.: High Temperature Air Combustion: from energy conservation to pollution reduction, CRC Press, Boca Raton, FL, 2003.

Development and Delivery of Course Material for Engineering Project Management Courses UMD Investigators: Ali Haghani & John Cable GRA’s: None PI Investigator(s): None Start Date: October 2006 Report Date: 30 September 2007

1.	Objective

Develop and deliver course material for an Engineering Project Management program at PI, develop and deliver a short course for GASCO, and perform a feasibility study of establishing a graduate program in Engineering Project Management at PI.

2.	Deliverables

Draft survey for use in collecting market feedback on establishing a graduate project management program at PI.

3.	Summary

UMD/PM delivered a draft survey to PI 24 July 2007. PI requested two additional undergraduate courses from the Project Management Program to be delivered next spring; ENCE 422 Project Cost Accounting & Economics + ENCE423 Project Planning, Scheduling & Control.

4.	Difficulties Encountered/Overcome

None

5.	Deliverables for the Next Quarter

We will be working on preparing the course material for the two requested courses listed above.

Appendix

Justification and Background

PI’s need to develop a graduate program in Engineering Project Management.

Approach

The material for all of these courses will be derived from the course material for the engineering project management courses at the University of Maryland, supplemented by additional material developed by the CEE faculty as needed.  After delivery of the material, the feasibility study will entail visiting PI, interviewing the PI faculty who are interested in the program, and assessing the facilities and human resources needs.

Two-Year Schedule

- Develop and deliver a one-week short course in project management for GASCO: January 2007 – delivered in Abu Dhabi in January.

- Develop and deliver materials for a semester-ling course in project management: September 2007 – hand delivered in Abu Dhabi in January 2007 (7 months early)

- Develop and deliver course materials for design and construction contract law course. – delivered slides only for ENCE 421 in January with the rest due in September 2007. Delivered balance of materials in June 2007. (3 months early)

- Develop and deliver materials for two additional semester-long courses in project management at PI: The third and fourth courses have just recently been selected and will be delivered in early 2008.

Key References

N/A

Solid Oxide Fuel Cells for CO2 Capture and Enhanced Oil Recovery UMD Investigators: Prof. Greg Jackson Senior Research Associates: Dr. Serguei Dessaitoun GRA’s: Paul Jawlik and Siddharth Patel PI Investigator(s): Prof. Valerie Eveloy, Prof. Ali Almansoori Start Date: October 2006 Report Date: 30 September 2007

1.	Objective/Abstract

This multi-faceted project will investigate the feasibility of implementing advanced solid oxide fuel cell (SOFC) technology for producing power from oil well off-gases while providing a source of concentrated CO2 for sequestration and enhanced oil recovery.  This project will explore fundamental issues in identifying preferred material combinations for durable SOFC anode operation with typical oil well off-gas composition. Along with these fundamental issues, multi-scale modeling will include detailed models for assessing SOFC membrane electrode assembly architectures for optimal operation with hydrocarbons, and higher-level system models for evaluating integrated systems with all accessory equipment within the context of oil well operation.  System models will assess the economic viability of such a system and thereby determine technology performance requirements for successful implementation of SOFC-based systems for enhanced oil recovery with CO2 injection.

2.	Deliverables

Task 1:  Experimental study of SOFC MEA’s for hydrocarbons

- Finalize fabrication protocol for high-power density cells with thin electrolytes and metal-doped CeO2 anodes.

- Complete preliminary UMD studies comparing operation of SOFC’s with syngas and with humidified and dry hydrocarbons (no larger than n-C4H10).

- Complete purchase and acquisition of supplies and equipment for PI SOFC test facility and begin assembly of test rig.

Task 2: Numerical modeling for design of SOFC architectures

- Complete development of hydrocarbon electrochemical models (CeO2 and Ni) and study optimal anode architectures for hydrocarbons with 1-D through-the-MEA models.

- Develop a down-the-channel model at UMD and begin study of SOFC operation with high fuel utilization and various inlet fuel compositions.

Task 3: System level analysis of integrated SOFC plants

- Begin development of SOFC and balance of plant models in Aspen or Hisys at PI.

Task 4: Identification of multi-university research team for SOFC’s in the petroleum industry.

- No activities are planned for this task until after some of the above accomplishments are achieved in Fall 2007.

3.	Summary

During the past quarter, the UMD/PI team has moved toward achieving the key milestones for Tasks 1 and 2.  Some unforeseen challenges in the SOFC fabrication have resulted in some delays in achieving all objectives in Task 1, but the progress in this past quarter as discussed below indicates that the delayed milestones should be reached in the final quarter of this year.  Prof. Almansoori visited UMD during this quarter for multiple days and a plan was discussed for the PI to begin moving forward on Task 3 as discussed below. Finally the PI and UMD teams worked together to develop a more detailed test plan for the PI’s portion of Task 1 to guide the final procurement of test equipment for the PI SOFC test facility.

Task 1:  Experimental study of SOFC MEA’s for hydrocarbons

UMD has continued to refine the protocol for developing high-power density cells.  During the past quarter, Paul Jawlik has developed multiple methods for producing anode-supported membrane electrode assemblies with very thin electrolytes (10-15 µm thick).  These protocols, as discussed below, have been used to make SOFC’s up to 3 cm in diameter, and some SOFC’s with approximately 4 cm2 active area have been tested for H2 and syngas mixtures that may be derived from light hydrocarbons.  The protocol for fabrication is summarized here by discussing the major components.  To date all anode-supported cells fabricated and tested have used Ni as the catalyst, and although significant progress has been made on making anode supports with Cu/CeO2 anode catalysts, some further progress is needed as discussed below.

Protocols for Fabrication of Thin Electrolyte Solid Oxide Fuel Cells:

Ni/YSZ Porous Anode Supports with Thin Electrolytes:

The Ni/YSZ porous anode and dense YSZ thin electrolyte have been fabricated using ceramic tapes purchased from Electroscience, King of Prussia, PA.  Three Ni/YSZ anode tapes (each being a 180 µm thick porous composite of NiO and YSZ) are pressed together with a 15 µm thick electrolyte tape of dense YSZ.  The cold-press lasts for 20 minutes at room temperature and 10 metric tons of pressure for a 3 cm diameter cell.  Best adhesion between electrolyte and anode support was achieved when the electrolyte tape is pressed concurrently with the Ni-YSZ tapes.  The anode-electrolyte structure is then heated in air over a well-defined schedule (lasting 1.5 days) to 1450ºC and held there for 3 hours before slowly cooling to room temperature (over a 1.0 day period).

Cu/CeO2/YSZ Anode Supports with Thin Electrolytes

The Cu/CeO2/YSZ anodes are fabricated by first mixing 35% wt. graphite pore former with 65% wt. YSZ powder.  The powder is suspended in ethanol and ball milled for a minimum of 24 hours.  Afterwards, the suspension is dried and passed through a 90 µm sieve in order to remove particle agglomerates.  The powder is then pressed for 20 minutes at 10 tons to form a disk approximately 3.0 cm in diameter and 1 mm thick.  After the powder is pressed, in some cases, a higher density interlayer with only 20% wt graphite pore formers with YSZ are drop-coated onto one side of the anode support in order to form a denser more active electrocatalyst region for the anode and to improve adhesion between the anode and the dense electrolyte.  An SEM image of an anode / interlayer / electrolyte cross-section is shown in Figure 1   After pressing, the anode discs (with or without interlayters) are heated to 800 ºC to burn out the graphite pore former, creating a porous YSZ matrix with porosities of 50% or more.

For the thin electrolyte, YSZ, polyvinyl butyral (PVB), and polyethylene glycol 600 (PEG 600) are mixed in iso-propanol and sonicated for 20 minutes to half an hour.  The appropriate volume of the YSZ suspension is then drop-coated (similar to another reference [1]) onto the surface of the porous YSZ anode supports and allowed to dry in air.  The porous anode – dense electrolyte structure is then heated to 1450 ºC in a similar manner as discussed above in the Ni/YSZ to densify the electrolyte as well as the porous anode structure.

Impregnation to the anode support of the active CeO2 and the conductive Cu occurs after the cathode sintering discussed below.  This is necessary as the temperatures required for cathode sintering exceed the melting point of copper and also have been shown to reduce the catalytic activity of CeO2.

Cerium (III) nitrate hexa-hydrate is mixed with water and methanol and sonicated for 20 minutes.  The porous anode matrix is impregnated with the solution until saturated.  The cell is then heated to 500 ºC to remove the nitrates (leaving behind cupric oxide) followed by further impregnation with the cerium solution.  This process is repeated several times in order to get the requisite amount of ceria into the cell.  A solution of cupric nitrate is generated and added to the cell in an analogous manner.  Again, it is required to heat the cell up to 500 ºC several times in order to remove the nitrate elements and create room for additional solution.

Figure 1 – An SEM cross-sectional view of the interfaces between the YSZ anode support, the anode interlayer, and the dense YSZ electrolyte

LSM/YSZ Composite Cathode:

For both types of anode supports, LSM-YSZ composite cathodes were implemented.  LSM-YSZ paste purchased from Fuel Cell Materials has been used for the cathode.  For safety purposes the MEA structure must be sealed around the anode to avoid leakage of fuel into the furnace in which the cell is tested.  To assist in sealing around the porous anode support, cathodes are made smaller and thereby determine the effective active area of the entire MEA.  For the cathode fabrication, Kapton tape (30 µm thick) with a 1.3 cm diameter hole is used as a mask for applying the cathode on the center of the exposed electrolyte plane.  The LSM-YSZ paste is spread evenly over the mask.  The paste is heat dried and the mask removed.  The cathode remaining behind is approximately 30 µm thick.  The cell is then heated in a controlled manner to 1300 ºC over a 1.5 day period.  Heating schedules will be provided to the PI as needed for any cell fabrication that may occur there.

Current Collection and Miscellaneous Preparation:

A gold wire is spot-welded to a gold mesh.  The mesh is attached to the anode with gold paste.  For the cathode side, a platinum wire is spot welded to a platinum mesh and attached to the electrode with platinum paste.  The cell is then attached to an alumina tube of similar diameter using a ceramic paste.  The tube assembly is placed inside a furnace and heated to 800ºC.  The anode side of the cell is then exposed to hydrogen for several hours to reduce either the cupric oxide to copper for the Cu/CeO2 anodes or the NiO to nickel for the Ni anodes.

These fabrication techniques are adaptations and modifications of techniques identified in the literature, and the development of a reliable fabrication protocol for both types of cells has been significantly more challenging than expected.  However, these protocols are now producing reliable structures with the lone exception that the Cu/CeO2 impregnation has not been optimized. Paul Jawlik is currently working to finalize this protocol, which will be shared with the PI upon completion.

Testing of the Anode-Supported Thin Electrolyte Cells

Because of the outstanding issues with the Cu/CeO2 impregnation, tests of these cells both with syngas and direct hydrocarbon feeds have not yet begun.  Although tests on sputter-deposited CeO2 anodes have been ongoing at UMD, these cells are for kinetic model development and do-not provide high current density performance as desired on this program.  Thus, testing to date has focused on the Ni/YSZ anode-supported cells.

The Ni/YSZ anode-supported, thin-electrolyte cells have been tested for a range of conditions primarily with H2 (dry and humidified) and with syngas mixtures.  Because of experiences with significant carbon deposition using porous Ni/YSZ anodes as reported in the previous quarterly report for electrolyte-supported cells, no tests with hydrocarbon anode feeds were performed with these cells.  However, it is desired from an overall system standpoint to compare the effectiveness of using such Ni/YSZ anodes in conjunction with an external steam reformer of the potential hydrocarbon feeds with the effectiveness of feeding the light hydrocarbons directly to a Cu/CeO2/YSZ anode that would allow for internal reforming of oxidation within the SOFC itself.  Thus, the testing of the Ni/YSZ cells on a variety of syngas feeds will be useful to provide a benchmark for assessing the effect of direct hydrocarbon feeds into the ceria-based anodes.

To date the Ni/YSZ anode-supported, thin-electrolyte cells that have been tested have had the following MEA architecture:

- Anode – 500 μm thick Ni/YSZ cermet with porosity ~ 40-50% (no interlayer at the electrolyte interface)

- Electrolyte – 15 μm thick dense YSZ electrolyte

- Cathode – 30 μm thick LSM/YSZ composite (uncertain porosity to date and without interlayer at the electrolyte interface)

- Anode current collector – 325 mesh gold mesh with porous gold paste to attach on outer surface of anode

- Cathode current collector – 325 mesh platinum mesh with porous platinum past to attach on outer surface of the cathode.

Figure 1 shows an example of data obtained from these tests and indicates that performance is still not as high as expected even for relatively high H2 partial pressures (0.67 bars).  The UMD team has set a desired performance of close to 0.5 W/cm2 at 800 °C for syngas and H2, and the current anode-supported electrolyte cells are producing currents that are off in power densities by over a factor of 3 at the set temperature.  Analyses of the cell performance, impedance data (not shown), and post-mortem material analysis suggest that the current collectors are not maintaining good contact over the entire area of the cell, causing the effective area of the cell to be reduced and thereby giving the low current and power densities.  Some alternative current collectors using silver mesh and pastes are being considered for follow-on studies.  In addition, the effectiveness of higher density Ni/YSZ interlayers is being considered.  Such interlayers have been fabricated with thin electrolytes with the intent that they may reduce activation overpotentials in the anode and thereby provide higher power densities. But as of yet, MEA architectures with these anode/electrolyte interlayers have not been tested.

Figure 2 – I*Rbulk corrected voltage and associated power density vs. current density curves for anode-supported thin-electrolyte cells running at a range of temperature on 67% H2 on the anode side and dry air on the cathode side, both at 1.0 bar.

Preparations for Testing Facility at the PI

While the participants at the PI continued to work on procuring hardware for a test facility, UMD worked with them to further develop and detail the experimental test plan.  The PI and UMD collaborators proceeded to develop a more detailed test plan with specific flow rates and operating conditions for the various light hydrocarbon and syngas conditions to be tested.  It was important, in developing the test plan for the button cells, that a range of simulated fuel conversions be performed in order to facilitate model validation for down-the-channel conditions where a significant fraction of the fuel stream has been converted to CO2 and H2O.  The proposed test plan is detailed in Appendix A and is the working document going forward for the testing program for the remainder of the program.

Task 2: Numerical modeling for design of SOFC architectures

The model development has continued at UMD with improved electrochemical models being incorporated into the through-the-MEA 1-D models.  The chemical mechanism part of the model includes adaptation/modification of a methane-oxidation model for Ni-based anodes published in 2006 [2]. The UMD team has combined this Ni surface mechanism with some fitted kinetic models of H2 and CO charge transfer reactions at the SOFC three-phase boundary.   These charge transfer reactions were derived from fitting patterned anode studies of both H2 [3] and more recently of CO, to be published in a Ph.D. dissertation by UMD student Bahman Habibzadeh this fall.   The kinetic model improvements are currently being extended to higher hydrocarbons by exploring models for rapid surface-catalyzed oxidative decomposition of butane into C1 surface species, which are in the existing kinetic model for Ni [2].  The model for CeO2 based chemistry is still under development with a synergistic program funded by the U.S. Office of Naval Research.

Continued efforts have been ongoing to look at the effects of anode microstructure on activation and so-called transport overpotentials to determine optimal structures for high-power densities with anode-supported structures.  The transport models in the porous-media anode rely on the dusty-gas model adaptation of the Stefan-Maxwell transport equations.  This is coupled to the anode surface chemistry models and bulk-phase ionic transport models in the electrolyte, which are described in a paper to be published by our group [4] and to be presented this October at the semi-annual Electrochemical Society Meeting.  This paper will be provided to the PI upon completion later this month.  Figure 3 shows a comparison of our latest model versions with experimental data from Zhao & Virkar [5], which explored different anode microstructures with humidified H2 as the anode fuel.  This baseline data was used to validate model parameters for the Ni/YSZ anode microstructure as well as the LSM/YSZ composite cathode, and the YSZ electrolyte.  Because our MEA fabrication techniques follow to some extent the methods used in Zhao & Virkar, the optimization of the various electrolyte and electrocatalyst parameters to fit this data provides a basis for analyzing our cells when they achieve the desired performance.

Figure 3 -- Polarization and power density curves at 800 °C for co-varying anode support porosity (Phi), anode support tortuosity, and thickness of electrochemically active region near the electrolyte (du).  Symbols represent experimental data from Zhao & Virkar [4], while solid lines represent simulation results.  Filled symbols are for polarization curves, while empty symbols are for power density curves.

The model has been used to explore the expected performance of the Ni/YSZ anode-supported SOFC’s with syngas feeds consistent with light-hydrocarbon steam reformer effluents.  The syngas feeds were determined from equilibrium calculations for a reformer feed of a hydrocarbon with an H: C ratio of 2.2 and with a steam to carbon ratio of 2.5.  The reformer outlet at 700 °C  gives a syngas feed with approximately 50% H2, 12% CO, 28% H2O and 10% CO2 (all mole percentages).  This feed was tested with the Ni/YSZ anode model, which included the detailed surface and electrochemistry models discussed above and the transport model with the fitted physical parameters at a porosity of 45%, a tortuosity of 2.9, and an anode support thickness of 500 and 1000 µm.    In order to explore how H2 and CO conversion would impact cell current densities, the model was run for a range of current densities assuming conversions equivalent to 33%, 60%, and 84%, which would represent different locations in a down-the-channel 2-D model that is currently being developed by the UMD team.

Figure 4 shows voltage and power density vs. current density plots for the range of conversions as discussed in the occasion.  These cases are for a relatively thick Ni/YSZ anode support of 1000 µm with a porosity of 45% and a tortuosity of 2.9.  The electrochemically active region was only 10 µm.   The thicker anode support would be indicative of a larger SOFC where more structural integrity might be necessary.  The results indicate that up to the 60% conversion, power densities at a fixed voltages in typical SOFC operating regimes (0.65 – 0.5 V) only drop by 30%.  However, at the 84% conversion, power density drops off dramatically, particularly at the lower voltages, because of the low concentration of reactants and the associated increases in both transport and activation overpotentials.  Results from the 1-D model provide a basis for assessing how much conversion can be tolerated for a constant voltage cell operation before significant penalties would be incurred at the downstream end of the cell.  These results will be borne out further in the next quarter with the testing of the 2-D down-the-channel model.

Figure 4 – Simulation results of a through-the-MEA model of a Ni/YSZ anode-supported cell with a 1000 µm thick anode support, a 10 µm thick YSZ electrolyte, and a 50 µm thick LSM/YSZ cathode.  Operating conditions are 800 °C and for a range of syngas feeds at different H2 + CO conversion as discussed in the text.

Task 3: System level analysis of integrated SOFC plants

The UMD team and Prof. Almansoori from the PI met at UMD and spent some time discussing system level model development to look at the SOFC models within the context of an entire plant that can include oil-well off-gas extraction, optional light-gas steam reforming, possible CO2 capture, and remaining balance of plant.  This was a follow-on to discussions between Prof. Jackson and Prof. Eveloy at the PI regarding the use of Aspen/Hisys in previous SOFC system-level modeling at the University of Waterloo.  In response to this, UMD has decided for this project and other PI collaboration to purchase the Aspen/Hisys Process Modeling package and to adapt the SOFC models developed at UMD to work as a way to form a look-up table for an SOFC model within that framework.  Look-up tables for syngas operation of Ni/YSZ anode SOFC’s are being developed for a range of conditions using the models described in Task 2.  The Aspen software at UMD should arrive early next month.

4.	Difficulties Encountered/Overcome

The delays in finalizing the fabrication of anode supported cells (Task 1) has delayed achieving all of the objectives in this program, as it has led to a delay not only in achieving the experimental objectives but also in providing the data needed to validate electrochemical and surface chemistry models for the CeO2-based anodes in Task 2.  With one final fabrication issue, achieving reliable impregnation of the anodes with both a conductive metal and the hydrocarbon-tolerant CeO2 catalyst, the fabrication protocol has been successfully identified.  The protocol in this report serves as the record for how some the other issues were overcome.

The other delay/difficulty has been in the development of the down-the-channel SOFC model.  This delay is currently being addressed with the hiring of a new student Siddharth Patel, who has fuel cell modeling experience.  He has rapidly gotten up to speed with the through-the-MEA models developed by our group and is beginning to move quickly toward the adaptation of this model into a down-the-SOFC model, which will be available for the PI to use some time in the upcoming quarter in conjunction with their modeling efforts.

5.	Deliverables for the Next Quarter

In the upcoming quarter, the following activities are expected for Tasks 1-3, and some discussions will begin concerning Task 4 as the next phase of this collaboration is being discussed.

Task 1:  Experimental study of SOFC MEA’s for hydrocarbons

- Finalize Cu/CeO2 anode fabrication protocol and begin testing with butane feeds as well as syngas feeds

- Use experimental results to validate models for Cu/CeO2 anode models for Task 2.

Task 2: Numerical modeling for design of SOFC architectures

- Complete development of hydrocarbon electrochemical models for CeO2 and study optimal anode architectures for hydrocarbons with 1-D through-the-MEA models

- Finish the down-the-channel model at UMD and pass this along to colleagues at PI to implement in their system level analysis in Task 3.

Task 3: System level analysis of integrated SOFC plants

- Initiate the development of the steam reformer, carbon capture, and balance of plant models in Aspen or Hisys at PI and UMD.

Task 4: Identification of multi-university research team for SOFC’s in the petroleum industry.

- Discussion will begin with the PI on how to broaden this effort to include other partners on this project.  To this end, Colorado School of Mines is a possible partner and it is believed that an industrial partner may be considered to look at some of the challenges with exploring a demonstration pilot project depending on the interest of ADNOC.

Appendix A

Experimental Test Plan for Q4-Q8 of EERC Project

Solid Oxide Fuel Cells for CO2 Capture and Enhanced Oil Recovery

P.I.’s Greg Jackson (UMD), Valerie Eveloy (PI), Ali Almansoori (PI)

Grad Students: Paul Jawlik (UMD), Siddharth Patel (UMD)

Background

The experiments performed at UMD to date are summarized in an earlier section of this report.  Before Q3, few experiments were performed on electrolyte-supported cells.  Most UMD experimental efforts have focused on cell fabrication, including material issues for thin electrolytes.  Humidified hydrogen tests have been performed recently and H2 + CO tests have commenced on Ni/YSZ anodes without a functional layer (Anode 1A).

MEA Architectures for Testing

Anode-supported cells fabricated at UMD will be tested with the following electrolyte, anode and cathode.

Electrolyte – 10-15 μm thick dense YSZ either formulated from a tape.  Diameter of cells characterized at UMD will be determined by the outer diameter of the UMD anode exhaust tube.  Preparation and sintering will follow the protocol discussed in an earlier section of this report.

Cathode – 30 μm thick LSM/YSZ composite cathodes (50% each with uncertain porosity) from Fuel Cell Materials paste.  For cells tested at UMD, cathode diameter will be determined by the inner diameter of anode exhaust tube.  Cathode fabrication and sintering will follow protocol outlined in an earlier section of this report.  Cathode current collector used at UMD for testing will be silver mesh cut to cathode size and pasted with porous silver on the outer surface of the cathode.  At least in a first phase, PI plans to use cathode of diameters maximum 15 mm and a gold mesh on the cathode side. PI may adopt silver if satisfactory results are obtained at UMD in Q4.

Anodes – Anode structure will be varied in order to test impact of electrocatalyst composition and functional layer microstructure on performance.  For cells tested at UMD, all anode diameters will be set by the outer diameter of the anode exhaust tube.  Anodes tested at UMD will be connected with a silver mesh pasted with a porous silver to the outer surface of the anode support.  At least in a first phase, PI plans to use 1 inch diameter anode supports, and a platinum mesh on the anode side. PI may adopt silver if satisfactory results are obtained at UMD in Q4.

(Anode 1A) ~500 μm thick Ni/YSZ porous anodes (~50% each with porosity of ~50%) fabricated from ceramic tapes from Electroscience (3 stacked 180 μm thick tapes made of porous composite of NiO and YSZ).  Fabrication of these cells will follow the protocol in an earlier section of this report.

(Anode 1B) Same as Anode 1A but with additional 20 μm thick Ni/YSZ functional layer next to the electrolyte and with reduced porosity (25%).  This layer will be fabricated by drop-coating NiO/YSZ solutions and carbon-based pore formers

(Anode 2A) ~500 μm thick Cu/CeO2/YSZ anodes with weight % to be determined in Quarter #4.

(Anode 2B)  Same as Anode 2A but with 20 μm thick Cu/CeO2/YSZ functional layer next to electrolyte and with reduced porosity.

(Anode 3A) ~500 μm thick Au/CeO2/YSZ anodes with weight percents to be determined and reported in Quarter #4.  This anode fabrication will largely follow that of Anode 2A.

Operational Conditions for Testing

Cathode flow composition and rates – All cells will be tested with air flowing on the cathode side at atmospheric pressure and flow rates of at least 150 ccm per cm2 of cathode.  The cathode flows do not need to be sealed, but UMD found that for their test fixture design and airflow rates, air should be blown at the cathodes with a feed tube placed on the order of 1-2 cm’s away from the cathode outer surface.  However, this guideline may not apply to other fixture designs and airflow rates.  Cathodic airflow rates may be increased to partly overcome transport limitations and potential sealing issues.

Anode fuels and flow rates – Anode flow rates will depend on fuel composition.  Anode flows will be at atmospheric pressure and flow rates of fuels for 0% conversion will be based on these guidelines:

H2 + CO at any composition:		total 70 sccm per cm2 of cathode

CH4: 					35 sccm per cm2 of cathode

C3H8 				 	14 sccm per cm2 of cathode

C4H10 					10 sccm per cm2 of cathode

Specific compositions of anode flows will include diluent, steam, and/or CO2 addition to the fuel stream.  The latter two product species will be used to simulate various locations along an SOFC channel where a certain fraction of the original fuel will be assumed to be converted to H2O and CO2.  The button cells will be tested at different degrees of inlet composition conversion (0%, 25%, 50% and 75%).  The test compositions will be determined by assuming equal fractions of conversion of C to CO2 and 2*H to H2O.  The table below gives examples of molar ratios for C3H8, H2O, and CO2 for different conversion ratios for tests with C3H8 / steam inlets.  Similar tables can be made for dry C3H8, humidified and dry C4H10, H2, and H2+CO fuel feeds.

Table 1 – C3H8-based fuel feed compositions.  Varying H2O and CO2 concentrations are used to simulate the impact of different degrees of fuel conversion at different fuel channel locations.

| Steam to Carbon Ratio | C3H8 Conversion | Anode Flow Molar Composition (relative to inlet moles of C3H8 flow at 0% conversion) |
| --- | --- | --- |
|  |  | C3H8 | H2O | CO2 |
| 1.5 | 0% | 1.00 | 4.50 | 0.00 |
| 1.5 | 25% | 0.75 | 5.50 | 0.75 |
| 1.5 | 50% | 0.50 | 6.50 | 1.50 |
| 1.5 | 75% | 0.25 | 7.50 | 1.50 |
| 2.0 | 0% | 1.00 | 6.00 | 0.00 |
| 2.0 | 25% | 0.75 | 7.00 | 0.75 |
| 2.0 | 50% | 0.50 | 8.00 | 1.50 |
| 2.0 | 75% | 0.25 | 9.00 | 1.50 |

Temperature – Cell temperature will typically range from 700 to 850°C, and possibly 900°C (depending on cell stability) in 50 °C increments.

Electrochemical Characterization – The electrochemical testing will rely on full cell voltammetry (linear-sweep) with fuel cell voltages remaining between open circuit voltages and approximately 700-800 mV overpotential.  Along with that, impedance spectroscopy should be performed at all temperatures and flow conditions at overpotentials of 0.0, V 0.1 V, and 0.3 V.

Exhaust composition measurements – UMD will employ their magnetic sector mass spectrometer to test for exhaust compositions with any carbon-containing fuel streams.  These tests will be used to assess hydrocarbon pyrolysis as well as C to H oxidation ratios for the various C-containing fuel streams.

Schedule for Testing – The following is a proposed start to the testing schedule.  The anode flow compositions for different fuel and conversions will be determined based on the scheme discussed above in the anode flow composition.  This table is not finalized and will be adjusted as the testing program progressesI.  However, it does serve as a guide and current objectives for the program.

Table 2 – Proposed testing schedule envisaged by UMD for SOFC button cells.

| Test # | Dates | Anode | Anode Flow Compositions | Temps. |
| --- | --- | --- | --- | --- |
|  | Year | Months |  |  |  |
| UMD-1 | ‘07 | 08-10 | 1A | H2 and H2+CO at 0-75% conversion | 700-850°C |
| UMD-2 | ‘07 | 10-11 | 1B | H2 and H2+CO at 0-75% conversion | 700-850 C |
| PI-1 |  |  | 1A or 1B | H2 and H2+CO at 0 & 50% conversion | 700-850°C |
| UMD-3 | ’07-‘08 | 11/07-1/08 | 1A or 1B | C4H10 with S/C ratios of 2.0 and 1.0 at 0-75% conversion | 700, 800, 900°C |
| PI-2 |  |  | 1A or 1B | CH4 with S/C ratios of 2.0 and 1.0 at 0-75% conversion | 800, 900°C |
| PI-3 |  |  | 1A or 1B | C3H8 with S/C ratios of 2.0 and 1.0 at 0-75% conversion | 700, 800, 900°C |
| UMD-4 | ’07-‘08 | 12/07-02/08 | 2A | H2 and H2+CO at 0-75% conversion | 700-850°C |
| UMD-5 | ‘08 | 03/08-05/08 | 2B | H2+CO at 0-75% conversion | 700-850°C |
| UMD-6 | ‘08 | 05/08-07/08 | 2A or 2B | CH4 with S/C ratios of 1.0 and 0.0 at 0-75% conversion | 800, 900°C |
| UMD-7 | ‘08 | 06/08-08/08 | 2A or 2B | C4H10 with S/C ratios of 1.0 and 0.0 at 0-75% conversion | 700, 800, 900°C |
| PI-4 |  |  | 2A or 2B | CH4 with S/C ratios of 1.0 and 0.0 at 0-75% conversion | 800, 900°C |
| PI-5 |  |  | 2A or 2B | C3H8 with S/C ratios of 1.0 and 0.0 at 0-75% conversion | 700-850°C |

Appendix B

Justification and Background

This work, combined with the development of detailed microstructure models and higher-level system models, will provide the basis for pursuing a combined experimental and multi-scale modeling effort that will explore the possibility of implementing new high-temperature solid oxide fuel cells in petroleum extraction. These models will aid in both high-efficiency power production and production of concentrated CO2 streams for enhancing oil recovery while sequestering CO2 emissions.  This collaborative work will allow the Petroleum Institute and UMD to become leaders in promoting SOFC technology to improve the operation of and reduce the environmental impact of oil recovery.

SOFC power plants provide a unique opportunity to provide ultra-high efficiencies (> 64% electrical) while simultaneously separating CO2 emissions from N2 dilution for efficient CO2 sequestration1. While SOFC architectures/membrane electrode assemblies (MEA’s) have been developed for operating with small-molecule fuels (H2, CO, and CH4)2, challenges remain in the development of SOFC assemblies for higher hydrocarbon fuels, although recent progress in SOFC design and materials has indicated the feasibility of such systems3,4 . The UMD team has been evaluating SOFC anodes5 for small hydrocarbon fuels, and recent unpublished work on alternative ceria-based anodes shows promise for stable operation with hydrocarbons.

Approach

Four tasks identified for this project are presented here.

Task 1:  Experimental study of SOFC MEA’s for hydrocarbons

UMD has high-temperature single-cell rigs with electrochemical characterization tools, electronic flow controls, and data acquisition for studying SOFC MEA’s.  This project will expand these capabilities to study porous MEA architectures of ceria-based anodes for stable operation on C3-C5 gases.  Experiments will explore the role of metal doping of the ceria for improved electronic conductivity and activity for fuel breakdown to avoid carbon build-up. The experiments will include V-I measurements as well as impedance spectroscopy to validate models developed in Task 2, as well as post-testing microscopy and surface characterization to evaluate the durability of the SOFC anodes for the different fuels. After being established at UMD, these capabilities will be duplicated at the Petroleum Institute (PI) with the aid of UMD researchers such that faculty at the PI will also participate in this effort while providing PI students a chance to explore SOFC technology.

Task 2: Numerical modeling for design of SOFC architectures Modeling of membrane electrode assemblies will explore optimal design of SOFC’s for hydrocarbon operation and high fuel conversion efficiency to provide optimal CO2 capturing by eliminating downstream combustion of unburned fuel.  This work will build on 1-D and 2-D detailed Matlab/Cantera-based models developed at UMD for SOFC MEA analysis.  New efforts will involve the development and validation of hydrocarbon kinetic models on preferred anode materials identified in Task 1.  The Petroleum Institute will seek to implement some of the multi-physics modeling capabilities/predictions of the UMD codes into commercial codes that provide for simulation of complex geometries.

Task 3: System level analysis of integrated SOFC plants

The economic and engineering viability of an integrated SOFC plant for CO2 sequestration and efficient power production1 will be put within the context of petroleum production with system level modeling tools developed at UMD (in Matlab) and at PI (in selected commercial software).  These tools will be used to explore overall balance of the plant, adequacy of fuel supplies, and power requirements for CO2 capture.

Task 4: Identification of multi-university research team for SOFC’s in the petroleum industry.

The UMD/PI team will spend a portion of his time developing a broader-base team for pushing this project further toward implementation. Potential partners may include the Colorado School of Mines and the Norwegian University of Science and Technology, with whom UMD has established collaborations.

Two-Year Schedule

Year 1:

- Begin experiments for identifying preferred material systems using ceria-based anodes for hydrocarbon SOFC operation.

- Perform post-testing material characterization for evaluation.

- Acquire equipment for assembly rig at the PI.

- Adopt Matlab SOFC models at UMD for hydrocarbon studies.

- Input Matlab models into Fluent simulations at PI.

- Establish system level models at both institutions.

Year 2:

- Perform experiments with preferred material systems for typical off-gas compositions (with varying team loadings).

- Validate models and perform SOFC design for both MEA microstructure and overall all fuel cell size.

Identify preferred system configurations for overall balance of plant.

Key References

1.	Armstrong, T.J. and Rich, J.G., J. Electrochem. Soc.  2006. 153(3): A515-A520.

2.	Janardhanan, V.M. and Deutschmann, O.  J. Power SourcesAnnual Review of Materials Research 2006. 162: 1192-1202.

3.	Bessler, W.G., Warnatz, J., and Goodwin, D.G., Solid State Ionics 2007. 177: 3371-3383.

4.	Decaluwe, S.D., Zhu, H., and Jackson, G.S., 2007 Electrochem. Solid State Lett. 2007 in preparation.

Development of a Probabilistic Model for Degradation Effects of Corrosion-Fatigue-Cracking in Oil and Gas Pipelines UMD Investigator: Prof. Mohammad Modarres GRA-1: Mohamed Chooka GRA-2: Mohamed Nefatni Research Assistant: Mohammad Nuhi PI Investigator(s): Prof. Abdennour Seibi Start Date: October 2006 Report Date: 30 September 2007

1.	Objective

This study involves developing and applying an engineering-based probabilistic model for health management of oil pipelines in process plants. The study involves two interrelated projects. The first project, which is the topic for the PhD student, focuses on model development and demonstration. The second project involves developing a degradation acceleration lab at PI and performing experiments to further validate the proposed models of the first project. Building the experimental set-up depends on the availability of funding from the Petroleum Institute.  GRA-1 (Mr. Mohamed Chookah) is working on the first project and GRA-2 (Mr. Mohamed Nefatni) will work on the second project.  Mr. M. Nuhi was hired as a Faculty Research Assistant to support the mechanistic failure part of the research.

The objective of this study is to propose and validate a probabilistic model based on the underlying degradation phenomena whose parameters are estimated from the observed field data and experimental investigations. Uncertainties about the structure of the model itself and parameters of the model should also be characterized.  The proposed model should be able to capture wider ranges of pipelines rather than only the process ones.  Thus, the proposed model will better represent the reality of the pipeline’s health and can account for material and size variability.  The existing probabilistic models sufficiently address the corrosion and fatigue mechanisms individually, but are inadequate to capture mechanisms that synergistically interact.  Admitting the fact that capturing all degradation mechanisms will be a challenging task, the new model will address two of the most important mechanisms: corrosion/crack growth and corrosion/fatigue/crack growth.

2.	Deliverables

Same as previous quarter.

3.	Summary

  - Professor Wei was approached to act as a consultant for the establishment of the corrosion-fatigue laboratory in the PI.  He has also been invited to serve as a PhD committee member for Mr. Chookah.  Dr. Wei is Paul B. Reinhold Professor of Mechanics and served as Chairman of the Department of Mechanical Engineering and Mechanics from 1990 to 1996. He received his B.S.E., M.S.E. and Ph.D. degrees in Mechanical Engineering from Princeton University in 1953, 1954 and 1960, respectively.  He served as Instructor in Mechanical Engineering at Princeton University from 1954 to 1956. From 1959 to 1966, Dr. Wei was affiliated with the Applied Research Laboratory of the United States Steel Corporation, where he studied the mechanics and metallurgical aspects of fracture and subcritical crack growth in ultrahigh strength steels. He also provided consultation on fracture testing and failure analysis. He joined the Lehigh University Faculty in 1966, and is also affiliated with its Institute of Fracture and Solid Mechanics and Zettlemoyer Center for Surface Studies. He served as Acting Chairman of the Department of Mechanical Engineering and Mechanics during the 1983-84 academic year, and as Chairman from 1990 to 1996.

His principal research activities involve the development of fundamental understanding of the mechanical, metallurgical and chemical aspects of environmentally assisted crack growth in aluminum, titanium, ferrous and nickel-based alloys, and the application of this understanding to failure analysis and prevention, and life prediction. He has served, and is serving, as Principal Investigator of a number of government and industry sponsored interdisciplinary research programs in this area. He has been active also as consultant on fracture mechanics based materials research and on failure analysis to a number of industrial and governmental organizations. He has published extensively in this area and has received a number of honors and awards for his research, including the Alexander von Humboldt Foundation Award for US Senior Scientists.

  - We are gathering information on the foundation of corrosion and corrosion fatigue.  The references consulted to accomplish this task have been highlighted in the key references section.

Since Wei’s superposition model describing the “mechanistically-based probabilistic model of corrosion fatigue” is one of the most appropriate models in petroleum applications, most of our work was focused on understanding and summarizing different articles related to different types of corrosion. Specific areas incude:

- Physics of failure-based approach and application of probabilistic model to different types of corrosion. [1,2,3,4]

- Particle-induced pitting and its transition to fatigue crack growth. [5,6,7]

- Wei’s papers on “Environmental consideration for fatigue cracking” with different chemical modeling on fatigue crack response. [7]

- Selected prognostic technologies and how we might them to suite our specific degradation problem of physics of failures. [8]

The following is a summary of our adapted models.

Pitting Corrosion Model

To assess the influence of concurrent pitting corrosion, a simplified model for pit growth proposed by Harlow and Wei was used [9].  The model is patterned after that proposed by Kondo [10] and assumes a pit of hemispherical shape growing at constant volumetric rate in accordance with Faraday’s law from an initial radius aο.  The rate of pit growth (with volume V = (2/3)πa3) is given as follows:

But assuming ρ is constant,

From Faraday’s Law,

Hence by substitution,

where,

;

and a is the pit radius at time t; M is the molecular weight of metal; Ip is the pitting current; Ipo is the pitting current coefficient; η is the metal’s valence; ρ is the density of the metal; F = 96,514 C/mole is Faraday’s constant; Ea is the activation energy; R = 8.314 J/mole-K is the universal gas constant; and T is the absolute temperature.

Corrosion Fatigue Crack Growth Model

Electrochemical Model

For the electrochemical reaction contribution, the surface coverage θ is identified with the ratio of the amount of charge transferred during each loading cycle (q) to that required to completely “repassivate” the bared surface (qs), or, more conveniently,

For this purpose, a simplified model for the reaction is used: for example, it is assumed that the underlying electrochemical reaction consists of a single step and is represented by thermally activated, first-order kinetics [1, 11].  The bare surface reaction current and charge densities are represented in simple exponential forms,

where io is the peak current density (initial rate of reaction on the clean (bare) surface), and k is the reaction rate constant in Arrhenius form.  Thus,

where .

Mechanistic Model

For mechanistic understanding of the problem, the following mechanistic model for fatigue crack growth was chosen. It is assumed that both parts of the above superposition equation can be modeled by the power law (Paris-Erdogan relationship) [12] of the form,

where

and Δσ is the far field stress range, and β is a geometric parameter.

The coefficients Cr and Cc reflect material properties, and the exponents nr and nc reflect the functional dependence of crack growth rate on the driving force ΔK.

Incorporating the electrochemical and mechanical relations yields a simple differential equation in that the variables a and N can be separated.  Estimation of parameters nr and nc may require numerical integration [1].

Superposition Model

A superposition model proposed by Wei [13] was adopted.  In the most general form the fatigue crack growth rate is given by [7]:

with a cycle–dependent rate and a time–dependent rate. Within each of these rates, the mechanical (deformation) and environmental contributions as being from independent parallel processes are treated.

The corrosion fatigue model becomes

From the solution of this equation, we can estimate the N as follows,

where af and atr are the final and initial crack sizes, respectively.

atr could be calculated iteratively using the criterion set earlier,

which reflects equality between the pitting and cracking rates at the onset of crack growth,

The corrosion-fatigue life NF is the sum of the number of loading cycles over which pitting and fatigue cracking dominates at a given stress level [7] and is given by

  - We also found appropriate generic data (from the related papers) to build and run the computer routine Matlab for corrosion fatigue according to Wei’s superposition model.  The following flowchart details the steps in locating the required variables:

Table 1.  Deterministic parameters for X70 steel used in life estimation [1]

Universal gas constant R = 8.314 J/mol-K

Activation energy Ea = 35 KJ/mol

Fatigue exponent nr = 2

Corrosion fatigue exponent nc = 2

Frequency ν = 0.1 and 10 Hz

Applied stress range Δσ = 100, 200, 300, 400, and 500 Mpa

Temperature T = 273, 293, and 313 K

Final crack size af = 25 mm Initial crack size ao = 0 mm

Shape Factor β = 1.24

Faraday’s constant F = 96,514 C/mole

Molecular weight M = 55 g/mole

Valence η = 3

Density ρ = 7.87 g/cm3

Table 2.  Random variable distribution (Weibull) for X70 steel used in life estimation [1]

Random Variable α (shape factor) β(scale factor) γ

Cr 12 4.0 × 10-11(m/cyc)(MPa√m)-2 0

Cc 8 2.0 × 10-10(m/cyc)(MPa√m)-2 0

κο 10 3.0 × 105 (s-1) 0

Ipo Exponential Distribution

The above curve was fitted exponentially using data of pitting corrosion of carbon steel given in the literature. [14]

  - We developed simple empirical parametric models estimated from curve fitting of data obtained from the computer simulation, as shown below.

Following are the proposed empirical models for the fitted data:

αNβ       for     0 ≤ a ≤ at

a =

γeδN       for    at ≤ a ≤ af

where at is the transition crack size.

  - Recently the PI approved $103K for procuring the corrosion-fatigue equipment for the proposed fatigue-corrosion lab at PI.

  - A space for the corrosion-fatigue lab has been designated in the new “Takreer Technology Center” building (within PI’s new campus) scheduled to be completed at end of 2008.

4.	Difficulties Encountered/Overcome

1.  The development of the empirical model was quite challenging mathematically and delayed progress of the project.  Most of the issues are now resolved, and our simulation tool works without any problem. Fitting curves to the simulation data required extensive trials of different models to find an appropriate fit.

- Collection of useful field data proved to be very difficult for the following reasons:

  - The busy environment of the refinery was a great communication obstacle.

  - The collected data were in many pieces and required a substantial effort to gather.

  - The confidentiality of the data was not compromised in preventing smooth data collection.

  - A lack of online monitoring devices made it impossible to obtain crack growth trends.

5.	Deliverables for the Next Quarter

- Application of the collected field data to validate the proposed corrosion-fatigue empirical model.

- Estimation of the distribution of the parameters of the proposed parametric models.

- Application of Markov Chain Monte Carlo (MCMC) Bayesian analysis to update the estimated model parameters of the parametric model.

- Uncertainty analysis to characterize limitation of data.

- Involvement the new student, Mr. Nefatni, for laboratory development (teach him our approach, and theory of corrosion and corrosion fatigue);

- Acquisition of the lab equipment for PI.

- Mr. Nefatni, who is set to move over to the PI starting January 2008 to look after the establishment of the lab as well as the related activities of the research.

Appendix

Justification and Background

Oil pipelines are susceptible to degradation over the span of their service life. Corrosion is one of the most common degradation mechanisms, but other critical mechanisms such as fatigue and creep cannot be overlooked.  The rate of degradation is influenced by factors such as pipeline materials, process conditions, geometry, and location.  Based on these factors, a best estimate of the pipeline’s service life (reliability) is calculated.  This estimate serves as a target that guides maintenance and replacement practices. After a long period of service, however, this estimate requires reevaluation due to new evidence observed from monitoring the conditions of the pipeline.

A number of deterministic models have been proposed to estimate reliability of pipelines.  Among these models is the ASME B31G code [15], which is the most widely accepted method for the assessment of corroded pipelines [16].  However, these models are highly conservative and lack the ability to estimate the true life and health of the pipeline. It is necessary, therefore, to develop a best-estimate assessment of the life of these pipelines and integrate the uncertainties surrounding this estimate.  In addition to the limitations embedded in these deterministic models are the problems with inspection techniques and tools that may be inadequate and susceptible to errors and imprecision.  The proposed probabilistic models would be capable of addressing the limitations of these models (by accounting for model uncertainties), inspection data (characterizing limited and uncertain evidences) and subjective proactive maintenance (involving decision making process under uncertainty).

Approach

The researchers will attempt to identify a focal point in one of ADNOC’s operating companies, such as TAKREER, which will champion this project and provide data pertinent to the core activities of this research study.  The study consists of two interrelated projects that will run over a period of two years and a half.  The first phase of Project 1 will focus on the development of a PhD thesis proposal, which encompasses the latest technological development and ongoing research activities and outlines the subject of the research project.  The second phase will concentrate on the development of a probabilistic model for piping in process plants followed by model validation through collected experimental and field data.  The second project, which will run a year later, will focus on the design, construction and commissioning of the corrosion-fatigue test cell.  The test rig will be designed and built by the research team at the University of Maryland (UMD) with the assistance of Dr. Abdennour Seibi from the Petroleum Institute (PI).  The third phase of this study will deal with model application to ADNOC process facilities in order to predict their remaining service life.

The test rig, which will be built at PI, will be used by Mr. Nefatni to conduct an experimental study reflecting field conditions for model validation developed in project 1.  The equipment needed would include corrosion test cells, autoclaves, multiphase flow loops, and testing machines for slow strain rate and crack growth testing. This activity also requires a complete line of monitoring equipment for evaluation of corrosion, scaling, and chemical treatment for field and laboratory.  This test rig, once built, will be a useful tool for teaching, research, and possibly training field engineers from operating companies.  See “Two-Year Schedule” for a summary of the major tasks and the corresponding timeline.

Two-Year Schedule

Project 1:

- PhD thesis proposal, which will include a literature search (9/1/2006 - 6/30/2007)

- Data collection from ADNOC process plants (1/1/2007 - 8/30/2007)

- Prof. Modarres visit to PI to review progress and plan for accelerated lab development (3/2007).

- Dr. Seibi visit to UMD to advise PhD student in his thesis work and assist in designing the accelerated Testing Facility (11 – 21 May/2007).

- Empirical/Engineering-Based Model Development (9/1/2006 – 6/30/2007)

  - Streamlining of the model to pipeline/pressure vessel application.

  - Collection of appropriate data (data availability is at the discretion of ADNOC operating companies).

  - Actual model development.

- Probabilistic estimation of model parameters (9/1/2007 – 12/31/2007)

- Application example (11/1/2007 – 2/15/2008)

- Dr. Seibi visit to UMD for thesis proposal defense and thesis defense (dates to be announced).

Project 2:

- Design, construction, and commissioning of Accelerated Degradation Lab at PI.  UMD research team will design the test facility with the assistance of Dr. A. Seibi from PI (6/1/2007 - 12/31/2007).

- Test planning (1/1/2008 – 1/31/2008).  Dr. Seibi will visit UMD for two weeks during this period to jointly develop the test plan with UMD researchers.

- Experimental test for model testing/validation (1/1/2008 - 8/31/2008)

- Examples of model applications (9/1/2008 – 12/31/2008)

- Conference and archival paper development (Dates of delivery depend on availability of results).

Key References

1. Harlow, D. G., and Wei, R. P. (1993).  A Mechanistically Based Approach to Probability Modeling for Corrosion Fatigue Crack Growth.  Engineering Fracture Mechanics, 45, 1, 79-88.

2. Wei, R. P., and Harlow, D. G. (2005).  Mechanistically Based Probability Modeling, Life Prediction and Reliability Assessment.  Modeling Simulation Material Science Engineering, 13, R33-R51.

3. Harlow, D. G., and Wei, R. P. (2001).  Probability Modeling and Statistical Analysis of Damage in the Lower Wing Skins of Two Retired B-707 Aircraft.  Fatigue Fracture Engineering Material Structure, 24, 523-535.

4. Wei, R. P., Masser, D., Liu, H., and Harlow, D. G. (1994).  Probabilistic Considerations of Creep Crack Growth.  Material Science and Engineering, A189, 69-76.

5. Wei, R. P. (2001).  A Model for Particle Induced Pit Growth in Aluminum Alloys.  Scripta Materialia, 44, 2647-2652.

6. Dolley, E. J., Lee, B., and Wei, R. P. (2000).  The Effect of Pitting Corrosion on Fatigue Life.  Fatigue Fracture Engineering Material Structure, 23, 555-560.

7. Wei, R. P. (2002).  Environmental Considerations for Fatigue Cracking.  Fatigue & Fracture of Engineering Materials & Structures, 25, 8/9, 845-854.

8. Trethewey, K. R., and Chamberlain, J. (1995).  Corrosion for Science and Engineering.  Longman, England.

9. Harlow, D. G., and Wei, R. P. (1994).  Probability Approach for Prediction of Corrosion and Corrosion Fatigue Life.  AIAA Journal, 32, 10, 2073-2079.

10. Kondo, Y. (1989).  Prediction of Fatigue Crack Initiation Life Based on Pit Growth.  Corrosion, 45, 7-11.

11. Atkins, P. W. (1994).  Physical Chemistry.  W. H. Freeman and Company, NY.

12. Dowling, N. E. (1993).  Mechanical Behavior of Materials.  Prentice Hall, NJ.

13. Wei, R. P., and Gao, M. (1983).  Reconsideration of the Superposition Model for Environmentally Assited Fatigue Crack Growth.  Scripta Metallurgica, 17, 959-962.

14. State Structures Research Laboratory, and State Materials Office – Corrosion Research Laboratory (2002).  Galvanic Testing of Stressed Strands Inside Carbon Steel Pipe – Final Report.  Florida Department of Transportation.

15. ASME-B31G (1991).  Manual for Determining the Remaining Strength of Corroded Pipelines: A Supplement to ASME B31G Code For Pressure Piping.  New York: American Society of Mechanical Engineers.

16. Lee, O. S., Kim, D. H. and Choi, S. S. (2006).  Reliability of Buried Pipeline Using A Theory Of Probability Of Failure. Solid State Phenomena, 110, 221-230.

Waste Heat Utilization in the Petroleum Industry UMD Investigators: Professor Reinhard Radermacher, Dr. Yunho Hwang GRA’s: Paul Kalinowski, Cara Martin PI Investigator(s): Saleh Al Hashimi, Peter Rodgers Start Date: December 1, 2006 Report Date: September 8, 2007

# 1.	Objective/Abstract

The main objective of this project is to minimize overall energy consumption of gas or oil processing plants by utilizing waste heat. One of the possibilities would be the design of a waste heat powered absorption refrigeration unit (ARU), which could be used in a chemical processing plant instead of conventional vapor-compression refrigeration systems. Figure 1 shows the schematics of the propane refrigeration system at the NGL recovery plant and the potential integration of the ARU into the process.

Figure 1: Schematic of: (a) the propane refrigeration system at the LNG recovery plant and (b) potential integration of the ARU into the process

# 2.	Deliverables

Model thermal systems that serve as waste heat sources and/or users

- Modeling of propane chillers

- Modeling of the gas turbine at different ambient and part load conditions.

- Modeling of a double-effect ammonia water absorption refrigeration unit (ARU).

3.	Summary

The propane chillers, the gas turbine, and a single-stage ammonia-water absorption refrigeration unit (ARU) were modeled to analyze the potential application of a waste heat powered ARU instead of conventional propane refrigeration. The engineering equation solver (EES) software was used for modeling.

  - Propane Chiller Models

The propane chillers were modeled to determine their cooling capacity. Figure 2 shows components of a vapor-compression refrigeration system and the presentation of the cycle in the T-s diagram.

Figure 2: Components of a vapor-compression refrigeration system and T-s diagram of the cycle

The following assumptions were made for the chiller models:

- No pressure drops through the evaporator, condenser, and connecting piping

- Negligible kinetic and potential energy

- Constant refrigerant flow rate

- Saturated vapor at the compressor inlet

- Saturated liquid at the condenser exit

- Compressor power input 1 MW

- Isentropic compressor efficiency 60%

- Heat rejection temperature at the condenser exit 50°C

- Saturated vapor temperature at the evaporator outlet 18°C and -42°C for 1st and 2nd chiller, respectively

Figure 3 shows p-h diagrams and state points for the 1st and 2nd chiller, respectively. All major results for the chillers are summarized in Table .

| 1st Chiller | 2nd Chiller |
| --- | --- |

Figure 3: p-h diagram of the 1st chiller and 2nd chiller

# Table 1: Major results of the propane chiller models

|  | 1st Chiller | 2nd Chiller |
| --- | --- | --- |
| Propane flow rate | 16.89 kg/s | 4.47 kg/s |
| Cooling capacity | 4,329 kW @ 18 °C | 842 kW @ -42 °C |
| COP | 4.329 | 0.8474 |

  - Gas Turbine Model

A 9 MWe single-shaft gas turbine was modeled to determine the amount of waste heat and the exhaust mass flow rate under different ambient and part load conditions, which affect the performance of the gas turbine. The irreversible (real) air-standard analysis was used to study the gas turbine. Two assumptions were made: (1) the working fluid is air, which behaves as an ideal gas, and (2) the temperature rises that would be brought about by combustion is accomplished by heat transfer from an external source. Figure 4 illustrates the schematic of a single-shaft gas turbine open cycle for power generation and Brayton cycle in T-s diagram, which was used to analyze the gas turbine process.

Figure 4: Schematic of a single-shaft gas turbine open cycle for power generation and Brayton cycle in T-s diagram

Since the gas turbine drives a generator, ISO conditions were applied for the gas turbine model. These are:

- 1.013 bar, sea level, ambient pressure

- 15°C ambient temperature

- 60% relative humidity

Quasi-dimensionless and referred parameters are used to describe the performance of the compressor and turbine while considering the effects of changing ambient conditions. The quasi-dimensionless parameters are applied in the gas turbine component design with fixed linear scale where the working fluid is dry air. The referred parameters are directly proportional to the quasi-dimensionless parameters and thus are interchangeable in use.  The distinction is the substitution of  and  for gas turbine or component inlet pressure and temperature, where:

(1)

(2)

The referred parameters enable to calculate the performance parameters of gas turbines or components at the standard ambient conditions. They take the values of the basic parameters, which would be at ISO conditions. Table  presents the main quasi-dimensionless and referred parameters.

Table 2: Gas turbine parameters

| Performance Parameter | Quasi-dimensionless Parameter | Referred Parameter |
| --- | --- | --- |
| Temperature a station () |  |  |
| Pressure at station () |  |  |
| Mass flow () |  |  |
| Net (shaft) power () |  |  |

The off-design performance of a gas turbine can be predicted by using off-design characteristics plotted in terms of referred parameters (Figure 5). With the varying power level the referred parameters vary while forming a unique running line or families of running lines that are independent of ambient conditions. The off-design performance may be defined via diagrams showing the interrelationship of the referred parameters. The actual performance parameter values can be easily calculated for a given operating condition if the absolute values of inlet pressure and temperature are known.

| Mass flow rate | Compressor discharge pressure | Turbine exhaust temperature |
| --- | --- | --- |

Figure 5: Referred performance diagrams for corrected mass flow rate, compressor discharge pressure and exhaust temperature

Table 3 shows technical specifications of the gas turbine used in modeling. The gas turbine generates approximately 9 MWe at the ISO conditions. The pressure ratio, exhaust flow rate, and exhaust mass flow rate were applied as initial conditions in the model.

Table 3: Gas turbine technical specifications

| Pressure ratio | 10 |
| --- | --- |
| Turbine inlet temperature | 975°C |
| Exhaust temperature | 508°C |
| Exhaust mass flow rate | 45 kg/s |
| Electrical power output (ISO) | 8,963 kW |
| Heat rate | 13,250 kJ/kWh |
| Shaft speed | 8,000 rpm |

Since it can be assumed that the mass flow rate through the compressor is the same as that through the turbine, the exhaust flow rate was considered to be the same as the air mass flow rate in the model. The isentropic efficiencies of the compressor and turbine were assumed 83% and 84.5%, respectively. The gear box and generator efficiency were assumed 99% and 97%, respectively. All pressure and mechanical losses were neglected. The referred parameters from Table  and the referred performance diagrams of single-shaft gas turbine from Figure 5 were used for off-design calculations. The effect of ambient pressure on the power output was neglected . Waste heat was calculated by assuming that the exhaust could be cool down to 100 °C.

Figure 6 illustrates the T-s diagram of the gas turbine at ISO conditions and Table  summarizes the major results of the gas turbine model. Compressor discharge pressure and turbine inlet temperature are 10.13 bar and 976.5°C, respectively. The thermal efficiency of the Brayton cycle is approximately 29%, which is typical for gas turbines of this size. The electrical power output and heat rate of the modeled gas turbine slightly differ from those in manufacturer’s specification. Approximately 71% of added energy is “wasted” by rejecting it to surroundings. A part of this heat (~23 MW) could be unitized to power an absorption refrigeration unit by cooling it down to 100 °C.

Figure 6: T-s diagram of the gas turbine at ISO conditions

Table 4: Major results of the gas turbine model at ISO conditions

| Thermal efficiency | 28.96 % |
| --- | --- |
| Electrical power output | 9,038 kW |
| Heat rate | 12,431 kJ/kWh |
| Mass flow rate | 45 kg/s |
| Added heat | 32,399 kW |
| Rejected heat | 23,087 kW |
| Waste heat | 19,236 kW |

  - Ammonia-Water Refrigeration Cycle Model

Two single-effect and one double-effect ammonia-water absorption refrigeration cycles were modeled to analyze their potential in the NGL recovery process. The waste heat from the gas turbine powers the absorption cycles.

The following assumptions were made for the models:

- No pressure changes except through the expansion valves and pumps

- Heat losses to the surroundings are negligible

- Saturated liquid at the exit of the condensers, absorbers, and generators

- Saturated vapor at the rectifier outlet with 0.99 ammonia concentration

- Isentropic pump efficiency 85%

- Heat exchanger efficiency 80%

- Heat rejection temperature at the condenser and absorber outlet 50 °C

- Saturated vapor temperature at the evaporator outlet 18°C and -42°C for 1st and 2nd chiller, respectively

The gas turbine was assumed to operate at 35°C ambient temperature and 80% load. The calculated exhaust mass flow rate and temperature are 42.86 kg/s 453.4°C, respectively. The external routings with ammonia-water properties were used for absorption refrigeration modeling.

Single-Effect Ammonia-Water Absorption Refrigeration Unit

Figure 7 shows the ammonia-water absorption refrigeration unit (ARU) consisted of two single-effect absorption systems. One of the systems could be a replacement for the 1st chiller while the other system could replace the 2nd chiller. The exhaust of the gas turbine powers the generator of the 2nd chiller, and then the cooler exhaust powers the generator of the 1st chiller. Solution and refrigerant heat exchanger are employed to increase the performance of the systems. The rectifier is also used to increase the performance of the system by increasing the ammonia concentration in the ammonia-water vapor mixture. The cooling loads of the evaporators were taken from the propane chiller models. The generator (maximum) temperature was set to be 190°C.

# Figure 7: Single-effect ammonia-water absorption refrigeration cycle

Table 5 summarizes the major results of the ARU consisted of two single-effect absorption refrigeration systems. Higher cooling load of the 1st chiller requires higher refrigerant flow rate, consequentially higher generator heat transfer rate, and higher exhaust temperature glide than those of the 2nd chiller. The ammonia concentration, vapor quality, and heat rejection temperature in the condenser determine the maximum pressure, which is approximately 20 bar in both systems. The low COP of 2nd absorption system is due to high heat transfer rate in the generator and high pump work. The COP of the absorption refrigeration unit is at around 41%.

Table 5: Major results for single-effect ARU

|  | 1st Chiller | 2nd Chiller |
| --- | --- | --- |
| Heat transfer rate in generator | 7,606 kW | 4,841 kW |
| Exhaust temperature @ generator inlet | 347.6 °C | 453.4 °C |
| Exhaust temperature @ generator exit | 176.5 °C | 347.6 °C |
| Pump work | 21.28 kW | 37.16 kW |
| Maximum pressure | 2,015 kPa | 2,015 kPa |
| COP of the system | 0.5676 | 0.1726 |
| COP of the unit | 0.4135 |

Double-Effect Ammonia-Water Absorption Refrigeration Unit

Table 5 illustrates a double-effect ammonia-water absorption refrigeration unit. The intermediate pressure evaporator (IPE) and low pressure evaporator (LPE) could replace the 1st chiller and the 2nd chiller, respectively. The cooling loads of the evaporators and evaporator temperatures directly affect the generator temperature.  Therefore, the cooling loads were adjusted in the ARU to keep the generator temperature lower than 200°C and consequently to reduce the additional water evaporation. The cooling load of the 2nd chiller was taken from the propane chiller model. However, the cooling load for LPE was reduced from 842 kW to 650 kW due to too high generator temperature (above 200 °C).

Figure 8: Double-effect ammonia-water refrigeration unit

The major results for the double-effect ammonia-water absorption refrigeration system are summarized in Table . The ARU requires over 10 MW exhaust heat to power the generator (GEN) while the generator temperature reaches 190°C. The exhaust gas from the gas turbine would be cooled to 195.4°C. Nearly 87% of the total pump work is consumed by the solution pump, which delivers the solution from the IPA to the GEN. The maximum pressure, determined by the ammonia concentration, vapor quality, and heat rejection temperature in the condenser, is increased over 20 bar. The COP of the unit is approximately 47%.

Table 6: Major results for double-effect ARU

| Heat transfer rate in generator | 10,470 kW |
| --- | --- |
| Exhaust temperature @ generator inlet | 453.4 °C |
| Exhaust temperature @ generator exit | 221.5 °C |
| Total pump work | 28.19 kW |
| Maximum pressure | 2,015 kPa |
| COP of the unit | 0.4743 |

  - Conclusions

The propane chillers were modeled to determine their cooling capacity for further absorption refrigeration analysis. Since the models are based on assumptions, their closer investigation would be required to achieve more accurate results. Nevertheless, the computer models would be a good tool for such an investigation.

The 9 MWe gas turbine was modeled at different ambient temperatures and operating loads. The off-design procedure shows good matches with the manufacturer’s specifications at ISO conditions and allows calculation of exhaust mass flow rates and exhaust temperatures, which are important for the design of an absorption refrigeration unit. However, it does not consider the changes in the isentropic compressor and turbine efficiencies. Besides, the results should be verified with test result of the gas turbine.

Two ammonia-water absorption refrigeration units (ARU) were modeled. The ARUs could replace the propane chillers. The single-effect ARU consisted of two single-effect absorption refrigeration systems could provide the required cooling for the NGL recovery process. The double-effect ARU has two evaporators (one for each propane chiller) which are powered only by one generator. Because of fewer components, the double-effect ARU would require less space and thus enhance the integration of the unit into the NGL recovery process. However, it can provide the required cooling load only to the 2nd chiller. The vapor-compression refrigeration system would be still necessary to provide the required cooling load to the 1st chiller. Due to the assumptions for the propane chillers, no specific conclusions can be made at this stage of analysis. The computer model for the double-effect ARU can be used as baseline if the cooling loads of the propane chiller are less than assumed.

# 4.	Difficulties Encountered/Overcome

Developing an advanced ammonia-water ARU using as a few components as possible to reduce manufacturing cost and to increase the overall efficiency of the entire system might be challenging.

# 5.	Deliverables for the Next Quarter

The following activities are to be conducted in the next quarter:

- Assessment of waste heat sources

- Assessment of utility needs

- Design CHP systems with specific focus on use in the plant to be selected

- Development of the software to optimize waste heat utilization.

# Appendix

Justification and Background

The petroleum industry is a big energy consumer itself. Using waste heat skillfully meets some of the demands placed on utilities, leading to significant energy savings.

CEEE at the University of Maryland has extensive experience in the design and implementation of integrated CHP (combined cooling heating and power) projects. The faculties at PI have experience in the design and operation of petroleum processing plants. Jointly, the team is excellently suited to address the challenge posed by this project.

Approach

- Assess waste heat (WH) sources (PI)

- Assess WH conversion processes (UMD)

- Assess utility requirements (PI)

- Match WH sources/processes and utility requirements (PI, UMD)

- Develop/implement of software for system analysis (PI, UMD)

- Rank and propose implementation of 1 or 2 preferred systems (PI, UMD)

- Define additional R&D as needed (PI, UMD)

Two-Year Schedule

June 1, 2007	Report assessing WH sources and utility requirements

June 1, 2007	WH conversion options report

Oct. 1, 2007	Useful version of software

Apr. 31, 2008	Ranking of systems and selection

Nov. 31, 2008	Report recommended steps forward

Key References

- Alefeld, G., Radermacher, R., 1994, “Heat conversion systems,” CRC Press, Boca Raton.

- Al-Hamdan, Q.Z., Ebaid, M.S.Y., 2006, “Modeling and simulation of a gas turbine engine for power generation,” ASME Journal of Engineering for Gas Turbines and Power, Vol. 128, pp. 302-311.

- ASHRAE, 2002, “ASHRAE Refrigeration Handbook,” American Society of Heating, Refrigeration and Air-Conditioning Engineers, Atlanta, GA, USA.

- ASHRAE, 2005, “ASHRAE Fundamentals Handbook,” American Society of Heating, Refrigeration and Air-Conditioning Engineers, Atlanta, GA, USA.

- Brant, B., Brueske, S., Erickson, D.C., Papar, R., 1998, “New waste-heat refrigeration unit cuts flaring, reduces pollution,” Oil & Gas Journal, May 18, pp.61-64.

- Brooks, F.,J., 2000 “GE gas turbine performance characteristics,” GE Power Systems Schenectady, NY, GER-3567H.

- Cohen, H., Rogers, G.F.C., Saravanamuttoo, H.I.H., 1996, “Gas turbine theory,” 4th edition, Longman Scientific & Technical, Singapore.

- Erickson, D.C., 2000 “LPG recovery from reformer treat gas,” US Patent 6,158,241.

- Erickson, D.C., Anand, G., Papar, R.A., Tang, J., 1998, “Refinery waste heat powered absorption refrigeration – cycle specification and design,” Proceeding of the ASME Advanced Energy System Division, AES-Vol. 38, pp.391-402.

- Erickson, D.C., Kelly, F., 1998, “LPG recovery from refinery by waste heat powered absorption refrigeration,” IECEC-98-079, 33rd Intersociety Engineering Conference on Energy Conversion, Colorado Springs, CO.

- Giampaolo, T., 2003, “The gas turbine handbook: principles and practices,” 2nd edition, The Fairmont Press, Lilburn, GA.

- Herold, K.E.; Radermacher, R., Klein, S, 1996, “Absorption chillers and heat pumps,” CRC Press, Boca Raton.

- Kim, T.S., Hwang, S.H., 2006, “Part load performance analysis of recuperated gas turbine considering engine configuration and operation strategy,” Energy, Vol. 31, pp., 260-277.

- Klein, S.A., 2005, “Engineering Equation Solver” F-Chart Software.

- Kurz, R., 2005, “Gas turbine performance,” 44th Turbomachinery Symposium, pp.131-146.

- Kurzke, J., 2003, “Model based gas turbine parameter corrections,” GT2003-38234, Proceedings of 2003 ASME TURBO EXPO: Power for Land, Sea, & Air, Atlanta, GA, USA.

- Li, Y.G., Pilidis, P., Newby, M.A., 2006, “An adaptation approach for gas turbine design-point performance simulation,” Journal of Engineering for Gas Turbines and Power, Vol. 128, pp. 789-795.

- Orlando, J.,A., 1996, “Cogeneration design guide,” American Society of Heating, Refrigeration and Air-Conditioning Engineers, Atlanta, GA.

- Pande, M., 1996, “Tools for fractionator design in ammonia-water absorption machines,” Master Thesis, University of Maryland, College Park.

- Walsh, P.P., Fletcher, P., 1998, “Gas turbine performance,” Blackwell Science, Oxford

Undergraduate Design and Best Educational Practices UMD Investigators: Prof. Linda Schmidt GRA’s: To be assigned PI Investigator(s): Dr. Kubo Start Date: November 2006 Report Date: 30 September 2007

1.	Objective

Dr. Schmidt will partner with PI design faculty to (1) assess existing PI curriculum to profile the design content and (2) compare the design content level to that of a top-ranked, ABET-accredited, US institution; and, (3) prepare design modules and recommend their selected placement within existing PI courses.

The ultimate goal in Year 2 is to create a semester-long project design course that challenges student teams in the same manner as the Mechanical Engineering Senior Capstone Design Experience. Two different design projects will be selected for up to four PI design teams. The PI Design Course Instructor will manage the PI teams, with Dr. Schmidt serving as a consultant and a final project referee. The projects will be the design of mechanical devices to meet a current petroleum engineering challenge.  That is, PI students will have actual customers to consult with at their site. The UM teams will use existing web-based asynchronous communication tools to interact with the same customers served by students at PI.  The PI students (who will be further ahead in the projects) will assist UM students in this communication.

2.	Deliverables

Dr. Kubo and Dr. Schmidt will schedule Schmidt to visit PI for capstone design planning for Year Two.

3.	Summary

Dr. Schmidt was unable to conduct project activities because of an intense course of physical therapy (May through July) arising from her car accident on March 11th and a separate rib injury sustained on UM’s campus on July 6th that required a two-week absence followed by reduced schedule of activities.

4.	Difficulties Encountered/Overcome

- Dr. Schmidt was unable to conduct project activities because of an intense course of physical therapy (May through July) arising from her car accident on March 11th and a separate rib injury sustained on UM’s campus on July 6th that required a two-week absence followed by reduced schedule of activities.

- Dr. Schmidt has resumed research and travel activities as of September 2007.

5.	Deliverables for the Next Quarter

The following items are ideas for PI/UMD to decide on:

- Schedule a site visit for Dr. Schmidt to coordinate with activities of student design projects in 2008.

- Identify short courses that Dr. Schmidt can provide to PI (possible scheduling in Jan. 2008)

  - Potential Design Short Courses Topics Include: TRIZ, Systematic Design, QFD’s House of Quality for student projects, Axiomatic Design, Overall Product Development Process

  - Additional Topics on Student Project Courses: Identifying Project Sponsors, Creating Teams, Using Peer Evaluation and Assessment Tools, Writing Project Specifications and matching assessment rubrics, BESTEAMS training

- Potentially identify an ADNOC sponsored design project that a UM student team could work on during Spring 2008. This will enable planning for a collaborative design project.

Appendix

Justification and Background

Approach

- Compare the following design aspects: a. Design experience prior to capstone b. Design methods to which students are exposed prior to capstone course. c. Level of original design content expected in projects. d. Constraints of typical projects. e. Degree of student team interaction with mentors f. Evaluation criteria and practices in place.

- Determine the design course content that can be used to enrich each institution’s courses. This will include material from the best prior projects and course examples.

- Identify challenges in collaboration on teams due to differences in institutions and partners.

- Plan phased faculty interaction in design course at partner institution to prepare for collaborative team-work.

- Identify projects that could be done at both institutions.

- Plan collaborative projects that would be done by teams of students spanning both institutions.

Two-Year Schedule

Year 1:

- Exchange senior design course syllabi and sample projects for comparison purposes.

- Planned site visit by Prof. Schmidt in March 2007 in conjunction with Participation in METSMaC 2007: “Active Teaching, Active Learning,” March 17-19, 2007.-- CANCELLED

- Visit of Dr. Kubo to UM including:

  - Attending UM Capstone design course lecture, student interim report presentation, and tour of DesignME Lab facilities for teamwork and prototyping.

  - Discussion with Dr. Schmidt on course syllabus and review of sample reports

Year 2:

- In Year 2, the team will make broader comparisons of curriculum design content to expectations of ADNOC employers (as this the group that will be employing most PI grads) and produce refined design modules.

- Implement a team collaboration capstone design project.

Key References

# Text boxes

Encoder

Optical sensor

Laser sensor

Drill String

Housing

Springs

Actuator

B

A

e

Y

O2

O

Y

(b)

X

X

Section II

Z

O

Y

X

Figure 11. Case 4 results with 100 m/s O2 jet into 0.66 m/s 50%H2S50%CO2 entering at 1000K.

mb

Section II

Section I

O2

O

Z

Z

Insulator

Needle

(Discharge Electrode)

+

Metal Tube

(Collector Electrode)

Air Flow

Ultrasonic Droplets Generator

HV Power Supply

Air-Water Mixture

-

DAS

Aerodynamic Particle Sizer

Temperature / Humidity Sensors

HV Power Supply

DP

Test Section

Temperature / Humidity Sensors

Flow Meter

Aerosol Generator

Temperature / Humidity Sensors

Flow Meter

Air Filter

Fan

DP

Figure 10.  Case 3 results with 100 m/s O2 jet into co-flow of  50%H2S and 50%CO2 at 0.2 m/s, both entering at ambient temperature.

Figure 9.  Case 2 results with 100 m/s O2 jet into co-flow of H2S at 0.1 m/s of, both entering at ambient temperature.

Figure 8.  Case 1 results with 85 m/s H2S jet into co-flow of air at 0.1 m/s, both entering at ambient temperature.

Figure 6.  2-D Cross-section of the Cylinder (distances are given in mm)

Figure 5. The Cylindrical Combustor Considered

Figure 4.  Sulfur recovery as a function of O2 content

H2S conversion

Temperature

Figure 3.  Sulfur recovery as a function of inlet temperature

H2S Conversion

Temperature

Figure 2.  Sulfur recovery as a function of temperature

Figure 1. H2S conversion (or sulfur recovery) as a function of H2S [%] at the inlet

H2S conversion

Temperature

(a)

The original image is taken from a video file of the two phase flow.

1

2

The image is converted from a color image to a gray scale image.

3

The image is filtered.

4

To further distinguish the bubble from the liquid, the image is adjusted

0.4 mm